## Slide 1: Data and Computer Communications
Tenth Edition
by William Stallings
Notes: “Data and Computer Communications”, 10/e, by William Stallings, Chapter 21 “Internetwork Operation”

## Slide 2: Internetwork Operation
Chapter 21
Notes: This chapter begins with a discussion of multicasting. Next we look at a new
approach to managing Internet traffic known as software-defined network
(SDN), and the related protocol OpenFlow. The chapter then introduces the
topic of Mobile IP. Refer to Figure 21.8 to see the position within the TCP/IP
suite of the protocols discussed in this chapter.

## Slide 3: Overview
Multicasting
Introduction to Software Defined Networks
Mobile IP
Dynamic Host Configuration Protocol (DHCP)

## Slide 4: Multicasting
The act of sending a packet from a source to the members of a multicast group
  Multicast addresses
  Addresses that refer to a group of hosts on one or more networks
Has a number of practical applications
Multimedia “broadcast”
Teleconferencing
Database
Distributed computing
Real time workgroups
Notes: Typically, an IP address refers to an individual host on a particular network. IP also accommodates addresses that refer to a group of hosts on one or more networks. Such addresses are referred to as multicast addresses, and the act of sending a packet from a source to the members of a multicast group is referred to as multicasting.
Multicasting has a number of practical applications. For example,
Multimedia: A number of users "tune in" to a video or audio transmission from a multimedia source station.
Teleconferencing: A group of workstations form a multicast group such that a transmission from any member is received by all other group members.
Database: All copies of a replicated file or database are updated at the same time.
Distributed computation: Intermediate results are sent to all participants.
Real-time workgroup: Files, graphics, and messages are exchanged among active group members in real time.

## Slide 5: LAN Multicast
LAN multicast is easy
  Send to IEEE 802 multicast MAC address
  Those in multicast group will accept it
  Only single copy of packet is needed
A transmission from any one station is received by all other stations on LAN
Notes: Multicasting done within the scope of a single LAN segment is straightforward. IEEE 802 and other LAN protocols include provision for MAC-level multicast addresses. A packet with a multicast address is transmitted on a LAN segment. Those stations that are members of the corresponding multicast group recognize the multicast address and accept the packet. In this case, only a single copy of the packet is ever transmitted. This technique works because of the broadcast nature of a LAN: a transmission from any one station is received by all other stations on the LAN.

## Slide 6
Notes: In an internet environment, multicasting is a far more difficult undertaking. To see this, consider the configuration of Figure 21.1; a number of LANs are interconnected by routers. Routers connect to each other either over high-speed links or across a wide area network (network N4). A cost is associated with each link or network in each direction, indicated by the value shown leaving the router for that link or network. Suppose that the multicast server on network N1 is transmitting packets to a multicast address that represents the workstations indicated on networks N3, N5, N6.

## Slide 7: Multicasting Strategies
Broadcast packet to each network
If server does not know members of group
Requires 13 packets
Could send multiple unicast packets
To each network with members in multicast group
Requires 11 packets
True multicast
Spanning tree
Replicated by routers at branch points
Requires 8 packets
Notes: Suppose that the server does not know the location of the members of the multicast group. Then one way to assure that the packet is received by all members of the group is to broadcast a copy of each packet to each network in the configuration, over the least-cost route for each network. For example, one packet would be addressed to N3 and would traverse N1, link L3, and N3. Router B is responsible for translating the IP-level multicast address to a MAC-level multicast address before transmitting the MAC frame onto N3
Now suppose the source system knows the location of each member of the multicast group. That is, the source has a table that maps a multicast address into a list of networks that contain members of that multicast group. In that case, the source need only send packets to those networks that contain members of the group. We could refer to this as the multiple unicast strategy. Stallings DCC9e Table 19.1 shows that in this case, 11 packets are required.
Both the broadcast and multiple unicast strategies are inefficient because they generate unnecessary copies of the source packet. In a true multicast strategy, the following method is used:
1. The least-cost path from the source to each network that includes members of the multicast group is determined. This results in a spanning tree of the configuration. Note that this is not a full spanning tree of the configuration. Rather, it is a spanning tree that includes only those networks containing group members.
2. The source transmits a single packet along the spanning tree.
3. The packet is replicated by routers only at branch points of the spanning tree.

## Slide 8: Table 21.1 Traffic Generated by Various Multicasting Strategies
Notes: Table 21.1 summarizes the number of packets generated on the various links and networks in order to transmit one packet to a multicast group by this method. In this table, the source is the multicast server on network N1 in Figure 21.1; the multicast address includes the group members on N3, N5, and N6
Now suppose the source system knows the location of each member of the
multicast group. That is, the source has a table that maps a multicast address into
a list of networks that contain members of that multicast group. In that case, the
source need only send packets to those networks that contain members of the
group. We could refer to this as the multiple unicast strategy. Table 21.1 shows that
in this case; 11 packets are required.

## Slide 9
Notes: Figure 21.2a shows the spanning tree for transmissions from the source to the multicast group, and Figure 21.2b shows this method in action. The source transmits a single packet over N1 to router D. D makes two copies of the packet, to transmit over links L3 and L4. B receives the packet from L3 and transmits it on N3, where it is read by members of the multicast group on the network. Meanwhile, C receives the packet sent on L4. It must now deliver that packet to both E and F. If network N4 were a broadcast network (e.g., an IEEE 802 LAN), then C would only need to transmit one instance of the packet for both routers to read. If N4 is a packet-switching WAN, then C must make two copies of the packet and address one to E and one to F. Each of these routers, in turn, retransmits the received packet on N5 and N6, respectively. As Table 21.1 shows, the multicast technique requires only eight copies of the packet.

## Slide 10: Requirements for Multicasting
Router may have to forward more than one copy of packet
Need convention to identify multicast addresses (IPv4, Class D, IPv6)
Nodes translate between IP multicast addresses and list of networks containing group members
Router must translate between IP multicast address and network multicast address
Cont…
Notes: In ordinary unicast transmission over an internet, in which each datagram has a unique destination network, the task of each router is to forward the datagram along the shortest path from that router to the destination network. With multicast transmission, the router may be required to forward two or more copies of an incoming datagram. In our example, routers D and C both must forward two copies of a single incoming datagram.
Thus, we might expect that the overall functionality of multicast routing is more complex than unicast routing. The following is a list of required functions:
1. A convention is needed for identifying a multicast address. In IPv4, Class D addresses are reserved for this purpose. These are 32-bit addresses with 1110 as their high-order 4 bits, followed by a 28-bit group identifier. In IPv6, a 128-bit multicast address consists of an 8-bit prefix of all ones, a 4-bit flags field, a 4-bit scope field, and a 112-bit group identifier. The flags field, currently, only indicates whether this address is permanently assigned or not. The scope field indicates the scope of applicability of the address, ranging from a single network to global.
2. Each node (router or source node participating in the routing algorithm) must translate between an IP multicast address and a list of networks that contain members of this group. This information allows the node to construct a shortest-path spanning tree to all of the networks containing group members.
3. A router must translate between an IP multicast address and a network multicast address in order to deliver a multicast IP datagram on the destination network. For example, in IEEE 802 networks, a MAC-level address is 48 bits long; if the highest-order bit is 1, then it is a multicast address. Thus, for multicast delivery, a router attached to an IEEE 802 network must translate a 32-bit IPv4 or a 128-bit IPv6 multicast address into a 48-bit IEEE 802 MAC-level multicast address.

## Slide 11: Requirements for Multicasting
Mechanism required for hosts to join and leave multicast group
Routers must exchange information
  Which networks include members of given group
  Sufficient information to work out shortest path to each network
Routing algorithm to calculate shortest path
Routers must determine routing paths based on source and destination addresses
Notes: 4. Although some multicast addresses may be assigned permanently, the more usual case is that multicast addresses are generated dynamically and that individual hosts may join and leave multicast groups dynamically. Thus, a mechanism is needed by which an individual host informs routers attached to the same network as itself of its inclusion in and exclusion from a multicast group. IGMP, described subsequently, provides this mechanism.
5. Routers must exchange two sorts of information. First, routers need to know which networks include members of a given multicast group. Second, routers need sufficient information to calculate the shortest path to each network containing group members. These requirements imply the need for a multicast routing protocol. A discussion of such protocols is beyond the scope of this book.
6. A routing algorithm is needed to calculate shortest paths to all group members.
7. Each router must determine multicast routing paths on the basis of both source and destination addresses.

## Slide 12
Notes: The last point is a subtle consequence of the use of multicast addresses. To illustrate the point, consider again Figure 21.1. If the multicast server transmits a unicast packet addressed to a host on network N5, the packet is forwarded by router D to C, which then forwards the packet to E. Similarly, a packet addressed to a host on network N3 is forwarded by D to B. But now suppose that the server transmits a packet with a multicast address that includes hosts on N3, N5, and N6. As we have discussed, D makes two copies of the packet and sends one to B and one to C. What will C do when it receives a packet with such a multicast address? C knows that this packet is intended for networks N3, N5, and N6. A simple-minded approach would be for C to calculate the shortest path to each of these three networks. This produces the shortest-path spanning tree shown in Figure 21.3. As a result, C sends two copies of the packet out over N4, one intended for N5 and one intended for N6. But it also sends a copy of the packet to B for delivery on N3. Thus B will receive two copies of the packet, one from D and one from C. This is clearly not what was intended by the host on N1 when it launched the packet.
To avoid unnecessary duplication of packets, each router must route packets on the basis of both source and multicast destination. When C receives a packet intended for the multicast group from a source on N1, it must calculate the spanning tree with N1 as the root (shown in Figure 21.2a) and route on the basis of that spanning tree.

## Slide 13: Internet Group Management Protocol (IGMP)
Defined in RFC 3376
Used to exchange multicast group information between hosts and routers on a LAN
Hosts send messages to routers to subscribe and unsubscribe from multicast group
Routers check which multicast groups are of interest to which hosts
IGMP currently at version 3
Notes: IGMP, defined in RFC 3376, is used by hosts and routers to exchange multicast group membership information over a LAN. IGMP takes advantage of the broadcast nature of a LAN to provide an efficient technique for the exchange of information among multiple hosts and routers. In general, IGMP supports two principal operations:
1. Hosts send messages to routers to subscribe to and unsubscribe from a multicast group defined by a given multicast address.
2. Routers periodically check which multicast groups are of interest to which hosts.

## Slide 14: Evolving Network Requirements
Increasingly widespread use of server virtualization
  Makes it possible to partition a single machine into multiple independent servers, conserving hardware resources
  Also makes it possible to quickly migrate a server from one machine to another for load balancing or for dynamic switchover in the case of machine failure
  Has become a central element in dealing with “big data” applications and in implementing cloud computing infrastructures
Increasing use by employees of mobile devices, such as smartphones, tablets, and notebooks to access enterprise resources
  Network managers must be able to respond to rapidly changing resource, QoS, and security requirements
Notes: One key driving factor is the increasingly widespread use of server virtualization.
In essence, server virtualization masks server resources, including the number
and identity of individual physical servers, processors, and operating systems, from
server users. This makes it possible to partition a single machine into multiple independent
servers, conserving hardware resources. It also makes it possible to quickly
migrate a server from one machine to another for load balancing or for dynamic
switchover in the case of machine failure. Server virtualization has become a central
element in dealing with “big data” applications and in implementing cloud computing
infrastructures. But it creates problems with traditional network architectures
(e.g., see [LAYL10]). One problem is configuring virtual LANs. Network managers
need to make sure the VLAN used by the virtual machine (VM) is assigned to the
same switch port as the physical server running the VM. But with the VM being
movable, it is necessary to reconfigure the VLAN every time that a virtual server
is moved. In general terms, to match the flexibility of server virtualization, the
network manager needs to be able to dynamically add, drop, and change network
resources and profiles. This is difficult to do with conventional network switches, in
which the control logic for each switch is collocated with the switching logic.
Another effect of server virtualization is that traffic flows differ substantially
from the traditional client/server model. Typically, there is a considerable amount
of traffic among virtual servers, for such purposes as maintaining consistent images
of database and invoking security functions such as access control. These serverto-
server flows change in location and intensity over time, demanding a flexible
approach to managing network resources.
Another factor leading to the need for rapid response in allocating network
resources is the increasing use by employees of mobile devices, such as smartphones,
tablets, and notebooks to access enterprise resources. Network managers must be
able to respond to rapidly changing resource, QoS, and security requirements.
Existing network infrastructures can respond to changing requirements for
the management of traffic flows, providing differentiated QoS levels and security
levels for individual flows, but the process can be very time consuming if the enterprise
network is large and/or involves network devices from multiple vendors. The
network manager must configure each vendor’s equipment separately, and adjust
performance and security parameters on a per-session, per-application basis. In a
large enterprise, every time a new virtual machine is brought up, it can take hours
or even days for network managers to do the necessary reconfiguration [ONF12].
This state of affairs has been compared to the mainframe era of computing
[DELL12]. In the era of the mainframe, applications, the operating system, and the
hardware were vertically integrated and provided by a single vendor. All of these
ingredients were proprietary and closed, leading to slow innovation. Today, most
computer platforms use the x86 instruction set and a variety of operating systems
(Windows, Linux, Mac OS) run on top of the hardware. The OS provides APIs
that enable outside providers to develop applications, leading to rapid innovation
and deployment. In a similar fashion, commercial networking devices have proprietary
features and specialized control planes and hardware, all vertically integrated
on the switch. As will be seen, the SDN architecture and the OpenFlow standard
provide an open architecture in which control functionality is separated from the
network device, and placed in accessible control servers. This enables the underlying
infrastructure to be abstracted for applications and network services, which can
treat the network as a logical entity.

## Slide 15
Notes: Figure 21.6 illustrates the logical structure of an SDN. A central controller performs
all complex functionality, including routing, naming, policy declaration, and security
checks. This constitutes the SDN control plane , and consists of one or more
SDN servers.
The SDN controller defines the data flows that occur in the SDN data plane .
Each flow through the network must first get permission from the controller, which
verifies that the communication is permissible by the network policy. If the controller
allows a flow, it computes a route for the flow to take, and adds an entry for
that flow in each of the switches along the path. With all complex function subsumed
by the controller, switches simply manage flow tables whose entries can only
be populated by the controller. Communication between the controller and the
switches uses a standardized protocol and API. Most commonly this interface is the
OpenFlow specification, discussed in the next section.
The SDN architecture is remarkably flexible; it can operate with different
types of switches and at different protocol layers. SDN controllers and switches can
be implemented for Ethernet switches (layer 2), Internet routers (layer 3), transport
(layer 4) switching, or application-layer switching and routing. SDN relies on the
common functions found on networking devices, which essentially involves forwarding
packets based on some form of flow definition. In an SDN architecture, a
switch performs the following functions:
1. The switch encapsulates and forwards a flow’s first packet to an SDN controller,
enabling the controller to decide whether the flow should be added to the
switch’s flow table.
2. The switch forwards incoming packets out the appropriate port based on the
flow table. The flow table may include priority information dictated by the
controller.
3. The switch can drop packets on a particular flow, temporarily or permanently,
as dictated by the controller. Packet dropping can be used for security purposes,
curbing denial-of-service attacks, or traffic management requirements.
In simple terms, the SDN controller manages the forwarding state of the
switches in the SDN. This management is done through a vendor-neutral API that
allows the controller to address a wide variety of operator requirements without
changing any of the lower-level aspects of the network, including topology.
With the decoupling of the control and data planes, SDN enables applications
to deal with a single abstracted network device, without concern for the
details of how the device operates. Network applications see a single API to
the controller. Thus it is possible to quickly create and deploy new applications
to orchestrate network traffic flow to meet specific enterprise requirements for
performance or security.

## Slide 16
Notes: In a large enterprise network, the deployment of a single controller to manage all
network devices would prove unwieldy or undesirable. A more likely scenario is
that the operator of a large enterprise or carrier network divides the whole network
into a number of nonoverlapping SDN domains (Figure 21.7).

## Slide 17: SDN Domains
Reasons for using SDN domains:
Scalability
The number of devices an SDN controller can feasibly manage is limited
A reasonably large network may need to deploy multiple SDN controllers
Privacy
A carrier may choose to implement different privacy policies in different SDN domains
Incremental deployment
A carrier’s network may consist of portion of legacy and nonlegacy infrastructure
Dividing the network into multiple, individually manageable SDN domains allows for flexible incremental deployment
Notes: Reasons for using
SDN domains include the following:
• Scalability: The number of devices an SDN controller can feasibly manage is
limited. Thus, a reasonably large network may need to deploy multiple SDN
controllers.
• Privacy: A carrier may choose to implement different privacy policies in different
SDN domains. For example, an SDN domain may be dedicated to a
set of customers who implement their own highly customized privacy policies,
requiring that some networking information in this domain (e.g., network
topology) should not be disclosed to an external entity.
• Incremental deployment: A carrier’s network may consist of portions of
legacy and nonlegacy infrastructure. Dividing the network into multiple,
individually manageable SDN domains allows for flexible incremental
deployment.

## Slide 18: SDNi
Protocol being developed for interfacing SDN domain controllers
Functionality includes:
  Coordinate flow setup originated by application, continuing information such as path requirement, QoS, and service level agreements across multiple SDN domains
  Exchange reachability information to facilitate inter-SDN routing
Message types tentatively include:
Reachability update
Flow setup/tear-down/update request
Capability update
Notes: The existence of multiple domains creates a requirement for individual controllers
to communicate with each other via a standardized protocol, to exchange
routing information. IETF is currently working on developing a protocol, called
SDNi, for interfacing SDN domain controllers. SDNi functionality includes the
following:
• Coordinate flow setup originated by applications, containing information such
as path requirement, QoS, and service level agreements across multiple SDN
domains.
• Exchange reachability information to facilitate inter-SDN routing. This will
allow a single flow to traverse multiple SDNs and have each controller select
the most appropriate path when multiple such paths are available.
The message types for SDNi tentatively include the following:
• Reachability update
• Flow setup/tear-down/update request (including application capability
requirement such as QoS, data rate, latency, etc.)
• Capability update (including network-related capabilities, such as data rate
and QoS, and system and software capabilities available inside the domain)

## Slide 19: OpenFlow
Defined in the OpenFlow Switch Specification published by the Open Networking Foundation (ONF)
  ONF is a consortium of software providers, content delivery networks, and networking equipment vendors whose purpose is to promote software-defined networking
Is both a protocol between SND controllers and network devices and a specification of the logical structure of the network switch functionality
To turn the concept of SND into practical implementation two requirements must be met:
1
2
There must be a common logical architecture in all switches, routers, and other network devices to be managed by an SDN controller
A standard, secure protocol is needed between the SDN controller and the network device
Notes: To turn the concept of SND into practical implementation, two requirements must be
met. First, there must be a common logical architecture in all switches, routers, and
other network devices to be managed by an SDN controller. This logical architecture
may be implemented in different ways on different vendor equipment and in different
types of network devices, so long as the SDN controller sees a uniform logical switch
functionality. Second, a standard, secure protocol is needed between the SDN controller
and the network device. Both of these requirements are addressed by OpenFlow,
which is both a protocol between SDN controllers and network devices and a specification
of the logical structure of the network switch functionality. OpenFlow is
defined in the OpenFlow Switch Specification , published by the Open Networking
Foundation (ONF). ONF is a consortium of software providers, content delivery networks,
and networking equipment vendors whose purpose is to promote softwaredefined
networking.
This section is based on the current OpenFlow specification, Version 1.3.0,
June 25, 2012. The original specification, 1.0, was developed at Stanford University
and was widely implemented. OpenFlow 1.2 was the first release from ONF after
inheriting the project from Stanford. OpenFlow 1.3 significantly expands the functionality
of the specification. Version 1.3 is likely to become the stable base upon
which future commercial implementations for OpenFlow will be built. ONF intends
for this version to be a stable target for chip and software vendors, so little if any
change is planned for the foreseeable future [KERN12].

## Slide 20
Notes: Figure 21.8 illustrates the basic structure of the OpenFlow environment. An
SDN controller communicates with OpenFlow-compatible switches using the
OpenFlow protocol running over the Secure Sockets Layer (SSL). Each switch
connects to other OpenFlow switches and, possibly, to end-user devices that are
the sources and destinations of packet flows. Within each switch, a series of tables,
typically implemented in hardware or firmware, are used to manage the flows of
packets through the switch.

## Slide 21: Mobile IP
Enables computers to maintain Internet connectivity while moving from one Internet attachment point to another
Particularly suited for wireless connections
Mobile implies:
  A user is connected to one or more applications across the Internet
  The user’s point of attachment changes dynamically
  All connections are automatically maintained despite the change
Notes: In response to the increasing popularity of palm-top and other mobile computers, Mobile IP was developed to enable computers to maintain Internet connectivity while moving from one Internet attachment point to another. Although Mobile IP can work with wired connections, in which a computer is unplugged from one physical attachment point and plugged into another, it is particularly suited to wireless connections.
The term mobile in this context implies that a user is connected to one or more applications across the Internet, that the user's point of attachment changes dynamically, and that all connections are automatically maintained despite the change. This is in contrast to a user, such as a business traveler, with a portable computer of some sort who arrives at a destination and uses the computer's notebook to dial into an ISP (Internet service provider). In this latter case, the user's Internet connection is terminated each time the user moves and a new connection is initiated when the user dials back in. Each time an Internet connection is established, software in the point of attachment (typically an ISP) is used to obtain a new, temporarily assigned IP address. This temporary IP address is used by the user's correspondent for each application-level connection (e.g., FTP, Web connection). A better term for this kind of use is nomadic.

## Slide 22: Operation of Mobile IP
Routers use the IP address in an IP datagram to perform routing
Network portion is used to move a datagram to the network the target computer is attached to
Final router uses the host portion to deliver to the destination
With a mobile host the IP address may change while one or more TCP connections are active
Notes: As was described earlier in this chapter, routers make use of the IP address in an IP datagram to perform routing. In particular, the network portion of an IP address (Figure 14.6) is used by routers to move a datagram from the source computer to the network to which the target computer is attached. Then the final router on the path, which is attached to the same network as the target computer, uses the host portion of the IP address to deliver the IP datagram to the destination. Further, this IP address is known to the next higher layer in the protocol architecture (Figure 14.1). In particular, most applications over the Internet are supported by TCP connections. When a TCP connection is set up, the TCP entity on each side of the connection knows the IP address of the correspondent host. When a TCP segment is handed down to the IP layer for delivery, TCP provides the IP address, and IP creates an IP datagram with that IP address in the IP header and sends the datagram out for routing and delivery. However, with a mobile host, the IP address may change while one or more TCP connections are active.

## Slide 23
Notes: Figure 21.10 shows in general terms how Mobile IP deals with the problem of dynamic IP addresses. A mobile node is assigned to a particular network, known as its home network. Its IP address on that network, known as its home address, is static. When the mobile node moves its attachment point to another network, that network is considered a foreign network for this host. Once the mobile node is reattached, it makes its presence known by registering with a network node, typically a router, on the foreign network known as a foreign agent. The mobile node then communicates with a similar agent on the user's home network, known as a home agent, giving the home agent the care-of address of the mobile node; the care-of address identifies the foreign agent's location. Typically, one or more routers on a network will implement the roles of both home and foreign agents.

## Slide 24: Basic Capabilities of Mobile IP
Mobile IP includes three basic capabilities
Discovery
A discovery procedure is used to identify prospective home and foreign agents
Registration
Authenticated registration procedure is used
Tunneling
Forwards IP datagram from a home address to a care-of address
Notes: To support the operations illustrated in Figure 21.10, Mobile IP includes three basic capabilities:
Discovery: A mobile node uses a discovery procedure to identify prospective home agents and foreign agents.
Registration: A mobile node uses an authenticated registration procedure to inform its home agent of its care-of address.
Tunneling: Tunneling is used to forward IP datagrams from a home address to a care-of address.

## Slide 25
Notes: Figure 21.11 indicates the underlying protocol support for the Mobile IP capability. The registration protocol communicates between an application on the mobile node and an application in the home agent and hence uses a transport-level protocol. Because registration is a simple request-response transaction, the overhead of the connection-oriented TCP is not required, and therefore UDP is used as the transport protocol. Discovery makes use of the existing ICMP (Internet Control Message Protocol) by adding the appropriate extensions to the ICMP header. Finally, tunneling is performed at the IP level.

## Slide 26: Table 21.3 Mobile IP Terminology (RFC 3334)
(Table can be found on page 693
in textbook)
Notes: Mobile IP is specified in a number of RFCs. The basic defining document is RFC 3344. Table 21.3 lists some useful terminology from RFC 3344.

## Slide 27
Notes: Once a mobile node is registered with a home agent, the home agent must be able to intercept IP datagrams sent to the mobile node's home address so that these datagrams can be forwarded via tunneling. The standard does not mandate a specific technique for this purpose but references ARP (Address Resolution Protocol) as a possible mechanism. The home agent needs to inform other nodes on the same network (the home network) that IP datagrams with a destination address of the mobile node in question should be delivered (at the link level) to this agent. In effect, the home agent steals the identity of the mobile node in order to capture packets destined for that node that are transmitted across the home network.
For example, suppose that R3 in Figure 21.12 is acting as the home agent for a mobile node that is attached to a foreign network elsewhere on the Internet. That is, there is a host H whose home network is LAN Z that is now attached to some foreign network. If host D has traffic for H, it will generate an IP datagram with H's home address in the IP destination address field. The IP module in D recognizes that this destination address is on LAN Z and so passes the datagram down to the link layer with instructions to deliver it to a particular MAC-level address on Z. Prior to this time, R3 has informed the IP layer at D that datagrams destined for that particular address should be sent to R3. Thus, D inserts the MAC address of R3 in the destination MAC address field of the outgoing MAC frame. Similarly, if an IP datagram with the mobile node's home address arrives at router R2, it recognizes that the destination address is on LAN Z and will attempt to deliver the datagram to a MAC-level address on Z. Again, R2 has previously been informed that the MAC-level address it needs corresponds to R3.
For traffic that is routed across the Internet and arrives at R3 from the Internet, R3 must simply recognize that for this destination address, the datagram is to be captured and forwarded.
To forward an IP datagram to a care-of address, the home agent puts the entire IP datagram into an outer IP datagram. This is a form of encapsulation, just as placing an IP header in front of a TCP segment encapsulates the TCP segment in an IP datagram. Three options for encapsulation are allowed for Mobile IP:
IP-within-IP encapsulation: This is the simplest approach, defined in RFC 2003.
Minimal encapsulation: This approach involves fewer fields, defined in RFC 2004.
Generic routing encapsulation (GRE): This is a generic encapsulation procedure that was developed prior to the development of Mobile IP, defined in RFC 1701.

## Slide 28
Figure 21.13 Mobile IP Encapsulation
Notes: With this approach, the entire IP datagram becomes
the payload in a new IP datagram (Figure 21.13a). The inner, original IP header is
unchanged except to decrement Time to Live (TTL) by 1. The outer header is a
full IP header. Two fields (indicated as unshaded in the figure) are copied from the
inner header: The version number is 4, which is the protocol identifier for IPv4, and
the type of service requested for the outer IP datagram is the same as that requested
for the inner IP datagram.
In the inner IP header, the source address refers to the host that is sending the original
datagram, and the destination address is the home address of the intended recipient.
In the outer IP header, the source and destination addresses refer to the entry and exit
points of the tunnel. Thus, the source address typically is the IP address of the home
agent, and the destination address is the care-of address for the intended destination.

## Slide 29
Figure 21.13 Mobile IP Encapsulation
Notes: Minimal encapsulation results in less overhead and can
be used if the mobile node, home agent, and foreign agent all agree to do so. With
minimal encapsulation, the new header is inserted between the original IP header
and the original IP payload (Figure 21.13b). It includes the following fields:
• Protocol: Copied from the protocol field in the original IP header. This field
identifies the protocol type of the original IP payload and thus identifies the
type of header that begins the original IP payload.
• S: If 0, the original source address is not present, and the length of this header
is 8 octets. If 1, the original source address is present, and the length of this
header is 12 octets.
• Header Checksum: Computed over all the fields of this header.
• Original Destination Address: Copied from the destination address field in
the original IP header.
• Original Source Address: Copied from the source address field in the original
IP header. This field is present only if the S bit is 1. The field is not present if
the encapsulator is the source of the datagram (i.e., the datagram originates at
the home agent).
The following fields in the original IP header are modified to form the new
outer IP header:
• Total Length: Incremented by the size of the minimal forwarding header (8 or 12).
• Protocol: 55; this is the protocol number assigned to minimal IP encapsulation.
• Header Checksum: Computed over all the fields of this header; because some
of the fields have been modified, this value must be recomputed.
• Source Address: The IP address of the encapsulator, typically the home agent.
• Destination Address: The IP address of the exit point of the tunnel. This is the
care-of address and may either be the IP address of the foreign agent or the IP
address of the mobile node (in the case of a co-located care-of address).
The processing for minimal encapsulation is as follows. The encapsulator
(home agent) prepares the encapsulated datagram with the format of Figure 21.13b.

## Slide 30: Dynamic Host Configuration Protocol (DHCP)
Internet protocol that enables dynamic allocation of IP addresses to hosts
Defined in RFC 2131
Was developed to deal with the shortage of IP addresses
Enables a local network to assign IP addresses from a pool of available IP addresses to hosts currently in use
When a host is not in use, its IP address is returned to the pool managed by a DHCP server
Can also assign permanent IP addresses to some systems, such as servers, so that the address remains the same when the system is rebooted
Notes: The Dynamic Host Configuration Protocol (DHCP) is an Internet protocol, defined
in RFC 2131, that enables dynamic allocation of IP addresses to hosts.
DHCP was developed to deal with the shortage of IP addresses, a shortage
that will remain an issue until the wholesale conversion to the longer IPv6
addresses. DHCP enables a local network, such as in a business enterprise, to assign
IP addresses from a pool of available IP addresses to hosts currently in use. When a
host is not in use, its IP address is returned to the pool managed by a DHCP server.
Even when there is not a shortage of IP addresses, DHCP is useful in
environments with mobile systems, such as laptops and tablets, that travel among
different networks or that are only used sporadically. DHCP also can assign permanent
IP addresses to some systems, such as servers, so that the address remains the
same when the system is rebooted.

## Slide 31
Notes: DHCP operates on a client/server model, with any host acting as a client that
needs an IP address upon booting up, and a DHCP server that provides the request IP
address along with related configuration parameters (Figure 21.14). The configuration
parameters may include the network address of a default router for communication
outside the local network and the address of a local DNS server.

## Slide 32
The following DHCP messages are used for protocol operation:
DHCPDISCOVER
DHCPOFFER
DHCPREQUEST
DHCPACK
DHCPNACK
DHCPDECLINE
DHCPRELEASE
DHCPINFORM
Client broadcast to locate available servers
Server to client in response to DHCPDISCOVER with offer of configuration parameters
Client message to servers either (a) requesting offered parameters from one server and implicitly declining offers from all others, (b) confirming correctness of previously allocated address after, for example, system reboot, or (c) extending the lease on a particular network address
Server to client with configuration parameters, including committed network address
Server to client indicating client’s notion of network address is incorrect (e.g., client has moved to new subnet) or client’s lease has expired
Client to server indicating network address is already in use. DHCP server should then notify sysadmin
Client to server relinquishing network address and canceling remaining lease
Client to server, asking only for local configuration parameters client already has externally configured network address

## Slide 33
Notes: Figure 21.15 illustrates a typical message exchange. The following steps are
involved:
1. The client broadcasts a DHCPDISCOVER message on its local physical network.
The message may include options that suggest values for the network
address and lease duration. Relay agents may pass the message on to DHCP
servers not on the same physical network.
2. Each server may respond with a DHCPOFFER message that includes an
available network address.
3. The client receives one or more DHCPOFFER messages from one or more
servers. The client may choose to wait for multiple responses. The client
chooses one server from which to request configuration parameters, based on
the configuration parameters offered in the DHCPOFFER messages. The client
broadcasts a DHCPREQUEST message that includes the server identifier
option to indicate which server it has selected, and that may include other
options specifying desired configuration values. This DHCPREQUEST message
is broadcast and relayed through DHCP relay agents. The client times
out and retransmits the DHCPDISCOVER message if the client receives no
DHCPOFFER messages.
4. The servers receive the DHCPREQUEST broadcast from the client. Those
servers not selected by the DHCPREQUEST message use the message as
notification that the client has declined that server’s offer. The server selected
in the DHCPREQUEST message commits the binding for the client to
persistent storage and responds with a DHCPACK message containing the
configuration parameters for the requesting client.
5. The client receives the DHCPACK message with configuration parameters.
At this point, the client is configured.
6. The client may choose to relinquish its lease on a network address by sending
a DHCPRELEASE message to the server.

## Slide 34: Summary
Multicasting
  Requirements for multicasting
  IGMP
  PIM
Software defined networks
  Evolving network requirements
  SDN architecture
  SDN domains
Dynamic host configuration protocol
OpenFlow
  Logical switch architecture
  Flow table components
  Flow table pipeline
  OpenFlow protocol
Mobile IP
  Operation of Mobile IP
  Discovery
  Registration
  Tunneling
Notes: Chapter 21 summary.

## Slide 35: Additional Slides

## Slide 36: Operation of IGMP v1 and v2
IGMPv1
  Hosts could join group
  Routers used timer to unsubscribe members
IGMPv2 enabled hosts to unsubscribe
Operational model:
  Receivers have to subscribe to groups
  Sources do not have to subscribe to groups
  Any host can send traffic to any multicast group
Problems:
  Spamming of multicast groups
  Establishment of distribution trees is problematic
  Finding globally unique multicast addresses is difficult
Notes: In IGMPv1, hosts could join a multicast group and routers used a timer to unsubscribe group members. IGMPv2 enabled a host to request to be unsubscribed from a group. The first two versions used essentially the following operational model:
Receivers have to subscribe to multicast groups.
Sources do not have to subscribe to multicast groups.
Any host can send traffic to any multicast group.
This paradigm is very general, but it also has some weaknesses:
1. Spamming of multicast groups is easy. Even if there are application level filters to drop unwanted packets, still these packets consume valuable resources in the network and in the receiver that has to process them.
2. Establishment of the multicast distribution trees is problematic. This is mainly because the location of sources is not known.
3. Finding globally unique multicast addresses is difficult. It is always possible that another multicast group uses the same multicast address.

## Slide 37: IGMP v3
Addresses weaknesses by:
  Allowing hosts to specify list from which they want to receive traffic
  Blocking traffic from other hosts at routers
  Allowing hosts to block packets from sources that send unwanted traffic
Notes: IGMPv3 addresses these weaknesses by
1. Allowing hosts to specify the list of hosts from which they want to receive traffic. Traffic from other hosts is blocked at routers.
2. Allowing hosts to block packets that come from sources that send unwanted traffic.

## Slide 38
Figure 21.4 IGMPv3 Message Formats
Notes: All IGMP messages are transmitted in IP datagrams. The current version defines two message types: Membership Query and Membership Report.
A Membership Query message is sent by a multicast router. There are three subtypes: a general query, used to learn which groups have members on an attached network; a group-specific query, used to learn if a particular group has any members on an attached network; and a group-and-source specific query, used to learn if any attached device desires reception of packets sent to a specified multicast address, from any of a specified list of sources.
Figure 21.4a shows the message format, which consists of the following fields:
Type: Defines this message type.
Max Response Code: Indicates the maximum allowed time before sending a responding report in units of 1/10 second.
Checksum: An error-detecting code, calculated as the 16-bit ones complement addition of all the 16-bit words in the message. For purposes of computation, the Checksum field is itself initialized to a value of zero. This is the same checksum algorithm used in IPv4.
Group Address: Zero for a general query message; a valid IP multicast group address when sending a group-specific query or group-and-source-specific query.
S Flag: When set to one, indicates to any receiving multicast routers that they are to suppress the normal timer updates they perform upon hearing a query.
QRV (querier's robustness variable): If nonzero, the QRV field contains the RV value used by the querier (i.e., the sender of the query). Routers adopt the RV value from the most recently received query as their own RV value, unless that most recently received RV was zero, in which case the receivers use the default value or a statically configured value. The RV dictates how many times a host will retransmit a report to assure that it is not missed by any attached multicast routers.
QQIC (querier's querier interval code): Specifies the QI value used by the querier, which is a timer for sending multiple queries. Multicast routers that are not the current querier adopt the QI value from the most recently received query as their own QI value, unless that most recently received QI was zero, in which case the receiving routers use the default QI value.
Number of Sources: Specifies how many source addresses are present in this query. This value is nonzero only for a group-and-source specific query.
Source Addresses: If the number of sources is N, then there are N 32-bit unicast addresses appended to the message.

## Slide 39
Figure 21.4 IGMPv3 Message Formats
Notes: Figure 21.2.4b shows the message format of an IGMP Membership Report message, which has the following fields:
Type: Defines this message type.
Checksum: An error-detecting code, calculated as the 16-bit ones complement addition of all the 16-bit words in the message.
Number of Group Records: Specifies how many group records are present in this report.
Group Records: If the number of group records is M, then there are M 32-bit unicast group records appended to the message.

## Slide 40
Figure 21.4 IGMPv3 Message Formats
Notes: Figure 21.4c shows the format of the group record in an IGMP Membership Report message. This has the following fields:
Record Type: Defines this record type, as described subsequently.
Aux Data Length: Length of the auxiliary data field, in 32-bit words.
Number of Sources: Specifies how many source addresses are present in this record.
Multicast Address: The IP multicast address to which this record pertains.
Source Addresses: If the number of sources is N, then there are N 32-bit unicast addresses appended to the message.
Auxiliary Data: Additional information pertaining to this record. Currently, no auxiliary data values are defined.

## Slide 41: IGMP Operation - Joining
IGMP host wants to make itself known as group member to other hosts and routers on LAN
IGMPv3 can signal group membership with filtering capabilities with respect to sources
  EXCLUDE mode – all members except those listed
  INCLUDE mode – only from group members listed
To join a group a host sends an IGMP membership report message
Address field is the multicast address of group
Sent in an IP datagram with the same multicast destination address
Current group members receive and learn new member
Routers listen to all IP multicast addresses to hear all reports
Notes: The objective of each host in using IGMP is to make itself known as a member of a group with a given multicast address to other hosts on the LAN and to all routers on the LAN. IGMPv3 introduces the ability for hosts to signal group membership with filtering capabilities with respect to sources. A host can either signal that it wants to receive traffic from all sources sending to a group except for some specific sources (called EXCLUDE mode) or that it wants to receive traffic only from some specific sources sending to the group (called INCLUDE mode). To join a group, a host sends an IGMP membership report message, in which the multicast address field is the multicast address of the group. This message is sent in an IP datagram with the same multicast destination address. In other words, the Multicast Address field of the IGMP message and the Destination Address field of the encapsulating IP header are the same. All hosts that are currently members of this multicast group will receive the message and learn of the new group member. Each router attached to the LAN must listen to all IP multicast addresses in order to hear all reports.

## Slide 42: IGMP Operation Keeping Lists Valid
Routers periodically issue IGMP general query message
In datagram with all-hosts multicast address
Hosts must read such datagrams
Hosts respond with report message
Router doesn’t know every host in a group
Needs to know at least one group member still active
Each host in group sets timer with random delay
Host hearing another report cancels own
If timer expires, host sends report
Only one member of each group reports to router
Notes: To maintain a valid current list of active group addresses, a multicast router periodically issues an IGMP general query message, sent in an IP datagram with an all-hosts multicast address. Each host that still wishes to remain a member of one or more multicast groups must read datagrams with the all-hosts address. When such a host receives the query, it must respond with a report message for each group to which it claims membership.
Note that the multicast router does not need to know the identity of every host in a group. Rather, it needs to know that there is at least one group member still active. Therefore, each host in a group that receives a query sets a timer with a random delay. Any host that hears another host claim membership in the group will cancel its own report. If no other report is heard and the timer expires, a host sends a report. With this scheme, only one member of each group should provide a report to the multicast router.

## Slide 43: IGMP Operation - Leaving
Host leaves group by sending a leave group message to the all-routers static multicast address
  Sends a membership report message with EXCLUDE option and null list of source addresses
Router determines if any group members using group-specific query message remain
Notes: When a host leaves a group, it sends a leave group message to the all-routers static multicast address. This is accomplished by sending a membership report message with the INCLUDE option and a null list of source addresses; that is, no sources are to be included, effectively leaving the group. When a router receives such a message for a group that has group members on the reception interface, it needs to determine if there are any remaining group members. For this purpose, the router uses the group-specific query message.

## Slide 44: Group Membership with IPv6
IGMP defined for IPv4
  Uses 32-bit addresses
IPv6 internets need functionality
IGMP functions included in Internet Control Message Protocol v6 (ICMPv6)
  ICMPv6 has functionality of ICMPv4 & IGMP
ICMPv6 includes group-membership query and group-membership report message
Notes: IGMP was defined for operation with IPv4 and makes use of 32-bit addresses. IPv6 internets need this same functionality. Rather than to define a separate version of IGMP for IPv6, its functions have been incorporated into the new version of the Internet Control Message Protocol (ICMPv6). ICMPv6 includes all of the functionality of ICMPv4 and IGMP. For multicast support, ICMPv6 includes both a group-membership query and a group-membership report message, which are used in the same fashion as in IGMP.

## Slide 45: Protocol Independent Multicast (PIM)
A separate routing protocol, independent of any existing unicast routing protocol
Designed to extract needed routing information from any unicast routing protocol
Recognizes that a different approach may be needed to multicast routing depending on the concentration of multicast group members
Defines two modes of operation:
Dense-mode
Sparse-mode
Notes: The use of a multicast extension to a unicast routing protocol is appropriate
within a single autonomous system, where it is typical that a single unicast routing
protocol is implemented. The assumption of a high concentration of multicast
group members is often valid within a single autonomous system and for applications
such as groupware. However, a different approach is needed to deal with
a large internet of multiple autonomous systems and with applications such as
multimedia, in which the size of a given multicast group may be relatively small
and widely scattered.
To provide a more general solution to multicast routing, a new protocol has
been developed, known as Protocol Independent Multicast (PIM). As the name
suggests, PIM is a separate routing protocol, independent of any existing unicast
routing protocol. PIM is designed to extract needed routing information from any
unicast routing protocol and may work across multiple ASs with a number of different
unicast routing protocols.
The design of PIM recognizes that a different approach may be
needed to multicast routing depending on the concentration of multicast group members.
When there are many multicast members and when many subnetworks within a
configuration have members of a given multicast group, then the frequent exchange
of group membership information is justified. In such an environment, it is desirable
to build shared spanning trees, such as we saw in Figure 21.2b, so that packet
duplication occurs as infrequently as possible. However, when there are a few widely
scattered members to a given multicast group, different considerations apply. First,
flooding of multicast group information to all routers is inefficient, because most
routers will not be along the path of any members of a given multicast group. Second,
there will be relatively little opportunity for using shared spanning trees, and therefore
the focus should be on providing multiple shortest-path unicast routes.
To accommodate these differing requirements, PIM defines two modes of
operation: dense-mode and sparse-mode operation.

## Slide 46: PIM
Dense-Mode PIM
Appropriate for intra-AS multicast routing
May be viewed as a potential alternative to a multicast version of OSPF known as MOSPF
Sparse-Mode PIM
Suited for inter-AS multicast routing
RFC 2362
Defined as a group in which:
  The number of networks/domains with group members present is significantly smaller than the number of networks/domains in the internet
  The internet spanned by the group is not sufficiently resource rich to ignore the overhead of current multicast routing schemes
Notes: The dense-mode protocol is appropriate for intra-AS multicast routing
and may be viewed as a potential alternative to a multicast version of OSPF known
as MOSPF.

## Slide 47
Notes: The approach taken for sparse-mode PIM has the following elements:
1. For a multicast group, one router is designated as a rendezvous point (RP).
2. A group destination router sends a Join message toward the RP, requesting
that its members be added to the group. The requesting router uses a unicast
shortest-path route to transmit the message toward the RP. The reverse of this
path becomes part of the distribution tree from this RP to listeners in this group.
3. Any node that wishes to send to a multicast group sends packets toward the
RP, using a shortest-path unicast route.
A transmission by this scheme, as defined so far, can be summarized as follows:
A single packet follows the shortest unicast path from the sending node to the RP.
From the RP, transmission occurs down the tree to the listeners, with each packet
replicated at each split in the tree. This scheme minimizes the exchange of routing
information, because routing information goes only from each router that supports
group members to the RP. The scheme also provides reasonable efficiency. In particular,
from the RP to the multicast receivers, a shared tree is used, minimizing the
number of packets duplicated.
In a widely dispersed group, any RP will, of necessity, be remote from many of
the group members, and paths for many group members will be much longer than the
least-cost path. To help alleviate these drawbacks while maintaining the benefits of the
PIM scheme, PIM allows a destination router to replace the group-shared tree with a
shortest-path tree to any source. Once a destination router receives a multicast packet,
it may elect to send a Join message back to the source router of that packet along a unicast
shortest path. From then on, multicast packets between that source and all group
members that are neighbors to that destination router follow the unicast shortest path.
Figure 21.5 illustrates the sequence of events. Once the destination begins
to receive packets from the source by the shortest-path router, it sends a Prune
message to the RP. This Prune message instructs the RP not to send any multicast
packets from that source to this destination. The destination will continue to
receive multicast packets from other sources via the RP-based tree, unless and until
it prunes those sources. Any source router must continue to send multicast packets
to the RP router for delivery to other multicast members.
The selection of an RP for a given multicast group is a dynamic process. The
initiator of a multicast group selects a primary RP and a small ordered set of alternative
RPs. In general, RP placement is not a critical issue because the RP-based
tree will not be used for most receivers after shortest-path routers are followed.

## Slide 48: Tables
    A flow is a sequence of packets traversing a network that share a set of header field values
The OpenFlow specification defines three types of tables in the logical switch architecture:
Flow table
Matches incoming packets to a particular flow and specifies what functions are to be performed on the packets
There may be multiple flow tables that operate in a pipeline fashion
Group table
May trigger a variety of actions that affect one or more flows
Meter table
Can trigger a variety of performance-related actions on a flow
Notes: The OpenFlow specification defines three types of tables in the logical switch
architecture. A flow table matches incoming packets to a particular flow and specifies
what functions are to be performed on the packets. There may be multiple
flow tables that operate in a pipeline fashion, as explained subsequently. A flow
table may direct a flow to a group table , which may trigger a variety of actions that
affect one or more flows. A meter table can trigger a variety of performance-related
actions on a flow.
Before proceeding it is helpful to define what is meant by the term flow .
Curiously, this term is not defined in the OpenFlow specification, nor is there an
attempt to define it in virtually all of the literature on OpenFlow. In general terms,
a flow is a sequence of packets traversing a network that share a set of header field
values. For example, a flow could consist of all packets with the same source and
destination IP addresses or all packets with the same virtual LAN (VLAN) identifier.
We provide a more specific definition subsequently.

## Slide 49: Flow Table Components
Basic building block of the logical switch architecture
May include a table-miss flow entry, which wildcards all match fields (regardless of value) and has the lowest priority (0)
Contains entries consisting of six components:
Match fields
Priority
Counters
Instructions
Time-outs
Cookie
Notes: The basic building block of the logical switch architecture is the flow table. Each
packet that enters a switch passes through one of more flow tables. Each flow table
contains entries consisting of six components:
• Match fields: Used to select packets that match the values in the fields.
• Priority: Relative priority of table entries.
• Counters: Updated for matching packets. The OpenFlow specification defines
a variety of timers. Examples include the number of received bytes and packets
per port, per flow table, and per flow table entry; number of dropped packets;
and duration of a flow.
• Instructions: Actions to be taken if a match occurs.
• Time-outs: Maximum amount of idle time before a flow is expired by the switch
• Cookie: opaque data value chosen by the controller. May be used by the controller
to filter flow statistics, flow modification and flow deletion; not used
when processing packets.
A flow table may include a table-miss flow entry, which wildcards all match fields
(every field is a match regardless of value) and has the lowest priority (priority 0)

## Slide 50: Match Fields Component
Consists of the following required fields which must be supported by any OpenFlow-compliant switch:
  Ingress port
  Ethernet source and destination addresses
  IPv4 or IPv6 protocol number
  IPv4 or IPv6 source address, and destination address
  TCP source and destination ports
  UDP source and destination ports
The following fields may be optionally supported:
Physical port
Metadata
Ethernet type
VLAN ID and VLAN user priority
IPv4 or IPv6 DS and ECN
SCTP source and destination ports
ICMP type and code fields
ARP opcodes
Source and target IPv4 addresses in ARP payload
IPv6 flow label
ICMPv6 type and code fields
IPv6 neighbor discovery source and target addresses
MPLS label value, traffic class, and BoS
Notes: The match fields component of a table entry consists
of the following required fields:
• Ingress port: The identifier of the port on this switch on which the packet
arrived. This may be a physical port or a switch-defined virtual port.
• Ethernet source and destination addresses: Each entry can be an exact address,
a bitmasked value for which only some of the address bits are checked, or a
wildcard value (match any value).
• IPv4 or IPv6 protocol number: A protocol number value, indicating the next
header in the packet.
• IPv4 or IPv6 source address, and destination address: Each entry can be an
exact address, a bitmasked value, a subnet mask value, or a wildcard value.
• TCP source and destination ports: Exact match or wildcard value.
• UDP source and destination ports: Exact match or wildcard value.
The preceding match fields must be supported by any OpenFlow-compliant
switch. The following fields may be optionally supported.
• Physical port: Used to designate underlying physical port when packet is
received on a logical port.
• Metadata: Additional information that can be passed from one table to
another during the processing of a packet. Its use is discussed subsequently.
• Ethernet type: Ethernet Type field.
• VLAN ID and VLAN user priority: Fields in the IEEE 802.1Q virtual LAN
header.
• IPv4 or IPv6 DS and ECN: Differentiated Services and Explicit Congestion
Notification fields.
• SCTP source and destination ports: Exact match or wildcard value.
• ICMP type and code fields: Exact match or wildcard value.
• ARP opcode: Exact match in Ethernet Type field.
• Source and target IPv4 addresses in ARP payload: Can be an exact address, a
bitmasked value, a subnet mask value, or a wildcard value.
• IPv6 flow label: Exact match or wildcard.
• ICMPv6 type and code fields: Exact match or wildcard value.
• IPv6 neighbor discovery target address: In an IPv6 Neighbor Discovery message.
• IPv6 neighbor discovery source and target addresses: Link-layer address
options in an IPv6 Neighbor Discovery message.
• MPLS label value, traffic class, and BoS: Fields in the top label of an MPLS
label stack.
Thus, OpenFlow can be used with network traffic involving a variety of protocols
and network services. Note that at the MAC/link layer, only Ethernet is supported.
Thus, OpenFlow as currently defined cannot control layer 2 traffic over
wireless networks.
We can now offer a more precise definition of the term flow . From the point
of view of an individual switch, a flow is a sequence of packets that matches a specific
entry in a flow table. The definition is packet oriented, in the sense that it is
function of the values of header fields of the packets that constitute the flow, and
not a function of the path they follow through the network. A combination of flow
entries on multiple switches defines a flow that is bound to a specific path.

## Slide 51: Instructions Component
Consist of a set of instructions that are executed if the packet matches the entry
“Actions” describe packet forwarding, packet modification, and group table processing operations
The OpenFlow specification includes the following actions
  Output
  Set-Queue
  Group
  Push-Tag/Pop-Tag
  Set-Field
  Change-TTL
Notes: The instructions component of a table entry consists
of a set of instructions that are executed if the packet matches the entry. Before
describing the types of instructions, we need to define the terms action and action
set . Actions describe packet forwarding, packet modification, and group table processing
operations. The OpenFlow specification includes the following actions:
• Output: Forward packet to specified port.
• Set-Queue: Sets the queue id for a packet. When the packet is forwarded to a
port using the output action, the queue id determines which queue attached to
this port is used for scheduling and forwarding the packet. Forwarding behavior
is dictated by the configuration of the queue and is used to provide basic
Quality-of-Service (QoS) support
• Group: Process packet through specified group.
• Push-Tag/Pop-Tag: Push or pop a tag field for a VLAN or MPLS packet.
• Set-Field: The various Set-Field actions are identified by their field type and
modify the values of respective header fields in the packet.
• Change-TTL: The various Change-TTL actions modify the values of the IPv4
TTL, IPv6 Hop Limit, or MPLS TTL in the packet.

## Slide 52: Instructions Component
“Action set” is a list of actions associated with a packet that are accumulated while the packet is processed by each table and that are executed when the packet exits the processing pipeline
Instructions are of four types
Direct packet through pipeline
Perform action on packet
Update action set
Update metadata
Notes: An action set is a list of actions associated with a packet that are accumulated
while the packet is processed by each table and that are executed when the packet
exits the processing pipeline.
Instructions are of four types:
• Direct packet through pipeline: The Goto-Table instruction directs the packet
to a table farther along in the pipeline. The Meter instruction directs the
packet to a specified meter.
• Perform action on packet: Actions may be performed on the packet when it is
matched to a table entry.
• Update action set: Merge specified actions into the current action set for this
packet on this flow, or clear all the actions in the action set.
• Update metadata: A metadata value can be associated with a packet. It is used
to carry information from one table to the next.

## Slide 53
Notes: A switch includes one or more flow tables. If there is more than one flow table, they
are organized as a pipeline (Figure 21.9), with the tables labeled with increasing
numbers starting with 0. When a packet is presented to a table for matching, the
input consists of the packet, the identity of the ingress port, the associated metadata
value, and the associated action set. For Table , the metadata value is blank and the
action set is null. Processing proceeds as follows:
1. Find the highest-priority matching flow entry. If there is no match on any
entry and there is no table-miss entry, then the packet is dropped. If there is a
match only on a table-miss entry, then that entry specifies one of three actions:
a. Send packet to controller. This will enable the controller to define a new
flow for this and similar packets, or decide to drop the packet.
b. Direct packet to another flow table farther down the pipeline.
c. Drop the packet.
2. If there is a match on one or more entries, other than the table-miss entry,
then the match is defined to be with the highest-priority matching entry. The
following actions may then be performed:
a. Update any counters associated with this entry.
b. Execute any instructions associated with this entry. This may include updating
the action set, updating the metadata value, and performing actions.
c. The packet is then forwarded to a flow table further down the pipeline, to
the group table, to the meter table, or directed to an output port.
For the final table in the pipeline, forwarding to another flow table is not an
option.
If and when a packet is finally directed to an output port, the accumulated
action set is executed and then the packet is queued for output.

## Slide 54: Table 21.2 OpenFlow Messages
(The table can be found on page 689 in the textbook)
Notes: The OpenFlow protocol describes message exchanges that take place between an
OpenFlow controller and an OpenFlow switch. Typically, the protocol is implemented
on top of SSL or TLS, providing a secure OpenFlow channel.
The OpenFlow protocol enables the controller to perform add, update, and
delete actions to the flow entries in the flow tables. It supports 3 types of messages
(Table 21.2):
• Controller-to-Switch: These messages are initiated by the controller and, in
some cases, require a response from the switch. This class of messages enables
the controller to manage the logical state of the switch, including its configuration
and details of flow and group table entries. Also included in this class is
the Packet-out message. This message is used when a switch sends a packet to
the controller and the controller decides not to drop the packet but to direct it
to a switch output port.
• Asynchronous: These types of messages are sent without solicitation from the
controller. This class includes various status messages to the controller. Also
included is the Packet-in message, which may be used by the switch to send a
packet to the controller when there is no flow table match.
• Symmetric: These messages are sent without solicitation from either the controller
or the switch. They are simple yet helpful. Hello messages are typically
sent back and forth between the controller and switch when the connection
is first established. Echo request and reply messages can be used
by either the switch or controller to measure the latency or bandwidth of a
controller-switch connection or just verify that the device is up and running.
The Experimenter message is used to stage features to be built into future
versions of OpenFlow.
The OpenFlow protocol enables the controller to manage the logical structure
of a switch, without regard to the details of how the switch implements the
OpenFlow logical architecture.

## Slide 55: Discovery
Similar to the router advertisement process defined in ICMP
Mobile node is responsible for an ongoing discovery process
  Home or foreign network
  Listens for agent advertisement message
  Compares IP address with home address
  If these do not match the mobile node is on a foreign network
Notes: The discovery process in Mobile IP is very similar to the router advertisement process defined in ICMP. Accordingly, agent discovery makes use of ICMP router advertisement messages, with one or more extensions specific to Mobile IP.
The mobile node is responsible for an ongoing discovery process. It must determine if it is attached to its home network, in which case IP datagrams may be received without forwarding, or if it is attached to a foreign network. Because handoff from one network to another occurs at the physical layer, a transition from the home network to a foreign network can occur at any time without notification to the network layer (i.e., the IP layer). Thus, discovery for a mobile node is a continuous process.
For the purpose of discovery, a router or other network node that can act as an agent periodically issues a router advertisement ICMP message (Figure 21.8d) with an advertisement extension. The router advertisement portion of the message includes the IP address of the router. The advertisement extension includes additional information about the router's role as an agent, as discussed subsequently. A mobile node listens for these agent advertisement messages. Because a foreign agent could be on the mobile node's home network (set up to serve visiting mobile nodes), the arrival of an agent advertisement does not necessarily tell the mobile node that it is on a foreign network. The mobile node must compare the network portion of the router's IP address with the network portion of its own home address. If these network portions do not match, then the mobile node is on a foreign network.
The agent advertisement extension follows the ICMP router advertisement fields. The extension includes the following one-bit flags:
R: Registration with this foreign agent is required (or another foreign agent on this network). Even those mobile nodes that have already acquired a care-of address from this foreign agent must re-register.
B: Busy. The foreign agent will not accept registrations from additional mobile nodes.
H: This agent offers services as a home agent on this network.
F: This agent offers services as a foreign agent on this network.
M: This agent can receive tunneled IP datagrams that use minimal encapsulation, explained subsequently.
G: This agent can receive tunneled IP datagrams that use GRE encapsulation, explained subsequently.
r: reserved.
T: Foreign agent supports reverse tunneling.
In addition, the extension includes zero or more care-of addresses supported by this agent on this network. There must be at least one such address if the F bit is set. There may be multiple addresses.

## Slide 56: Use of Lifetime Field
Upon receipt of an agent advertisement from a foreign agent the mobile node records the lifetime field as a timer
If timer expires before receipt of another advertisement, node assumes it lost contact
If node has received an advertisement that is not expired, node registers with the new agent
Otherwise, node uses agent solicitation to find an agent
Notes: As was mentioned, a mobile node may move from one network to another due to some handoff mechanism, without the IP level being aware of it. The agent discovery process is intended to enable the agent to detect such a move. The agent may use one of two algorithms for this purpose:
Use of lifetime field: When a mobile node receives an agent advertisement from a foreign agent that it is currently using or that it is now going to register with, it records the lifetime field as a timer. If the timer expires before the mobile node receives another agent advertisement from the agent, then the node assumes that it has lost contact with that agent. If, in the meantime, the mobile node has received an agent advertisement from another agent and that advertisement has not yet expired, the mobile node can register with this new agent. Otherwise, the mobile node should use agent solicitation to find an agent.

## Slide 57: Use of Network Prefix
Mobile node checks if newly received agent advertisement is on the same network as the node’s current care-of address
If it is not, the node assumes it moved and registers with advertisement the node has just received
Notes: Use of network prefix: The mobile node checks whether any newly received agent advertisement is on the same network as the node's current care-of address. If it is not, the mobile node assumes that it has moved and may register with the agent whose advertisement the mobile node has just received.

## Slide 58: Co-Located Address
Node may move to a network that has no foreign agents or foreign agents are busy
  May act as its own foreign agent by using a co-located care-of address
Co-located care-of address is an IP address that is associated with the node’s current interface to a network
  Can dynamically acquire a temporary IP address
  Co-located address may be owned by the node
Notes: CO-LOCATED ADDRESSES
The discussion so far has involved the use of a care-of address associated with a foreign agent; that is, the care-of address is an IP address for the foreign agent. This foreign agent will receive datagrams at this care-of address, intended for the mobile node, and then forward them across the foreign network to the mobile node. However, in some cases a mobile node may move to a network that has no foreign agents or on which all foreign agents are busy. As an alternative, the mobile node may act as its own foreign agent by using a co-located care-of address. A co-located care-of address is an IP address obtained by the mobile node that is associated with the mobile node's current interface to a network.
The means by which a mobile node acquires a co-located address is beyond the scope of Mobile IP. One means is to dynamically acquire a temporary IP address through an Internet service such as DHCP (Dynamic Host Configuration Protocol). Another alternative is that the co-located address may be owned by the mobile node as a long-term address for use only while visiting a given foreign network.

## Slide 59: Registration
Once care-of address is acquired the mobile node needs to request the home agent forward its IP traffic
Registration process:
  If node is using a co-located care-of address it registers directly with its home agent
Node sends a registration request to the foreign agent requesting forwarding service
Foreign agent relays request to home agent
Home agent accepts or denies request
Foreign agent relays reply to node
Notes: Once a mobile node has recognized that it is on a foreign network and has acquired a care-of address, it needs to alert a home agent on its home network and request that the home agent forward its IP traffic. The registration process involves four steps:
The mobile node requests the forwarding service by sending a registration request to the foreign agent that the mobile node wants to use.
The foreign agent relays this request to the mobile node's home agent.
The home agent either accepts or denies the request and sends a registration reply to the foreign agent.
The foreign agent relays this reply to the mobile node.
If the mobile node is using a co-located care-of address, then it registers directly with its home agent, rather than going through a foreign agent.

## Slide 60: Registration Messages
Registration operation uses two types of messages carried in UDP segments
Registration request message includes:
  One-bit flags
  Home address field
  Home agent field
  Care-of address field
  Identification field
  Registration reply message includes:
  Acceptance code
  Reason for denial
Notes: The registration operation uses two types of messages, carried in UDP segments. The registration request message includes the following one-bit flags:
S: Simultaneous bindings. The mobile node is requesting that the home agent retain its prior mobility bindings. When simultaneous bindings are in effect, the home agent will forward multiple copies of the IP datagram, one to each care-of address currently registered for this mobile node. Multiple simultaneous bindings can be useful in wireless handoff situations, to improve reliability.
B: Broadcast datagrams. Indicates that the mobile node would like to receive copies of broadcast datagrams that it would have received if it were attached to its home network.
D: Decapsulation by mobile node. The mobile node is using a co-located care-of address and will decapsulate its own tunneled IP datagrams.
M: Indicates that the home agent should use minimal encapsulation, explained subsequently.
G: Indicates that the home agent should use GRE encapsulation, explained subsequently.
T: Reverse tunneling requested.
In addition, the message includes the following fields:
Home Address: The home IP address of the mobile node. The home agent can expect to receive IP datagrams with this as a destination address, and must forward those to the care-of address.
Home Agent: The IP address of the mobile node's home agent. This informs the foreign agent of the address to which this request should be relayed.
Care-Of Address: The IP address at this end of the tunnel. The home agent should forward IP datagrams that it receives with mobile node's home address to this destination address.
Identification: A 64-bit number generated by the mobile node, used for matching registration requests to registration replies and for security purposes, as explained subsequently.
Extensions: The only extension so far defined is the authentication extension, explained subsequently.
The registration reply message includes a code that indicates whether the request is accepted and, if not, the reason for denial.

## Slide 61: Registration Security
Mobile IP is designed to resist two types of attacks:
  Node pretends to be a foreign agent and sends registration request to home agent to divert traffic
  Malicious agent may replay old registration messages effectively cutting node from the network
Notes: A key concern with the registration procedure is security. Mobile IP is designed to resist two types of attacks:
A node may pretend to be a foreign agent and send a registration request to a home agent so as to divert traffic intended for a mobile node to itself.
A malicious agent may replay old registration messages, effectively cutting the mobile node from the network.

## Slide 62: Message Authentication
Message authentication is used to protect against registration message attacks
Authentication extension includes the following fields:
  Security parameter index (SPI)
  Authenticator
Three types of authentication extensions:
Mobile-home
Mobile-foreign
Foreign-home
Notes: The technique that is used to protect against such attacks involves the use of message authentication and the proper use of the identification field of the registration request and reply messages.
For purposes of message authentication, each registration request and reply contains an authentication extension, which includes the following fields:
Security Parameter Index (SPI): An index that identifies a security context between a pair of nodes. This security context is configured so that the two nodes share a secret key and parameters relevant to this association (e.g., authentication algorithm).
Authenticator: A code used to authenticate the message. The sender inserts this code into the message using a shared secret key. The receiver uses the code to ensure that the message has not been altered or delayed. The authenticator protects the entire registration request or reply message, any extensions prior to this extension, and the type and length fields of this extension.
The default authentication algorithm is HMAC-MD5, defined in RFC 2104, which produces a 128-bit message digest. HMAC-MD4 is an example of what is known as a keyed hash code. Appendix R describes such codes. The digest is computed over a shared secret key, and the protected fields from the registration message.
Three types of authentication extensions are defined:
Mobile-home: This extension must be present and provides for authentication of the registration messages between the mobile node and the home agent.
Mobile-foreign: The extension may be present when a security association exists between the mobile node and the foreign agent. The foreign agent will strip this extension off before relaying a request message to the home agent and add this extension to a reply message coming from a home agent.
Foreign-home: The extension may be present when a security association exists between the foreign agent and the home agent.
Note that the authenticator protects the identification field in the request and reply messages. As a result, the identification value can be used to thwart replay types of attacks. As was mentioned, the identification value enables the mobile node to match a reply to a request. Further, if the mobile node and the home agent maintain synchronization, so that the home agent can distinguish a reasonable identification value from a suspicious one, then the home agent can reject suspicious messages. One way to do this is to use a timestamp value. As long as the mobile node and home agent have reasonably synchronized values of time, the timestamp will serve the purpose. Alternatively, the mobile node could generate values using a pseudorandom number generator. If the home agent knows the algorithm, then it knows what identification value to expect next.