## Slide 1: Data and Computer Communications
Tenth Edition
by William Stallings
Notes: “Data and Computer Communications”, 10/e, by William Stallings, Chapter 11 “Local Area Network Overview”.

## Slide 2: Local Area Network Overview
Chapter 11
Notes: In this chapter, we look at the underlying technology and protocol architecture
of LANs. Chapters 12 and 13 are devoted to a discussion of specific
LAN systems.

## Slide 3: Bus Topology
Topology
  Refers to the way in which the endpoints, or stations, attached to the network are interconnected
Bus topology
  All stations attach, through a tap, directly to a linear transmission medium, or bus
  Full-duplex operation between the station and the tap allows data to be transmitted onto the bus and received from the bus
  A transmission from any station propagates the length of the medium in both directions and can be received by all other stations
  At each end of the bus is a terminator, which absorbs any signal, removing it from the bus
Notes: In the context of a communication network, the term topology refers to the way
in which the endpoints, or stations, attached to the network are interconnected.
Historically, common topologies for LANs are bus, tree, ring, and star. In contemporary
LANs, the star topology, based around the use of switches, dominates.
However, it is useful to briefly look at the operation of the bus topology because it
shares some characteristics with wireless LANs, and key elements of wireless LAN
access protocols evolved from bus LAN access protocols. In this section, we first
describe the bus topology, and then introduce the star topology.
In the bus topology , all stations attach, through appropriate hardware interfacing
known as a tap, directly to a linear transmission medium, or bus. Full-duplex operation
between the station and the tap allows data to be transmitted onto the bus and
received from the bus. A transmission from any station propagates the length of the
medium in both directions and can be received by all other stations. At each end of
the bus is a terminator, which absorbs any signal, removing it from the bus.
Two problems present themselves in this arrangement. First, because a transmission
from any one station can be received by all other stations, there needs
to be some way of indicating for whom the transmission is intended. Second, a
mechanism is needed to regulate transmission. To see the reason for this, consider
that if two stations on the bus attempt to transmit at the same time, their signals
will overlap and become garbled. Or consider that if one station decides to transmit
continuously for a long period of time, other stations will be blocked from
transmitting.
To solve these problems, stations transmit data in small blocks, known as
frames. Each frame consists of a portion of the data that a station wishes to transmit,
plus a frame header that contains control information. Each station on the bus
is assigned a unique address, or identifier, and the destination address for a frame is
included in its header.
So the frame structure solves the first problem mentioned previously: It provides a
mechanism for indicating the intended recipient of data. It also provides the basic
tool for solving the second problem, the regulation of access. In particular, the stations
take turns sending frames in some cooperative fashion. This involves putting
additional control information into the frame header, as discussed later.
No special action needs to be taken to remove frames from the bus. When a
signal reaches the end of the bus, it is absorbed by the terminator.

## Slide 4
Notes: Figure 11.1 illustrates the bus scheme. In this example, station
C wishes to transmit a frame of data to A. The frame header includes A’s address.
As the frame propagates along the bus, it passes B. B observes the address and
ignores the frame. A, on the other hand, sees that the frame is addressed to itself
and therefore copies the data from the frame as it goes by.

## Slide 5: Star Topology
Each station connects to common central node
  Usually via two point-to-point links
    One for transmission and one for reception
Central node
Operate in broadcast fashion
Physical star, logical bus
Only one station can transmit at a time (hub)
Can act as frame switch
Notes: In the star LAN topology, each station is directly connected to a common central node. Typically, each station attaches to a central node via two point-to-point links, one for transmission and one for reception.
In general, there are two alternatives for the operation of the central node. One approach is for the central node to operate in a broadcast fashion. A transmission of a frame from one station to the node is retransmitted on all of the outgoing links. In this case, although the arrangement is physically a star, it is logically a bus: A transmission from any station is received by all other stations, and only one station at a time may successfully transmit. In this case, the central element is referred to as a hub. Another approach is for the central node to act as a frame-switching device. An incoming frame is buffered in the node and then retransmitted on an outgoing link to the destination station.

## Slide 6
Notes: In the star LAN topology, each station is directly connected to a common central
node (Figure 11.2).

## Slide 7
Notes: Protocols defined specifically for LAN and metropolitan area networks (MAN)
transmission address issues relating to the transmission of blocks of data over the
network. In OSI (open systems interconnection) terms, higher layer protocols
(layer 3 or 4 and above) are independent of network architecture and are applicable
to LANs, MANs, and WANs. Thus, a discussion of LAN protocols is concerned
principally with lower layers of the OSI model.
Figure 11.3 relates the LAN protocols to the OSI architecture. This architecture
was developed by the IEEE 802 LAN standards committee and has been
adopted by all organizations working on the specification of LAN standards. It is
generally referred to as the IEEE 802 reference model.

## Slide 8: IEEE 802 Reference Model
Lowest layer corresponds to the physical layer of the OSI model
  Includes a specification of the transmission medium and the topology
Includes functions such as:
Encoding/decoding of signals
Preamble generation/removal
Bit transmission/reception
Notes: The lowest layer of the IEEE 802 reference model corresponds to the physical layer of the OSI model and includes such functions as
Encoding/decoding of signals
Preamble generation/removal (for synchronization)
Bit transmission/reception
In addition, the physical layer of the 802 model includes a specification of the transmission medium and the topology. Generally, this is considered "below" the lowest layer of the OSI model. However, the choice of transmission medium and topology is critical in LAN design, and so a specification of the medium is included.

## Slide 9: IEEE 802 Layers
Logical Link Control Layer (LLC)
  Provide interface to higher levels
  Perform flow and error control
Media Access Control (MAC)
  On transmit assemble data into frame
  On reception disassemble frame, perform address recognition and error detection
  Govern access to LAN transmission medium
Notes: Above the physical layer are the functions associated with providing service to LAN users. These include
On transmission, assemble data into a frame with address and error-detection fields.
On reception, disassemble frame, and perform address recognition and error detection.
Govern access to the LAN transmission medium.
Provide an interface to higher layers and perform flow and error control.
These are functions typically associated with OSI layer 2. The set of functions in the last bullet item are grouped into a logical link control (LLC) layer. The functions in the first three bullet items are treated as a separate layer, called medium access control (MAC). The separation is done for the following reasons:
The logic required to manage access to a shared-access medium is not found in traditional layer 2 data link control.
For the same LLC, several MAC options may be provided.

## Slide 10
Notes: Figure 11.4 illustrates the relationship between the levels of the architecture
(compare Figure 2.5). Higher-level data are passed down to LLC, which appends
control information as a header, creating an LLC protocol data unit (PDU ). This
control information is used in the operation of the LLC protocol. The entire LLC
PDU is then passed down to the MAC layer, which appends control information at
the front and back of the packet, forming a MAC frame . Again, the control information
in the frame is needed for the operation of the MAC protocol. For context,
the figure also shows the use of TCP/IP and an application layer above the LAN
protocols.

## Slide 11: LLC Services
Unacknowledged connectionless service
Data-gram style service
Connection-mode service
Logical connection is set up between two users
Delivery of data is not guaranteed
Flow and error control are provided
Acknowledged connectionless service
Datagrams are to be acknowledged, but no logical connection is set up
Notes: LLC specifies the mechanisms for addressing stations across the medium and for controlling the exchange of data between two users. The operation and format of this standard is based on HDLC. Three services are provided as alternatives for attached devices using LLC:
Unacknowledged connectionless service: This service is a datagram-style service. It is a very simple service that does not involve any of the flow- and error-control mechanisms. Thus, the delivery of data is not guaranteed. However, in most devices, there will be some higher layer of software that deals with reliability issues.
Connection-mode service: This service is similar to that offered by HDLC. A logical connection is set up between two users exchanging data, and flow control and error control are provided.
Acknowledged connectionless service: This is a cross between the previous two services. It provides that datagrams are to be acknowledged, but no prior logical connection is set up.
Typically, a vendor will provide these services as options that the customer can select when purchasing the equipment. Alternatively, the customer can purchase equipment that provides two or all three services and select a specific service based on application.

## Slide 12: LLC Service Alternatives
Unacknowledged connectionless service
Requires minimum logic
Connection-mode service
Used in simple devices
Avoids duplication of mechanisms
Preferred option in most cases
Provides flow control and reliability mechanisms
Acknowledged connectionless service
Large communication channel needed
Time critical or emergency control signals
Notes: The unacknowledged connectionless service requires minimum logic and is useful in two contexts. First, it will often be the case that higher layers of software will provide the necessary reliability and flow-control mechanism, and it is efficient to avoid duplicating them. For example, TCP could provide the mechanisms needed to ensure that data is delivered reliably. Second, there are instances in which the overhead of connection establishment and maintenance is unjustified or even counterproductive (for example, data collection activities that involve the periodic sampling of data sources, such as sensors and automatic self-test reports from security equipment or network components). In a monitoring application, the loss of an occasional data unit would not cause distress, as the next report should arrive shortly. Thus, in most cases, the unacknowledged connectionless service is the preferred option.
The connection-mode service could be used in very simple devices, such as terminal controllers, that have little software operating above this level. In these cases, it would provide the flow control and reliability mechanisms normally implemented at higher layers of the communications software.
The acknowledged connectionless service is useful in several contexts. With the connection-mode service, the logical link control software must maintain some sort of table for each active connection, to keep track of the status of that connection. If the user needs guaranteed delivery but there are a large number of destinations for data, then the connection-mode service may be impractical because of the large number of tables required. An example is a process control or automated factory environment where a central site may need to communicate with a large number of processors and programmable controllers. Another use of this is the handling of important and time-critical alarm or emergency control signals in a factory. Because of their importance, an acknowledgment is needed so that the sender can be assured that the signal got through. Because of the urgency of the signal, the user might not want to take the time first to establish a logical connection and then send the data.

## Slide 13
Notes: All three LLC protocols employ the same PDU format (Figure 11.5), which
consists of four fields. The DSAP (Destination Service Access Point) and SSAP
(Source Service Access Point) fields each contain a 7-bit address, which specifies
the destination and source users of LLC. One bit of the DSAP indicates whether the
DSAP is an individual or group address. One bit of the SSAP indicates whether the
PDU is a command or response PDU. The format of the LLC control field is identical
to that of HDLC (Figure 7.7), using extended (7-bit) sequence numbers.
For type 1 operation , which supports the unacknowledged connectionless
service, the unnumbered information (UI) PDU is used to transfer user data. There
is no acknowledgment, flow control, or error control. However, there is error detection
and discard at the MAC level.

## Slide 14: Medium Access Control (MAC) Protocol
Controls access to the transmission medium
Key parameters:
  Where
    Greater control, single point of failure
    More complex, but more redundant
  How
    Synchronous
      Capacity dedicated to connection, not optimal
    Asynchronous
      Response to demand
      Round robin, reservation, contention
Notes: All LANs and MANs consist of collections of devices that must share the network's transmission capacity. Some means of controlling access to the transmission medium is needed to provide for an orderly and efficient use of that capacity. This is the function of a medium access control (MAC) protocol.
The key parameters in any medium access control technique are where and how. Where refers to whether control is exercised in a centralized or distributed fashion. In a centralized scheme, a controller is designated that has the authority to grant access to the network. A station wishing to transmit must wait until it receives permission from the controller. In a decentralized network, the stations collectively perform a medium access control function to determine dynamically the order in which stations transmit. A centralized scheme has certain advantages, including
It may afford greater control over access for providing such things as priorities, overrides, and guaranteed capacity.
It enables the use of relatively simple access logic at each station.
It avoids problems of distributed coordination among peer entities
The principal disadvantages of centralized schemes are
It creates a single point of failure; that is, there is a point in the network that, if it fails, causes the entire network to fail.
It may act as a bottleneck, reducing performance.
The pros and cons of distributed schemes are mirror images of the points just made.
The second parameter, how, is constrained by the topology and is a tradeoff among competing factors, including cost, performance, and complexity. In general, we can categorize access control techniques as being either synchronous or asynchronous. With synchronous techniques, a specific capacity is dedicated to a connection. This is the same approach used in circuit switching, frequency division multiplexing (FDM), and synchronous time division multiplexing (TDM). Such techniques are generally not optimal in LANs and MANs because the needs of the stations are unpredictable. It is preferable to be able to allocate capacity in an asynchronous (dynamic) fashion, more or less in response to immediate demand. The asynchronous approach can be further subdivided into three categories: round robin, reservation, and contention.

## Slide 15: Asynchronous Systems
Round robin
Each station given turn to transmit data
Reservation
Divide medium into slots
Contention
All stations contend for time
Good for stream traffic
Good for bursty traffic
Simple to implement
Tends to collapse under heavy load
Notes: With round robin, each station in turn is given the opportunity to transmit. During that opportunity, the station may decline to transmit or may transmit subject to a specified upper bound, usually expressed as a maximum amount of data transmitted or time for this opportunity. In any case, the station, when it is finished, relinquishes its turn, and the right to transmit passes to the next station in logical sequence. Control of sequence may be centralized or distributed. Polling is an example of a centralized technique.
When many stations have data to transmit over an extended period of time, round-robin techniques can be very efficient. If only a few stations have data to transmit over an extended period of time, then there is a considerable overhead in passing the turn from station to station, because most of the stations will not transmit but simply pass their turns. Under such circumstances other techniques may be preferable, largely depending on whether the data traffic has a stream or bursty characteristic. Stream traffic is characterized by lengthy and fairly continuous transmissions; examples are voice communication, telemetry, and bulk file transfer. Bursty traffic is characterized by short, sporadic transmissions; interactive terminal-host traffic fits this description.
RESERVATION
For stream traffic, reservation techniques are well suited. In general, for these techniques, time on the medium is divided into slots, much as with synchronous TDM. A station wishing to transmit reserves future slots for an extended or even an indefinite period. Again, reservations may be made in a centralized or distributed fashion.
CONTENTION
For bursty traffic, contention techniques are usually appropriate. With these techniques, no control is exercised to determine whose turn it is; all stations contend for time in a way that can be, as we shall see, rather rough and tumble. These techniques are of necessity distributed in nature. Their principal advantage is that they are simple to implement and, under light to moderate load, efficient. For some of these techniques, however, performance tends to collapse under heavy load.
Although both centralized and distributed reservation techniques have been implemented in some LAN products, round-robin and contention techniques are the most common.

## Slide 16: MAC Frame Handling
MAC layer receives data from LLC layer
PDU is referred to as a MAC frame
MAC layer detects errors and discards frames
LLC optionally retransmits unsuccessful frames
Fields:
MAC control
Destination MAC address
Source MAC address
LLC
CRC
Notes: The MAC layer receives a block of data from the LLC layer and is responsible for performing functions related to medium access and for transmitting the data. As with other protocol layers, MAC implements these functions making use of a protocol data unit at its layer. In this case, the PDU is referred to as a MAC frame.
The exact format of the MAC frame differs somewhat for the various MAC protocols in use. In general, all of the MAC frames have a format similar to that of Stallings DCC9e Figure 11.5. The fields of this frame are
MAC Control: This field contains any protocol control information needed for the functioning of the MAC protocol. For example, a priority level could be indicated here.
Destination MAC Address: The destination physical attachment point on the LAN for this frame.
Source MAC Address: The source physical attachment point on the LAN for this frame.
LLC: The LLC data from the next higher layer.
CRC: The Cyclic Redundancy Check field (also known as the frame check sequence, FCS, field). This is an error-detecting code, as we have seen in HDLC and other data link control protocols (Chapter 7).
In most data link control protocols, the data link protocol entity is responsible not only for detecting errors using the CRC, but for recovering from those errors by retransmitting damaged frames. In the LAN protocol architecture, these two functions are split between the MAC and LLC layers. The MAC layer is responsible for detecting errors and discarding any frames that are in error. The LLC layer optionally keeps track of which frames have been successfully received and retransmits unsuccessful frames.

## Slide 17: Bridges
Connects similar LANs with identical physical and link layer protocols
Minimal processing
Can map between MAC formats
Reasons for use:
  Reliability
  Performance
  Security
  Geography
Notes: In virtually all cases, there is a need to expand beyond the confines of a single LAN, to provide interconnection to other LANs and to wide area networks. Two general approaches are used for this purpose: bridges and routers. The bridge is the simpler of the two devices and provides a means of interconnecting similar LANs. The router is a more general-purpose device, capable of interconnecting a variety of LANs and WANs. We explore bridges in this section and look at routers in Part Five.
The bridge is designed for use between local area networks (LANs) that use identical protocols for the physical and link layers (e.g., all conforming to IEEE 802.3). Because the devices all use the same protocols, the amount of processing required at the bridge is minimal. More sophisticated bridges are capable of mapping from one MAC format to another (e.g., to interconnect an Ethernet and a token ring LAN).
Because the bridge is used in a situation in which all the LANs have the same characteristics, the reader may ask, why not simply have one large LAN? Depending on circumstance, there are several reasons for the use of multiple LANs connected by bridges:
Reliability: The danger in connecting all data processing devices in an organization to one network is that a fault on the network may disable communication for all devices. By using bridges, the network can be partitioned into self-contained units.
Performance: In general, performance on a LAN declines with an increase in the number of devices or the length of the wire. A number of smaller LANs will often give improved performance if devices can be clustered so that intranetwork traffic significantly exceeds internetwork traffic.
Security: The establishment of multiple LANs may improve security of communications. It is desirable to keep different types of traffic (e.g., accounting, personnel, strategic planning) that have different security needs on physically separate media. At the same time, the different types of users with different levels of security need to communicate through controlled and monitored mechanisms.
Geography: Clearly, two separate LANs are needed to support devices clustered in two geographically distant locations. Even in the case of two buildings separated by a highway, it may be far easier to use a microwave bridge link than to attempt to string coaxial cable between the two buildings.

## Slide 18
Notes: Figure 11.6 illustrates the action of a bridge connecting two
LANs, A and B, using the same MAC protocol. In this example, a single bridge
attaches to both LANs; frequently, the bridge function is performed by two “halfbridges,”
one on each LAN. The functions of the bridge are few and simple:
• Read all frames transmitted on A and accept those addressed to any station
on B.
• Using the medium access control protocol for B, retransmit each frame
on B.
• Do the same for B-to-A traffic.

## Slide 19: Bridge Design Aspects
Makes no modification to the content or format of the frames it receives
Should contain enough buffer space to meet peak demands
Must contain routing and addressing intelligence
May connect more than two LANs
Bridging is transparent to stations
Notes: Several design aspects of a bridge are worth highlighting:
The bridge makes no modification to the content or format of the frames it receives, nor does it encapsulate them with an additional header. Each frame to be transferred is simply copied from one LAN and repeated with exactly the same bit pattern on the other LAN. Because the two LANs use the same LAN protocols, it is permissible to do this.
The bridge should contain enough buffer space to meet peak demands. Over a short period of time, frames may arrive faster than they can be retransmitted.
The bridge must contain addressing and routing intelligence. At a minimum, the bridge must know which addresses are on each network to know which frames to pass. Further, there may be more than two LANs interconnected by a number of bridges. In that case, a frame may have to be routed through several bridges in its journey from source to destination.
A bridge may connect more than two LANs.
In summary, the bridge provides an extension to the LAN that requires no modification to the communications software in the stations attached to the LANs. It appears to all stations on the two (or more) LANs that there is a single LAN on which each station has a unique address. The station uses that unique address and need not explicitly discriminate between stations on the same LAN and stations on other LANs; the bridge takes care of that.

## Slide 20
Notes: The IEEE 802.1D specification defines the protocol architecture for MAC bridges.
Within the 802 architecture, the endpoint or station address is designated at the
MAC level. Thus, it is at the MAC level that a bridge can function. Figure 11.7
shows the simplest case, which consists of two LANs connected by a single bridge.
The LANs employ the same MAC and LLC protocols. The bridge operates as previously
described. A MAC frame whose destination is not on the immediate LAN
is captured by the bridge, buffered briefly, and then transmitted on the other LAN.
As far as the LLC layer is concerned, there is a dialogue between peer LLC entities
in the two endpoint stations. The bridge need not contain an LLC layer because it is
merely serving to relay the MAC frames.
Figure 11.7b indicates the way in which data are encapsulated using a bridge.
Data are provided by some user to LLC. The LLC entity appends a header and
passes the resulting data unit to the MAC entity, which appends a header and a
trailer to form a MAC frame. On the basis of the destination MAC address in the
frame, it is captured by the bridge. The bridge does not strip off the MAC fields; its
function is to relay the MAC frame intact to the destination LAN. Thus, the frame
is deposited on the destination LAN and captured by the destination station.
The concept of a MAC relay bridge is not limited to the use of a single bridge
to connect two nearby LANs. If the LANs are some distance apart, then they can
be connected by two bridges that are in turn connected by a communications facility.
The intervening communications facility can be a network, such as a wide area
packet-switching network, or a point-to-point link. In such cases, when a bridge captures
a MAC frame, it must encapsulate the frame in the appropriate packaging and
transmit it over the communications facility to a target bridge. The target bridge
strips off these extra fields and transmits the original, unmodified MAC frame to
the destination station.

## Slide 21
Notes: There is a trend within many organizations to an increasing number of LANs
interconnected by bridges. As the number of LANs grows, it becomes important
to provide alternate paths between LANs via bridges for load balancing and
reconfiguration in response to failure. Thus, many organizations will find that static,
preconfigured routing tables are inadequate and that some sort of dynamic routing
is needed.
Consider the configuration of Figure 11.8. Suppose that
station 1 transmits a frame on LAN A intended for station 6. The frame will be
read by bridges 101, 102, and 107. For each bridge, the addressed station is not
on a LAN to which the bridge is attached. Therefore, each bridge must make a
decision whether or not to retransmit the frame on its other LAN, in order to
move it closer to its intended destination. In this case, bridge 102 should repeat
the frame on LAN C, whereas bridges 101 and 107 should refrain from retransmitting
the frame. Once the frame has been transmitted on LAN C, it will be
picked up by both bridges 105 and 106. Again, each must decide whether or not
to forward the frame. In this case, bridge 105 should retransmit the frame on
LAN F, where it will be received by the destination, station 6.
Thus we see that, in the general case, the bridge must be equipped with a
routing capability. When a bridge receives a frame, it must decide whether or not
to forward it. If the bridge is attached to two or more networks, then it must decide
whether or not to forward the frame and, if so, on which LAN the frame should be
transmitted.
The routing decision may not always be a simple one. Figure 11.8 also shows
that there are two routes between LAN A and LAN E. Such redundancy provides
for higher overall Internet availability and creates the possibility for load balancing.
In this case, if station 1 transmits a frame on LAN A intended for station 5 on LAN E,
then either bridge 101 or bridge 107 could forward the frame. It would appear preferable
for bridge 107 to forward the frame, since it will involve only one hop, whereas if
the frame travels through bridge 101, it must suffer two hops. Another consideration
is that there may be changes in the configuration. For example, bridge 107 may fail,
in which case subsequent frames from station 1 to station 5 should go through bridge
101. So we can say that the routing capability must take into account the topology of
the internet configuration and may need to be dynamically altered.

## Slide 22: Fixed Routing
Simplest and most common strategy
Suitable for small internets and internets that are relatively stable
A fixed route is selected for each pair of LANs
    Usually least hop route
  Only change when topology changes
  Widely used but limited flexibility
Notes: A variety of routing strategies have been proposed and implemented in recent
years. The simplest and most common strategy is fixed routing . This strategy is suitable
for small internets and for internets that are relatively stable. In addition, two
groups within the IEEE 802 committee have developed specifications for routing
strategies. The IEEE 802.1 group has issued a standard for routing based on the use
of a spanning tree algorithm. The token ring committee, IEEE 802.5, has issued its
own specification, referred to as source routing . In the remainder of this section, we
look at fixed routing and the spanning tree algorithm, which is the most commonly
used bridge routing algorithm.
For fixed routing, a route is selected for each source–destination pair of LANs
in the configuration. If alternate routes are available between two LANs, then typically
the route with the least number of hops is selected. The routes are fixed, or at
least only change when there is a change in the topology of the internet.
The strategy for developing a fixed routing configuration for bridges is similar
to that employed in a packet-switching network. A central routing matrix is created,
to be stored perhaps at a network control center. The matrix shows, for each
source–destination pair of LANs, the identity of the first bridge on the route.
Once the directories have been established, routing is a simple matter.
A bridge copies each incoming frame on each of its LANs. If the destination MAC
address corresponds to an entry in its routing table, the frame is retransmitted on
the appropriate LAN.
The fixed routing strategy is widely used in commercially available products.
It requires that a network manager manually load the data into the routing tables.
It has the advantage of simplicity and minimal processing requirements. However,
in a complex internet, in which bridges may be dynamically added and in which failures
must be allowed for, this strategy is too limited.

## Slide 23: Spanning Tree
Bridge automatically develops routing table
Automatically updates routing table in response to changing topology
Algorithm consists of three mechanisms:
Frame forwarding
Address learning
Loop resolution
Notes: The spanning tree approach is a mechanism in which bridges automatically develop
a routing table and update that table in response to changing topology. The algorithm
consists of three mechanisms: frame forwarding, address learning, and loop
resolution.

## Slide 24: Frame Forwarding
Maintain forwarding database for each port attached to a LAN
For a frame arriving on port X:
Search forwarding database to see if MAC address is listed for any port except port X
If destination MAC address is not found, forward frame out all ports except the one from which it was received
If the destination address is in the forwarding database for some port y, check port y for blocking or forwarding state
If port y is not blocked, transmit frame through port y onto the LAN to which that port attaches
Notes: In this scheme, a bridge maintains a forwarding database for
each port attached to a LAN. The database indicates the station addresses for which
frames should be forwarded through that port. We can interpret this in the following
fashion. For each port, a list of stations is maintained. A station is on the list
if it is on the “same side” of the bridge as the port. For example, for bridge 102 of
Figure 11.8, stations on LANs C, F, and G are on the same side of the bridge as
the LAN C port, and stations on LANs A, B, D, and E are on the same side of the
bridge as the LAN A port. When a frame is received on any port, the bridge must
decide whether that frame is to be forwarded through the bridge and out through
one of the bridge’s other ports. Suppose that a bridge receives a MAC frame on
port x .
The following rules are applied:
1. Search the forwarding database to determine if the MAC address is listed for
any port except port x .
2. If the destination MAC address is not found, forward frame out all ports
except the one from which it was received. This is part of the learning process
described subsequently.
3. If the destination address is in the forwarding database for some port y, then
determine whether port y is in a blocking or forwarding state. For reasons
explained later, a port may sometimes be blocked, which prevents it from
receiving or transmitting frames.
4. If port y is not blocked, transmit the frame through port y onto the LAN to
which that port attaches.

## Slide 25: Address Learning
Can preload forwarding database
When frame arrives at port X, it has come from the LAN attached to port X
Use source address to update forwarding database for port X to include that address
Have a timer on each entry in database
If timer expires, entry is removed
Each time frame arrives, source address checked against forwarding database
  If present timer is reset and direction recorded
  If not present entry is created and timer set
Notes: The preceding scheme assumes that the bridge is already equipped with a forwarding database that indicates the direction, from the bridge, of each destination station. This information can be preloaded into the bridge, as in fixed routing. However, an effective automatic mechanism for learning the direction of each station is desirable. A simple scheme for acquiring this information is based on the use of the source address field in each MAC frame.
The strategy is this. When a frame arrives on a particular port, it clearly has come from the direction of the incoming LAN. The source address field of the frame indicates the source station. Thus, a bridge can update its forwarding database for that port on the basis of the source address field of each incoming frame. To allow for changes in topology, each element in the database is equipped with a timer. When a new element is added to the database, its timer is set. If the timer expires, then the element is eliminated from the database, since the corresponding direction information may no longer be valid. Each time a frame is received, its source address is checked against the database. If the element is already in the database, the entry is updated (the direction may have changed) and the timer is reset. If the element is not in the database, a new entry is created, with its own timer.

## Slide 26: Spanning Tree Algorithm
Address learning works for tree layout if there are no alternate routes in the network
  Alternate route means there is a closed loop
For any connected graph there is a spanning tree maintaining connectivity with no closed loops
Algorithm must be dynamic
IEEE 802.1 Spanning Tree Algorithm:
Each bridge assigned unique identifier
Cost assigned to each bridge port
Exchange information between bridges to find spanning tree
Automatically updated whenever topology changes
Notes: The spanning tree algorithm developed by IEEE 802.1, as the name suggests,
is able to develop such a spanning tree. All that is required is that each bridge be
assigned a unique identifier and that costs be assigned to each bridge port. In the
absence of any special considerations, all costs could be set equal; this produces a
minimum-hop tree. The algorithm involves a brief exchange of messages among
all of the bridges to discover the minimum-cost spanning tree. Whenever there is a
change in topology, the bridges automatically recalculate the spanning tree.
For more information on the spanning tree algorithm, see Appendix J.

## Slide 27
Notes: To see the problem created by a closed loop, consider Figure 11.09. At time t0, station A transmits a frame addressed to station B. The frame is captured by both bridges. Each bridge updates its database to indicate that station A is in the direction of LAN X, and retransmits the frame on LAN Y. Say that bridge a retransmits at time t1 and bridge b a short time later t2. Thus B will receive two copies of the frame. Furthermore, each bridge will receive the other's transmission on LAN Y. Note that each transmission is a frame with a source address of A and a destination address of B. Thus each bridge will update its database to indicate that station A is in the direction of LAN Y. Neither bridge is now capable of forwarding a frame addressed to station A.
To overcome this problem, a simple result from graph theory is used: For any
connected graph, consisting of nodes and edges connecting pairs of nodes, there is
a spanning tree of edges that maintains the connectivity of the graph but contains
no closed loops. In terms of internets, each LAN corresponds to a graph node, and
each bridge corresponds to a graph edge. Thus, in Figure 11.8, the removal of one
(and only one) of bridges 107, 101, and 104 results in a spanning tree. What is desired
is to develop a simple algorithm by which the bridges of the internet can exchange
sufficient information to automatically (without user intervention) derive a spanning
tree. The algorithm must be dynamic. That is, when a topology change occurs,
the bridges must be able to discover this fact and automatically derive a new spanning
tree.
The spanning tree algorithm developed by IEEE 802.1, as the name suggests,
is able to develop such a spanning tree. All that is required is that each bridge be
assigned a unique identifier and that costs be assigned to each bridge port. In the
absence of any special considerations, all costs could be set equal; this produces a
minimum-hop tree. The algorithm involves a brief exchange of messages among
all of the bridges to discover the minimum-cost spanning tree. Whenever there is a
change in topology, the bridges automatically recalculate the spanning tree.
For more information on the spanning tree algorithm, see Appendix J.

## Slide 28: Hubs
Active central element of star layout
Each station connected to hub by two lines
Hub acts as a repeater
Length of a line is limited to about 100m
Optical fiber may be used to about 500m
Physically a star, logically a bus
Transmission from any one station is received by all other stations
If two stations transmit at the same time there will be a collision
Notes: In recent years, there has been a proliferation of types of devices for interconnecting
LANs that goes beyond the bridges discussed in Section 11.3 and the routers
discussed in Part Five. These devices can conveniently be grouped into the categories
of hubs and switches.
Earlier, we used the term hub in reference to a star-topology LAN. The hub is the
active central element of the star layout. Each station is connected to the hub by two
lines (transmit and receive). The hub acts as a repeater: When a single station transmits,
the hub repeats the signal on the outgoing line to each station. Ordinarily, the
line consists of two unshielded twisted pairs. Because of the high data rate and the
poor transmission qualities of unshielded twisted pair, the length of a line is limited
to about 100 m. As an alternative, an optical fiber link may be used. In this case, the
maximum length is about 500 m.
Note that although this scheme is physically a star, it is logically a bus: A transmission
from any one station is received by all other stations, and if two stations
transmit at the same time there will be a collision.

## Slide 29
Notes: In recent years, a new device, the layer 2 switch, has replaced the hub in popularity, particularly for high-speed LANs. The layer 2 switch is also sometimes referred to as a switching hub.
To clarify the distinction between hubs and switches, Figure 11.11a shows a
typical bus layout of a traditional 10-Mbps LAN. A bus is installed that is laid out so
that all the devices to be attached are in reasonable proximity to a point on the bus.
In the figure, station B is transmitting. This transmission goes from B, across the
lead from B to the bus, along the bus in both directions, and along the access lines of
each of the other attached stations. In this configuration, all the stations must share
the total capacity of the bus, which is 10 Mbps.
A hub, often in a building wiring closet, uses a star wiring arrangement to
attach stations to the hub. In this arrangement, a transmission from any one station
is received by the hub and retransmitted on all of the outgoing lines. Therefore,
to avoid collision, only one station can transmit at a time. Again, the total capacity
of the LAN is 10 Mbps. The hub has several advantages over the simple bus
arrangement. It exploits standard building wiring practices in the layout of cable.
In addition, the hub can be configured to recognize a malfunctioning station that is
jamming the network and to cut that station out of the network. Figure 11.11b illustrates
the operation of a hub. Here again, station B is transmitting. This transmission
goes from B, across the transmit line from B to the hub, and from the hub along the
receive lines of each of the other attached stations.
We can achieve greater performance with a layer 2 switch. In this case, the
central hub acts as a switch, much as a packet switch or circuit switch. With a layer 2
switch, an incoming frame from a particular station is switched to the appropriate
output line to be delivered to the intended destination. At the same time, other
unused lines can be used for switching other traffic. Figure 11.11c shows an example
in which B is transmitting a frame to A and at the same time C is transmitting
a frame to D. So, in this example, the current throughput on the LAN is 20 Mbps,
although each individual device is limited to 10 Mbps.

## Slide 30: Layer 2 Switch Benefits
No change is required to the software or hardware of the attached devices to convert a bus LAN or a hub LAN to a switched LAN
Have dedicated capacity equal to original LAN
  Assuming switch has sufficient capacity to keep up with all devices
Scales easily
  Additional devices attached to switch by increasing capacity of layer 2
Notes: The layer 2 switch has several attractive features:
1. No change is required to the software or hardware of the attached devices to convert a bus LAN or a hub LAN to a switched LAN. In the case of an Ethernet LAN, each attached device continues to use the Ethernet medium access control protocol to access the LAN. From the point of view of the attached devices, nothing has changed in the access logic.
2. Each attached device has a dedicated capacity equal to that of the entire original LAN, assuming that the layer 2 switch has sufficient capacity to keep up with all attached devices. For example, in Figure 11.11c, if the layer 2 switch can sustain a throughput of 20 Mbps, each attached device appears to have a dedicated capacity for either input or output of 10 Mbps.
3. The layer 2 switch scales easily. Additional devices can be attached to the layer 2 switch by increasing the capacity of the layer 2 switch correspondingly.

## Slide 31: Types of Layer 2 Switches
Store-and-forward switch
  Accepts frame on input line, buffers briefly, routes to appropriate output line
  See delay between sender and receiver
  Boosts overall integrity
Cut-through switch
  Use destination address at beginning of frame
  Switch begins repeating frame onto output line as soon as destination address is recognized
  Yields highest possible throughput
  Risk of propagating bad frames
Notes: Two types of layer 2 switches are available as commercial products:
Store-and-forward switch: The layer 2 switch accepts a frame on an input line, buffers it briefly, and then routes it to the appropriate output line.
Cut-through switch: The layer 2 switch takes advantage of the fact that the destination address appears at the beginning of the MAC (medium access control) frame. The layer 2 switch begins repeating the incoming frame onto the appropriate output line as soon as the layer 2 switch recognizes the destination address.
The cut-through switch yields the highest possible throughput but at some risk of propagating bad frames, because the switch is not able to check the CRC prior to retransmission. The store-and-forward switch involves a delay between sender and receiver but boosts the overall integrity of the network.

## Slide 32: Layer 2 Switch vs. Bridge
Differences between switches and bridges:
Layer 2 switch can be viewed as full-duplex hub
Incorporates logic to function as multiport bridge
New installations typically include layer 2 switches with bridge functionality rather than bridges
Bridge
Frame handling done in software
Analyzes and forwards one frame at a time
Uses store-and-forward operation
Switch
Performs frame forwarding in hardware
Can handle multiple frames at a time
Can have cut-through operation
Notes: A layer 2 switch can be viewed as a full-duplex version of the hub. It can also incorporate logic that allows it to function as a multiport bridge. The following are differences between layer 2 switches and bridges:
Bridge frame handling is done in software. A layer 2 switch performs the address recognition and frame forwarding functions in hardware.
A bridge can typically only analyze and forward one frame at a time, whereas a layer 2 switch has multiple parallel data paths and can handle multiple frames at a time.
A bridge uses store-and-forward operation. With a layer 2 switch, it is possible to have cut-through instead of store-and-forward operation.
Because a layer 2 switch has higher performance and can incorporate the functions of a bridge, the bridge has suffered commercially. New installations typically include layer 2 switches with bridge functionality rather than bridges.

## Slide 33
Notes: Figure 11.12 shows a relatively common type of hierarchical LAN configuration. In
this example, the devices on the LAN are organized into four groups, each served
by a LAN switch. The three lower groups might correspond to different departments,
which are physically separated, and the upper group could correspond to a
centralized server farm that is used by all the departments.
Let us consider the transmission of a single MAC frame from workstation X.
Suppose the destination MAC address in the frame (see Figure 11.5) is workstation
Y. This frame is transmitted from X to the local switch, which then directs the
frame along the link to Y. If X transmits a frame addressed to Z or W, then its local
switch routes the MAC frame through the appropriate switches to the intended
destination. All these are examples of unicast addressing , in which the destination
address in the MAC frame designates a unique destination. A MAC frame may also
contain a broadcast address , in which case the destination MAC address indicates
that all devices on the LAN should receive a copy of the frame. Thus, if X transmits a
frame with a broadcast destination address, all of the devices on all of the switches in
Figure 11.12 receive a copy of the frame. The total collection of devices that receive
broadcast frames from each other is referred to as a broadcast domain .
In many situations, a broadcast frame is used for a purpose, such as network
management or the transmission of some type of alert, that has a relatively local
significance. Thus, in Figure 11.12, if a broadcast frame has information that is only
useful to a particular department, then transmission capacity is wasted on the other
portions of the LAN and on the other switches.

## Slide 34
Notes: One simple approach to improving efficiency is to physically partition the
LAN into separate broadcast domains, as shown in Figure 11.13. We now have four
separate LANs connected by a router. In this case, an IP packet from X intended
for Z is handled as follows. The IP layer at X determines that the next hop to the
destination is via router V. This information is handed down to X’s MAC layer,
which prepares a MAC frame with a destination MAC address of router V. When
V receives the frame, it strips off the MAC header, determines the destination, and
encapsulates the IP packet in a MAC frame with a destination MAC address of Z.
This frame is then sent to the appropriate Ethernet switch for delivery.
The drawback to this approach is that the traffic pattern may not correspond to
the physical distribution of devices. For example, some departmental workstations
may generate a lot of traffic with one of the central servers. Further, as the networks
expand, more routers are needed to separate users into broadcast domains and provide
connectivity among broadcast domains. Routers introduce more latency than
switches because the router must process more of the packet to determine destinations
and route the data to the appropriate end node.

## Slide 35
Notes: A more effective alternative is the creation of virtual LANs (VLANs). In essence,
a VLAN is a logical subgroup within a LAN that is created by software rather than
by physically moving and separating devices. It combines user stations and network
devices into a single broadcast domain regardless of the physical LAN segment
they are attached to and allows traffic to flow more efficiently within populations of
mutual interest. The VLAN logic is implemented in LAN switches and functions at
the MAC layer. Because the objective is to isolate traffic within the VLAN, in order
to link from one VLAN to another, a router is required. Routers can be implemented
as separate devices, so that traffic from one VLAN to another is directed
to a router, or the router logic can be implemented as part of the LAN switch, as
shown in Figure 11.14.
VLANs provide the ability for any organization to be physically dispersed
throughout the company while maintaining its group identity. For example, accounting
personnel can be located on the shop floor, in the research and development
center, in the cash disbursement office, and in the corporate offices while all members
reside on the same virtual network, sharing traffic only with each other.
In Figure 11.14, five VLANs are defined. A transmission from workstation
X to server Z is within the same VLAN, so it is efficiently switched at the MAC
level. A broadcast MAC frame from X is transmitted to all devices in all portions of
the same VLAN. But a transmission from X to printer Y goes from one VLAN to
another. Accordingly, router logic at the IP level is required to move the IP packet
from X to Y. In Figure 11.14, that logic is integrated into the switch, so that the switch
determines whether or not the incoming MAC frame is destined for another device
on the same VLAN. If not, the switch routes the enclosed IP packet at the IP level.

## Slide 36: Defining VLANs
Broadcast domain consisting of a group of end stations not limited by physical location and communicate as if they were on a common LAN
Membership by:
  Port group
  MAC address
  Protocol information
Notes: A VLAN is a broadcast domain consisting of a group of end stations, perhaps on multiple physical LAN segments, that are not constrained by their physical location and can communicate as if they were on a common LAN. Some means is therefore needed for defining VLAN membership. A number of different approaches have been used for defining membership, including the following:
Membership by port group: Each switch in the LAN configuration contains two types of ports: a trunk port, which connects two switches, and an end port, which connects the switch to an end system. A VLAN can be defined by assigning each end port to a specific VLAN. This approach has the advantage that it is relatively easy to configure. The principle disadvantage is that the network manager must reconfigure VLAN membership when an end system moves from one port to another.
Membership by MAC address: Since MAC-layer addresses are hard-wired into the workstation’s network interface card (NIC), VLANs based on MAC addresses enable network managers to move a workstation to a different physical location on the network and have that workstation automatically retain its VLAN membership. The main problem with this method is that VLAN membership must be assigned initially. In networks with thousands of users, this is no easy task. Also, in environments where notebook PCs are used, the MAC address is associated with the docking station and not with the notebook PC. Consequently, when a notebook PC is moved to a different docking station, its VLAN membership must be reconfigured.
Membership based on protocol information: VLAN membership can be assigned based on IP address, transport protocol information, or even higher-layer protocol information. This is a quite flexible approach, but it does require switches to examine portions of the MAC frame above the MAC layer, which may have a performance impact.

## Slide 37: Defining VLANs
A VLAN is a broadcast domain consisting of a group of end stations that are not constrained by their physical location and can communicate as if they were on a common LAN
Defining membership
Membership by port group
Each switch in the LAN configuration contains two types of ports: a trunk port, which connects two switches; and an end port, which connects the switch to an end system
A VLAN can be defined by assigning each port to a specific VLAN
Has the advantage that it is relatively easy to configure
Principle disadvantage is that the network manager must reconfigure VLAN membership when an end system moves from one port to another
Membership by MAC address
VLANs based on MAC addresses enable network managers to move a workstation to a different physical location on the network and have that workstation automatically retain its VLAN membership
The main problem with this method is that VLAN membership must be assigned initially
Membership based on protocol information
VLAN membership can be assigned based on IP address, transport protocol information, or higher-layer protocol information
A flexible approach, but requires switches to examine portions of the MAC frame above the MAC layer, which may have a performance impact
Notes: A VLAN is a broadcast domain consisting of a group of end stations, perhaps on
multiple physical LAN segments, that are not constrained by their physical location
and can communicate as if they were on a common LAN. Some means is therefore
needed for defining VLAN membership. A number of different approaches have been
used for defining membership, including the following:
■ Membership by port group : Each switch in the LAN configuration contains
two types of ports: a trunk port, which connects two switches; and an end
port, which connects the switch to an end system. A VLAN can be defined by
assigning each end port to a specific VLAN. This approach has the advantage
that it is relatively easy to configure. The principle disadvantage is that the
network manager must reconfigure VLAN membership when an end system
moves from one port to another.
■ Membership by MAC address: Because MAC layer addresses are hardwired
into the workstation’s network interface card (NIC), VLANs based on
MAC addresses enable network managers to move a workstation to a different
physical location on the network and have that workstation automatically
retain its VLAN membership. The main problem with this method is that
VLAN membership must be assigned initially. In networks with thousands
of users, this is no easy task. Also, in environments where notebook PCs are
used, the MAC address is associated with the docking station and not with
the notebook PC. Consequently, when a notebook PC is moved to a different
docking station, its VLAN membership must be reconfigured.
■ Membership based on protocol information : VLAN membership
can be assigned based on IP address, transport protocol information, or even
higher-layer protocol information. This is a quite flexible approach, but it does
require switches to examine portions of the MAC frame above the MAC layer,
which may have a performance impact.

## Slide 38: Communicating VLAN Membership
Switches need to know VLAN membership
Configure information manually
Network management signaling protocol
Frame tagging (IEEE802.1Q)
Notes: Switches must have a way of understanding VLAN membership (that is, which stations belong to which VLAN) when network traffic arrives from other switches; otherwise, VLANs would be limited to a single switch. One possibility is to configure the information manually or with some type of network management signaling protocol, so that switches can associate incoming frames with the appropriate VLAN.
A more common approach is frame tagging, in which a header is typically inserted into each frame on interswitch trunks to uniquely identify to which VLAN a particular MAC-layer frame belongs. The IEEE 802 committee has developed a standard for frame tagging, IEEE 802.1Q, which we examine in the next chapter.

## Slide 39: Communicating VLAN Membership
Switches must have a way of understanding VLAN membership when network traffic arrives from other switches
One possibility is to configure the information manually or with some type of network management signaling protocol
A more common approach is frame tagging, in which a header is typically inserted into each frame on the interswitch trunks to uniquely identify to which VLAN a particular MAC-layer frame belongs
The IEEE 802 committee has developed a standard for frame tagging, IEEE 802.1Q
Notes: Switches must have a way of understanding VLAN membership (that is, which
stations belong to which VLAN) when network traffic arrives from other switches;
otherwise, VLANs would be limited to a single switch. One possibility is to configure
the information manually or with some type of network management signaling
protocol, so that switches can associate incoming frames with the appropriate VLAN.
A more common approach is frame tagging, in which a header is typically inserted
into each frame on interswitch trunks to uniquely identify to which VLAN a particular
MAC-layer frame belongs. The IEEE 802 committee has developed a standard for
frame tagging, IEEE 802.1Q , which we examine next.

## Slide 40
Notes: The IEEE 802.1Q standard, last updated in 2014, defines the operation of VLAN
bridges and switches that permits the definition, operation, and administration of
VLAN topologies within a bridged/switched LAN infrastructure. In this section, we
concentrate on the application of this standard to 802.3 LANs.
Recall that a VLAN is an administratively configured broadcast domain, consisting
of a subset of end stations attached to a LAN. A VLAN is not limited to one switch
but can span multiple interconnected switches. In that case, traffic between switches
must indicate VLAN membership. This is accomplished in 802.1Q by inserting a tag
with a VLAN identifier (VID) with a value in the range from 1 to 4094. Each VLAN
in a LAN configuration is assigned a globally unique VID. By assigning the same
VID to end systems on many switches, one or more VLAN broadcast domains can be
extended across a large network.
Figure 9.4 shows the position and content of the 802.1 tag, referred to as Tag Control
Information (TCI). The presence of the two-octet TCI field is indicated by inserting
a Length/Type field in the 802.3 MAC frame with a value of 8100 hex. The TCI
consists of three subfields, as described in the list that follows.
■ User priority (3 bits): The priority level for this frame.
■ Canonical format indicator (1 bit): Is always set to 0 for Ethernet
switches. CFI is used for compatibility between Ethernet type networks and
Token Ring type networks. If a frame received at an Ethernet port has a CFI
set to 1, that frame should not be forwarded as it is to an untagged port.
■ VLAN identifier (12 bits): The identification of the VLAN. Of the 4096 possible
VIDs, a VID of 0 is used to identify that the TCI contains only a priority
value, and 4095 (0xFFF) is reserved, so the maximum possible number of
VLAN configurations is 4094.

## Slide 41
Notes: Figure 9.5 illustrates a LAN configuration that includes three switches that implement
802.1Q and one “legacy” switch that does not. In this case, all the end systems of the
legacy device must belong to the same VLAN. The MAC frames that traverse trunks
between VLAN-aware switches include the 802.1Q TCI tag. This tag is stripped off
before a frame is forwarded to a legacy switch. For end systems connected to a VLANaware
switch, the MAC frame may or may not include the TCI tag, depending on the
implementation. The important point is that the TCI tag is used between VLAN-aware
switches so that appropriate routing and frame handling can be performed.

## Slide 42
Notes: The original 802.1Q specification allowed for a single VLAN tag field to be inserted
into an Ethernet MAC frame. More recent versions of the standard allow for the
insertion of two VLAN tag fields, allowing the definition of multiple sub-VLANs
within a single VLAN. This additional flexibility might be useful in some complex
configurations.
For example, a single VLAN level suffices for an Ethernet configuration entirely
on a single premises. However, it is not uncommon for an enterprise to make use
of a network service provider to interconnect multiple LAN locations, and to use
metropolitan area Ethernet links to connect to the provider. Multiple customers of
the service provider may wish to use the 802.1Q tagging facility across the service
provider network (SPN).
One possible approach is for the customer’s VLANs to be visible to the service
provider. In that case, the service provider could support a total of only 4094 VLANs
for all its customers. Instead, the service provider inserts a second VLAN tag into
Ethernet frames. For example, consider two customers with multiple sites, both of
which use the same SPN (see part a of Figure 9.6). Customer A has configured VLANs
1 to 100 at their sites, and similarly Customer B has configured VLANs 1 to 50 at their
sites. The tagged data frames belonging to the customers must be kept separate while
they traverse the service provider’s network. The customer’s data frame can be identified
and kept separate by associating another VLAN for that customer’s traffic. This
results in the tagged customer data frame being tagged again with a VLAN tag, when
it traverses the SPN (see part b of Figure 9.6). The additional tag is removed at the
edge of the SPN when the data enters the customer’s network again. Packed VLAN
tagging is known as VLAN stacking or as Q-in-Q.

## Slide 43: Summary
Bus and tree topologies and transmission media
  Topologies
  Choice of topology
  Choice of transmission medium
LAN protocol architecture
  IEEE 802 reference model
  Logical link control
  Medium access control
Hubs and switches
  Hubs
  Layer 2 switches
Bridges
  Functions of a bridge
  Bridge protocol architecture
  Fixed routing
  The spanning tree approach
Virtual LANs
  The use of virtual LANs
  Defining VLANs
  Communicating VLAN membership
Notes: Chapter 11 summary.