## Slide 1: Data and Computer Communications
Tenth Edition
by William Stallings
Notes: “Data and Computer Communications”, 10/e, by William Stallings, Chapter 15 “Transport Protocols”.

## Slide 2: Transport Protocols
Chapter 15
Notes: We begin this chapter by examining the protocol mechanisms required
to provide these services. We find that most of the complexity relates to reliable
connection-oriented services. As might be expected, the less the network
service provides, the more the transport protocol must do. The remainder
of the chapter looks at two widely used transport protocols: Transmission
Control Protocol (TCP) and User Datagram Protocol (UDP).
Refer to Figure 2.8 to see the position within the TCP/IP suite of the
protocols discussed in this chapter.

## Slide 3: Connection-Oriented Transport Mechanisms
Two basic types of transport service:
Connection-oriented
Establishment, maintenance and termination of a logical connection between TS users
Has a wide variety of applications
Most common
Implies service is reliable
Connectionless or datagram service
Notes: Two basic types of transport service are possible: connection oriented and connectionless or datagram service. A connection-oriented service provides for the establishment, maintenance, and termination of a logical connection between TS users. This has, so far, been the most common type of protocol service available and has a wide variety of applications. The connection-oriented service generally implies that the service is reliable. This section looks at the transport protocol mechanisms needed to support the connection-oriented service.
A full-feature connection-oriented transport protocol, such as TCP, is very complex. For purposes of clarity we present the transport protocol mechanisms in an evolutionary fashion. We begin with a network service that makes life easy for the transport protocol, by guaranteeing the delivery of all transport data units in order and defining the required mechanisms. Then we will look at the transport protocol mechanisms required to cope with an unreliable network service. All of this discussion applies in general to transport-level protocols. In Section 15.2, we apply the concepts developed in this section to describe TCP.

## Slide 4: Reliable Sequencing Network Service
Issues:
Addressing
Multiplexing
Flow control
Connection establishment/termination
Notes: Let us assume that the network service accepts messages of arbitrary length and, with virtually 100% reliability, delivers them in sequence to the destination. Examples of such networks:
A highly reliable packet-switching network with an X.25 interface
A frame relay network using the LAPF control protocol
An IEEE 802.3 LAN using the connection-oriented LLC service
In all of these cases, the transport protocol is used as an end-to-end protocol between two systems attached to the same network, rather than across an internet.
The assumption of a reliable sequencing networking service allows the use of a quite simple transport protocol. Four issues need to be addressed:
Addressing
Multiplexing
Flow control
Connection establishment/termination

## Slide 5: Addressing
Transport protocol must be able to derive the following information from the TS user address:
  User identification
  Transport entity identification
  Host address
  Network number
Notes: The issue concerned with addressing is simply this: a user of a given transport entity wishes either to establish a connection with or make a data transfer to a user of some other transport entity using the same transport protocol. The target user needs to be specified by all of the following:
User identification
Transport entity identification
Host address
Network number
The transport protocol must be able to derive the information listed above from the TS user address. Typically, the user address is specified as (Host, Port). The Port variable represents a particular TS user at the specified host. Generally, there will be a single transport entity at each host, so a transport entity identification is not needed. If more than one transport entity is present, there is usually only one of each type. In this latter case, the address should include a designation of the type of transport protocol (e.g., TCP, UDP). In the case of a single network, Host identifies an attached network device. In the case of an internet, Host is a global internet address. In TCP, the combination of port and host is referred to as a socket.
Because routing is not a concern of the transport layer, it simply passes the Host portion of the address down to the network service. Port is included in a transport header, to be used at the destination by the destination transport protocol entity.
One question remains to be addressed: How does the initiating TS user know the address of the destination TS user? Two static and two dynamic strategies suggest themselves:
The TS user knows the address it wishes to use ahead of time. This is basically a system configuration function. For example, a process may be running that is only of concern to a limited number of TS users, such as a process that collects statistics on performance. From time to time, a central network management routine connects to the process to obtain the statistics. These processes generally are not, and should not be, well known and accessible to all.
Some commonly used services are assigned "well-known addresses." Examples include the server side of FTP, SMTP, and some other standard protocols.
A name server is provided. The TS user requests a service by some generic or global name. The request is sent to the name server, which does a directory lookup and returns an address. The transport entity then proceeds with the connection. This service is useful for commonly used applications that change location from time to time. For example, a data entry process may be moved from one host to another on a local network to balance load.
In some cases, the target user is to be a process that is spawned at request time. The initiating user can send a process request to a well-known address. The user at that address is a privileged system process that will spawn the new process and return an address. For example, a programmer has developed a private application (e.g., a simulation program) that will execute on a remote server but be invoked from a local workstation. A request can be issued to a remote job-management process that spawns the simulation process.

## Slide 6: Multiplexing
Multiple users employ the same transport protocol and are distinguished by port numbers or service access points
Downward multiplexing
Splitting of a single connection among multiple lower-level connections
Multiplexing of multiple connections on a single lower-level connection
Upward multiplexing
Notes: With respect to the interface between the transport protocol and higher-level protocols, the transport protocol performs a multiplexing/demultiplexing function. That is, multiple users employ the same transport protocol and are distinguished by port numbers or service access points.
The transport entity may also perform a multiplexing function with respect to the network services that it uses. Recall that we defined upward multiplexing as the multiplexing of multiple connections on a single lower-level connection, and downward multiplexing as the splitting of a single connection among multiple lower-level connections.
Consider, for example, a transport entity making use of a connection-oriented
network service. Why should the transport entity employ upward multiplexing?
One reason would be if the network provider determines what it charges in part
on the number of connections, because each network-layer connection consumes
some node buffer resources. Thus, if a network-layer connection provides sufficient
throughput for multiple TS users, upward multiplexing is indicated.
On the other hand, downward multiplexing or splitting might be used to
improve throughput. For example, the network layer connection may have a small
sequence number space. A larger sequence space might be needed for high-speed,
high-delay networks. Of course, throughput can only be increased so far. If there
is a single host-node link over which all logical network connections are multiplexed,
the throughput of a transport connection cannot exceed the data rate of
that link.

## Slide 7: Flow Control
Complex at the transport layer:
  Considerable delay in the communication of flow control information
  Amount of the transmission delay may be highly variable, making it difficult to effectively use a timeout mechanism for retransmission of lost data
Reasons for control:
User of the receiving transport entity cannot keep up with the flow
Receiving transport entity itself cannot keep up with the flow of segments
Notes: Whereas flow control is a relatively simple mechanism at the link layer, it is a rather complex mechanism at the transport layer, for two main reasons:
The transmission delay between transport entities is generally long compared to actual transmission time. This means that there is a considerable delay in the communication of flow control information.
Because the transport layer operates over a network or internet, the amount of the transmission delay may be highly variable. This makes it difficult to effectively use a timeout mechanism for retransmission of lost data.
In general, there are two reasons why one transport entity would want to restrain the rate of segment transmission over a connection from another transport entity:
The user of the receiving transport entity cannot keep up with the flow of data.
The receiving transport entity itself cannot keep up with the flow of segments.
How do such problems manifest themselves? Presumably a transport entity has a certain amount of buffer space. Incoming segments are added to the buffer. Each buffered segment is processed (i.e., the transport header is examined) and the data are sent to the TS user. Either of the two problems just mentioned will cause the buffer to fill up. Thus, the transport entity needs to take steps to stop or slow the flow of segments to prevent buffer overflow. This requirement is difficult to fulfill because of the annoying time gap between sender and receiver. We return to this point subsequently.

## Slide 8: Alternatives to Flow Control Requirements
Do nothing
Segments that overflow the buffer are discarded
Sending transport entity will retransmit
Refuse to accept further segments from the network service
Relies on network service to do the work
Use a fixed sliding window protocol
With a reliable network service this works quite well
Use a credit scheme
A more effective scheme to use with an unreliable network service
Receiving transport entity can:
Notes: First, we present four ways of coping with the flow control requirement. The receiving transport entity can
1. Do nothing.
2. Refuse to accept further segments from the network service.
3. Use a fixed sliding-window protocol.
4. Use a credit scheme.
Alternative 1 means that the segments that overflow the buffer are discarded. The sending transport entity, failing to get an acknowledgment, will retransmit. This is a shame, because the advantage of a reliable network is that one never has to retransmit. Furthermore, the effect of this maneuver is to exacerbate the problem. The sender has increased its output to include new segments plus retransmitted old segments.
The second alternative is a backpressure mechanism that relies on the network service to do the work. When a buffer of a transport entity is full, it refuses additional data from the network service. This triggers flow control procedures within the network that throttle the network service at the sending end. This service, in turn, refuses additional segments from its transport entity. It should be clear that this mechanism is clumsy and coarse grained. For example, if multiple transport connections are multiplexed on a single network connection (virtual circuit), flow control is exercised only on the aggregate of all transport connections.
The third alternative is already familiar to you from our discussions of link layer protocols in Chapter 7. The key ingredients, recall, are
The use of sequence numbers on data units
The use of a window of fixed size
The use of acknowledgments to advance the window
With a reliable network service, the sliding-window technique would work quite well. For example, consider a protocol with a window size of 7. When the sender receives an acknowledgment to a particular segment, it is automatically authorized to send the succeeding seven segments (of course, some may already have been sent). When the receiver's buffer capacity gets down to seven segments, it can withhold acknowledgment of incoming segments to avoid overflow. The sending transport entity can send at most seven additional segments and then must stop. Because the underlying network service is reliable, the sender will not time out and retransmit. Thus, at some point, a sending transport entity may have a number of segments outstanding for which no acknowledgment has been received. Because we are dealing with a reliable network, the sending transport entity can assume that the segments will get through and that the lack of acknowledgment is a flow control tactic. This tactic would not work well in an unreliable network, because the sending transport entity would not know whether the lack of acknowledgment is due to flow control or a lost segment.
The fourth alternative, a credit scheme, provides the receiver with a greater degree of control over data flow. Although it is not strictly necessary with a reliable network service, a credit scheme should result in a smoother traffic flow. Further, it is a more effective scheme with an unreliable network service, as we shall see.
The credit scheme decouples acknowledgment from flow control. In fixed sliding-window protocols, such as X.25 and HDLC, the two are synonymous. In a credit scheme, a segment may be acknowledged without granting new credit, and vice versa. For the credit scheme, each individual octet of data that is transmitted is considered to have a unique sequence number. In addition to data, each transmitted segment includes in its header three fields related to flow control: sequence number (SN), acknowledgment number (AN), and window (W). When a transport entity sends a segment, it includes the sequence number of the first octet in the segment data field. Implicitly, the remaining data octets are numbered sequentially following the first data octet. A transport entity acknowledges an incoming segment with a return segment that includes (AN = i, W = j), with the following interpretation:
All octets through sequence number SN = i – 1 are acknowledged; the next expected octet has sequence number i.
Permission is granted to send an additional window of W = j octets of data; that is, the j octets corresponding to sequence numbers i through i + j – 1.

## Slide 9
Notes: Figure 15.1 illustrates the mechanism (compare Figure 7.4). For simplicity, we show data flow in one direction only and assume that 200 octets of data are sent in each segment. Initially, through the connection establishment process, the sending and receiving sequence numbers are synchronized and A is granted an initial credit allocation of 1400 octets, beginning with octet number 1001. The first segment transmitted by A contains data octets numbered 1001 through 1200. After sending 600 octets in three segments, A has shrunk its window to a size of 800 octets (numbers 1601 through 2400). After B receives these three segments, 600 octets out of its original 1400 octets of credit are accounted for, and 800 octets of credit are outstanding. Now suppose that, at this point, B is capable of absorbing 1000 octets of incoming data on this connection. Accordingly, B acknowledges receipt of all octets through 1600 and issues a credit of 1000 octets. This means that A can send octets 1601 through 2600 (5 segments). However, by the time that B's message has arrived at A, A has already sent two segments, containing octets 1601 through 2000 (which was permissible under the initial allocation). Thus, A's remaining credit upon receipt of B's credit allocation is only 600 octets (3 segments). As the exchange proceeds, A advances the trailing edge of its window each time that it transmits and advances the leading edge only when it is granted credit.

## Slide 10: Connection Establishment and Termination
Serves three main purposes:
  Allows each end to assure that the other exists
  Allows exchange or negotiation of optional parameters
  Triggers allocation of transport entity resources
  Is by mutual agreement
Notes: Even with a reliable network service, there is a need for connection establishment and termination procedures to support connection-oriented service. Connection establishment serves three main purposes:
It allows each end to assure that the other exists.
It allows exchange or negotiation of optional parameters (e.g., maximum segment size, maximum window size, quality of service).
It triggers allocation of transport entity resources (e.g., buffer space, entry in connection table).

## Slide 11
Notes: Connection establishment is by mutual agreement and can be accomplished by a simple set of user commands and control segments, as shown in the state diagram of Figure 15.3. To begin, a TS user is in an CLOSED state (i.e., it has no open transport connection). The TS user can signal to the local TCP entity that it will passively wait for a request with a Passive Open command. A server program, such as time-sharing or a file transfer application, might do this. The TS user may change its mind by sending a Close command. After the Passive Open command is issued, the transport entity creates a connection object of some sort (i.e., a table entry) that is in the LISTEN state.
From the CLOSED state, a TS user may open a connection by issuing an Active Open command, which instructs the transport entity to attempt connection establishment with a designated remote TS user, which triggers the transport entity to send a SYN (for synchronize) segment. This segment is carried to the receiving transport entity and interpreted as a request for connection to a particular port. If the destination transport entity is in the LISTEN state for that port, then a connection is established by the following actions by the receiving transport entity:
Signal the local TS user that a connection is open.
Send a SYN as confirmation to the remote transport entity.
Put the connection object in an ESTAB (established) state.
When the responding SYN is received by the initiating transport entity, it too can move the connection to an ESTAB state. The connection is prematurely aborted if either TS user issues a Close command.

## Slide 12
Notes: Figure 15.4 shows the robustness of this protocol. Either side can initiate a connection. Further, if both sides initiate the connection at about the same time, it is established without confusion. This is because the SYN segment functions both as a connection request and a connection acknowledgment.
The reader may ask what happens if a SYN comes in while the requested TS user is idle (not listening). Three courses may be followed:
The transport entity can reject the request by sending a RST (reset) segment back to the other transport entity.
The request can be queued until the local TS user issues a matching Open.
The transport entity can interrupt or otherwise signal the local TS user to notify it of a pending request.
Note that if the third mechanism is used, a Passive Open command is not strictly necessary but may be replaced by an Accept command, which is a signal from the user to the transport entity that it accepts the request for connection.
Connection termination is handled similarly. Either side, or both sides, may initiate a close. The connection is closed by mutual agreement. This strategy allows for either abrupt or graceful termination. With abrupt termination, data in transit may be lost; a graceful termination prevents either side from closing the connection until all data have been delivered. To achieve the latter, a connection in the FIN WAIT state must continue to accept data segments until a FIN (finish) segment is received.
Figure 15.3 defines the procedure for graceful termination. First, consider the side that initiates the termination procedure:
In response to a TS user's Close primitive, a transport entity sends a FIN segment to the other side of the connection, requesting termination.
Having sent the FIN, the transport entity places the connection in the FIN WAIT state. In this state, the transport entity must continue to accept data from the other side and deliver that data to its user.
3. When a FIN is received in response, the transport entity informs its user and closes the connection.
From the point of view of the side that does not initiate a termination,
1. When a FIN segment is received, the transport entity informs its user of the termination request and places the connection in the CLOSE WAIT state. In this state, the transport entity must continue to accept data from its user and transmit it in data segments to the other side.
2. When the user issues a Close primitive, the transport entity sends a responding FIN segment to the other side and closes the connection.
This procedure ensures that both sides have received all outstanding data and that both sides agree to connection termination before actual termination.

## Slide 13: Unreliable Network Service
  Segments are occasionally lost and may arrive out of sequence due to variable transit delays
Examples:
Internetwork using IP
IEEE 802.3 LAN using the unacknowledged connectionless LLC service
Notes: A more difficult case for a transport protocol is that of an unreliable network service. Examples of such networks:
An internetwork using IP
A frame relay network using only the LAPF core protocol
An IEEE 802.3 LAN using the unacknowledged connectionless LLC service
The problem is not just that segments are occasionally lost, but that segments may arrive out of sequence due to variable transit delays. As we shall see, elaborate machinery is required to cope with these two interrelated network deficiencies. We shall also see that a discouraging pattern emerges. The combination of unreliability and nonsequencing creates problems with every mechanism we have discussed so far. Generally, the solution to each problem raises new problems. Although there are problems to be overcome for protocols at all levels, it seems that there are more difficulties with a reliable connection-oriented transport protocol than any other sort of protocol.

## Slide 14: Issues to Address
Ordered delivery
Retransmission strategy
Duplicate detection
Flow control
Connection establishment
Connection termination
Failure recovery
Notes: In the remainder of this section, unless otherwise noted, the mechanisms discussed are those used by TCP. Seven issues need to be addressed:
Ordered delivery
Retransmission strategy
Duplicate detection
Flow control
Connection establishment
Connection termination
Failure recovery

## Slide 15: Ordered Delivery
With an unreliable network service it is possible that segments may arrive out of order
Solution to this problem is to number segments sequentially
  TCP uses scheme where each data octet is implicitly numbered
Notes: With an unreliable network service, it is possible that segments,
even if they are all delivered, may arrive out of order. The required solution
to this problem is to number segments sequentially. We have seen that for data
link control protocols, such as HDLC, each data unit (frame, packet) is numbered
sequentially with each successive sequence number being one more than the previous
sequence number. This scheme is used in some transport protocols, such as the
ISO transport protocols. However, TCP uses a somewhat different scheme in which
each data octet that is transmitted is implicitly numbered. Thus, the first segment
may have a sequence number of 1. If that segment has 200 octets of data, then the
second segment would have the sequence number 201, and so on. For simplicity in
the discussions of this section, we will continue to assume that each successive segment’s
sequence number is 200 more than that of the previous segment; that is, each
segment contains exactly 200 octets of data.

## Slide 16: Retransmission Strategy
Events necessitating retransmission:
Sending transport does not know transmission was unsuccessful
Receiver acknowledges successful receipt by returning a segment containing an acknowledgment number
Cont.
Segment may be damaged in transit but still arrives at its destination
Segment fails to arrive
Notes: Two events necessitate the retransmission of a segment. First, a segment may be damaged in transit but nevertheless arrive at its destination. If a checksum is included with the segment, the receiving transport entity can detect the error and discard the segment. The second contingency is that a segment fails to arrive. In either case, the sending transport entity does not know that the segment transmission was unsuccessful. To cover this contingency, a positive acknowledgment scheme is used: The receiver must acknowledge each successfully received segment by returning a segment containing an acknowledgment number. For efficiency, we do not require one acknowledgment per segment. Rather, a cumulative acknowledgment can be used, as we have seen many times in this book. Thus, the receiver may receive segments numbered 1, 201, and 401, but only send AN = 601 back. The sender must interpret AN = 601 to mean that the segment with SN = 401 and all previous segments have been successfully received.

## Slide 17: Retransmission Strategy
No acknowledgment will be issued if a segment does not arrive successfully
  Resulting in a retransmit
A timer needs to be associated with each segment as it is sent
If timer expires before acknowledgment is received, sender must retransmit
Notes: If a segment does not arrive successfully, no acknowledgment will be issued and a retransmission is in order. To cope with this situation, there must be a timer associated with each segment as it is sent. If the timer expires before the segment is acknowledged, the sender must retransmit.
So the addition of a timer solves that problem. Next problem: At what value should the timer be set? Two strategies suggest themselves. A fixed timer value could be used, based on an understanding of the network's typical behavior. This suffers from an inability to respond to changing network conditions. If the value is too small, there will be many unnecessary retransmissions, wasting network capacity. If the value is too large, the protocol will be sluggish in responding to a lost segment. The timer should be set at a value a bit longer than the round trip time (send segment, receive ACK). Of course, this delay is variable even under constant network load. Worse, the statistics of the delay will vary with changing network conditions.
An adaptive scheme has its own problems. Suppose that the transport entity keeps track of the time taken to acknowledge data segments and sets its retransmission timer based on the average of the observed delays. This value cannot be trusted for three reasons:
The peer transport entity may not acknowledge a segment immediately. Recall that we gave it the privilege of cumulative acknowledgments.
If a segment has been retransmitted, the sender cannot know whether the received acknowledgment is a response to the initial transmission or the retransmission.
Network conditions may change suddenly.
Each of these problems is a cause for some further tweaking of the transport algorithm, but the problem admits of no complete solution. There will always be some uncertainty concerning the best value for the retransmission timer. We return to this issue in Section 15.3.

## Slide 18: Duplicate Detection
Receiver must be able to recognize duplicates
Segment sequence numbers help
Complications arise if:
  A duplicate is received prior to the close of the connection
    Sender must not get confused if it receives multiple acknowledgments to the same segment
    Sequence number space must be long enough
  A duplicate is received after the close of the connection
Notes: If a segment is lost and then retransmitted, no confusion will result. If, however, one or more segments in sequence are successfully delivered, but the corresponding ACK is lost, then the sending transport entity will time out and one or more segments will be retransmitted. If these retransmitted segments arrive successfully, they will be duplicates of previously received segments. Thus, the receiver must be able to recognize duplicates. The fact that each segment carries a sequence number helps, but, nevertheless, duplicate detection and handling is not simple. There are two cases:
A duplicate is received prior to the close of the connection.
A duplicate is received after the close of the connection.
The second case is discussed in the subsection on connection establishment. We deal with the first case here.
Notice that we say "a" duplicate rather than "the" duplicate. From the sender's point of view, the retransmitted segment is the duplicate. However, the retransmitted segment may arrive before the original segment, in which case the receiver views the original segment as the duplicate. In any case, two tactics are needed to cope with a duplicate received prior to the close of a connection:
The receiver must assume that its acknowledgment was lost and therefore must acknowledge the duplicate. Consequently, the sender must not get confused if it receives multiple acknowledgments to the same segment.
The sequence number space must be long enough so as not to "cycle" in less than the maximum possible segment lifetime (time it takes segment to transit network).

## Slide 19
Notes: Figure 15.5 illustrates the reason for the latter requirement. In this example, the sequence space is of length 1600; that is, after SN = 1600, the sequence numbers cycle back and begin with SN = 1. For simplicity, we assume the receiving transport entity maintains a credit window size of 600. Suppose that A has transmitted data segments with SN = 1, 201, and 401. B has received the two segments with SN = 201 and SN = 401, but the segment with SN = 1 is delayed in transit. Thus, B does not send any acknowledgments. Eventually, A times out and retransmits segment SN = 1. When the duplicate segment SN = 1 arrives, B acknowledges 1, 201, and 401 with AN = 601. Meanwhile, A has timed out again and retransmits SN = 201, which B acknowledges with another AN = 601. Things now seem to have sorted themselves out and data transfer continues. When the sequence space is exhausted, A cycles back to SN = 1 and continues. Alas, the old segment SN = 1 makes a belated appearance and is accepted by B before the new segment SN = 1 arrives. When the new segment SN = 1 does arrive, it is treated as a duplicate and discarded.
It should be clear that the untimely emergence of the old segment would have caused no difficulty if the sequence numbers had not yet wrapped around. The larger the sequence number space (number of bits used to represent the sequence number), the longer the wraparound is avoided. How big must the sequence space be? This depends on, among other things, whether the network enforces a maximum packet lifetime, and the rate at which segments are being transmitted. Fortunately, each addition of a single bit to the sequence number field doubles the sequence space, so it is rather easy to select a safe size.

## Slide 20: Flow Control
Future acknowledgments will resynchronize the protocol if an ACK/CREDIT segment is lost
If no new acknowledgments are forthcoming the sender times out and retransmits a data segment which triggers a new acknowledgment
Notes: The credit allocation flow control mechanism described earlier is quite robust in the face of an unreliable network service and requires little enhancement. As was mentioned, a segment containing (AN = i, W = j) acknowledges all octets through number i – 1 and grants credit for an additional j octets beginning with octet i. The credit allocation mechanism is quite flexible. For example, suppose that the last octet of data received by B was octet number i – 1 and that the last segment issued by B was (AN = i, W = j). Then
To increase credit to an amount k (k > j) when no additional data have arrived, B issues (AN = i, W = k).
To acknowledge an incoming segment containing m octets of data (m < j) without granting additional credit, B issues (AN = i + m, W = j – m).
If an ACK/CREDIT segment is lost, little harm is done. Future acknowledgments will resynchronize the protocol. Further, if no new acknowledgments are forthcoming, the sender times out and retransmits a data segment, which triggers a new acknowledgment. However, it is still possible for deadlock to occur. Consider a situation in which B sends (AN = i, W = 0), temporarily closing the window. Subsequently, B sends (AN = i, W = j), but this segment is lost. A is awaiting the opportunity to send data and B thinks that it has granted that opportunity. To overcome this problem, a persist timer can be used. This timer is reset with each outgoing segment (all segments contain the AN and W fields). If the timer ever expires, the protocol entity is required to send a segment, even if it duplicates a previous one. This breaks the deadlock and also assures the other end that the protocol entity is still alive.

## Slide 21: Connection Establishment
Must take into account the unreliability of a network service
Three-way handshake
Notes: As with other protocol mechanisms, connection establishment must take into account the unreliability of a network service. Recall that a connection establishment calls for the exchange of SYNs, a procedure sometimes referred to as a two-way handshake. Suppose that A issues a SYN to B. It expects to get a SYN back, confirming the connection. Two things can go wrong: A's SYN can be lost or B's answering SYN can be lost. Both cases can be handled by use of a retransmit-SYN timer (Table 15.1). After A issues a SYN, it will reissue the SYN when the timer expires.
This gives rise, potentially, to duplicate SYNs. If A's initial SYN was lost, there are no duplicates. If B's response was lost, then B may receive two SYNs from A. Further, if B's response was not lost, but simply delayed, A may get two responding SYNs. All of this means that A and B must simply ignore duplicate SYNs once a connection is established.

## Slide 22
Notes: Figure 15.9 illustrates typical three-way handshake operations. In Figure 15.9a, transport entity A initiates the connection, with a SYN including the sending sequence number, i. The value i is referred to as the initial sequence number (ISN) and is associated with the SYN; the first data octet to be transmitted will have sequence number i + 1. The responding SYN acknowledges the ISN with (AN = i + 1) and includes its ISN. A acknowledges B's SYN/ACK in its first data segment, which begins with sequence number i + 1. Figure 15.9b shows a situation in which an old SYN i arrives at B after the close of the relevant connection. B assumes that this is a fresh request and responds with SYN j, AN = i + 1. When A receives this message, it realizes that it has not requested a connection and therefore sends an RST, AN = j. Note that the AN = j portion of the RST message is essential so that an old duplicate RST does not abort a legitimate connection establishment. Figure 15.9c shows a case in which an old SYN/ACK arrives in the middle of a new connection establishment. Because of the use of sequence numbers in the acknowledgments, this event causes no mischief.
For simplicity, the upper part of Figure 15.8 does not include transitions in which RST is sent. The basic rule is as follows: Send an RST if the connection state is not yet OPEN and an invalid ACK (one that does not reference something that was sent) is received. The reader should try various combinations of events to see that this connection establishment procedure works in spite of any combination of old and lost segments.

## Slide 23
Notes: The way out of this problem is for each side to acknowledge explicitly the other's SYN and sequence number. The procedure is known as a three-way handshake. The revised connection state diagram, which is the one employed by TCP, is shown in the upper part of Figure15.8. A new state (SYN RECEIVED) is added. In this state, the transport entity hesitates during connection opening to assure that the SYN segments sent by the two sides have both been acknowledged before the connection is declared established. In addition to the new state, there is a control segment (RST) to reset the other side when a duplicate SYN is detected.

## Slide 24
Notes: TCP uses only a single type of protocol data unit, called a TCP segment. The header is shown in Figure 15.10. Because one header must serve to perform all protocol mechanisms, it is rather large, with a minimum length of 20 octets. The fields are:
Source Port (16 bits): Source TCP user. Example values are Telnet = 23; TFTP = 69; HTTP = 80. A complete list is maintained at http://www.iana.org/assignments/port-numbers.
Destination Port (16 bits): Destination TCP user.
Sequence Number (32 bits): Sequence number of the first data octet in this segment except when the SYN flag is set. If SYN is set, this field contains the initial sequence number (ISN) and the first data octet in this segment has sequence number ISN + 1.
Acknowledgment Number (32 bits): Contains the sequence number of the next data octet that the TCP entity expects to receive.
Data Offset (4 bits): Number of 32-bit words in the header.
Reserved (4 bits): Reserved for future use.
Flags (8 bits): For each flag, if set to 1, the meaning is
CWR: congestion window reduced.
ECE: ECN-Echo; the CWR and ECE bits, defined in RFC 3168, are used for the explicit congestion notification function; a discussion of this function is beyond our scope.
URG: urgent pointer field significant.
ACK: acknowledgment field significant.
PSH: push function.
RST: reset the connection.
SYN: synchronize the sequence numbers.
FIN: no more data from sender.
Window (16 bits): Flow control credit allocation, in octets. Contains the number of data octets, beginning with the sequence number indicated in the acknowledgment field that the sender is willing to accept.
Checksum (16 bits): The ones complement of the ones complement sum of all the 16-bit words in the segment plus a pseudoheader, described subsequently.
Urgent Pointer (16 bits): This value, when added to the segment sequence number, contains the sequence number of the last octet in a sequence of urgent data. This allows the receiver to know how much urgent data is coming.
Options (Variable): An example is the option that specifies the maximum segment size that will be accepted.
The Sequence Number and Acknowledgment Number are bound to octets rather than to entire segments. For example, if a segment contains sequence number 1001 and includes 600 octets of data, the sequence number refers to the first octet in the data field; the next segment in logical order will have sequence number 1601. Thus, TCP is logically stream oriented: It accepts a stream of octets from the user, groups them into segments as it sees fit, and numbers each octet in the stream.
The Checksum field applies to the entire segment plus a pseudoheader prefixed to the header at the time of calculation (at both transmission and reception). The pseudoheader includes the following fields from the IP header: source and destination internet address and protocol, plus a segment length field. By including the pseudoheader, TCP protects itself from misdelivery by IP. That is, if IP delivers a packet to the wrong host, even if the packet contains no bit errors, the receiving TCP entity will detect the delivery error.
By comparing the TCP header to the TCP user interface defined in Tables 15.2 and 15.3, the reader may feel that some items are missing from the TCP header; that is indeed the case. TCP is intended to work with IP. Hence, some TCP user parameters are passed down by TCP to IP for inclusion in the IP header. The precedence parameter can be mapped into the DS (Differentiated Services) field, and the security parameter into the optional security field in the IP header.
It is worth observing that this TCP/IP linkage means that the required minimum overhead for every data unit is actually 40 octets.

## Slide 25: Table 15.4 TCP Service Parameters
(Table is on Page 490 in textbook)
Notes: Table 15.4 provides a brief definition of the parameters involved. The two passive open commands signal the TCP user's willingness to accept a connection request. The active open with data allows the user to begin transmitting data with the opening of the connection.

## Slide 26: TCP Mechanisms
Can be grouped into:
Connection establishment
Always uses a three-way handshake
Connection is determined by host and port
Data transfer
Viewed logically as consisting of a stream of octets
Flow control is exercised using credit allocation
Connection termination
Each TCP user must issue a CLOSE primitive
An abrupt termination occurs if the user issues an ABORT primitive
Notes: We can group TCP mechanisms into the categories of connection establishment, data transfer, and connection termination.
Connection establishment in TCP always uses a three-way handshake. When the SYN flag is set, the segment is essentially a request for connection and functions as explained in Section 15.1. To initiate a connection, an entity sends a SYN, SN = X, where X is the initial sequence number. The receiver responds with SYN, SN = Y, AN = X + 1 by setting both the SYN and ACK flags. Note that the acknowledgment indicates that the receiver is now expecting to receive a segment beginning with data octet X + 1, acknowledging the SYN, which occupies SN = X. Finally, the initiator responds with AN = Y + 1. If the two sides issue crossing SYNs, no problem results: Both sides respond with SYN/ACKs (Figure 15.4).
A connection is uniquely determined by the source and destination sockets (host, port). Thus, at any one time, there can only be a single TCP connection between a unique pair of ports. However, a given port can support multiple connections, each with a different partner port.
Although data are transferred in segments over a transport connection, data transfer is viewed logically as consisting of a stream of octets. Hence every octet is numbered, modulo 232. Each segment contains the sequence number of the first octet in the data field. Flow control is exercised using a credit allocation scheme in which the credit is a number of octets rather than a number of segments, as explained in Section 15.1.
Data are buffered by the transport entity on both transmission and reception. TCP normally exercises its own discretion as to when to construct a segment for transmission and when to release received data to the user. The PUSH flag is used to force the data so far accumulated to be sent by the transmitter and passed on by the receiver. This serves an end-of-block function.
The user may specify a block of data as urgent. TCP will designate the end of that block with an urgent pointer and send it out in the ordinary data stream. The receiving user is alerted that urgent data are being received.
If, during data exchange, a segment arrives that is apparently not meant for the current connection, the RST flag is set on an outgoing segment. Examples of this situation are delayed duplicate SYNs and an acknowledgment of data not yet sent.
The normal means of terminating a connection is a graceful close. Each TCP user must issue a CLOSE primitive. The transport entity sets the FIN bit on the last segment that it sends out, which also contains the last of the data to be sent on this connection.
An abrupt termination occurs if the user issues an ABORT primitive. In this case, the entity abandons all attempts to send or receive data and discards data in its transmission and reception buffers. An RST segment is sent to the other side.

## Slide 27: TCP Implementation Policy Options
Implementation opportunities:
Send policy
Deliver policy
Accept policy
Retransmit policy
Acknowledge policy
Notes: The TCP standard provides a precise specification of the protocol to be used between TCP entities. However, certain aspects of the protocol admit several possible implementation options. Although two implementations that choose alternative options will be interoperable, there may be performance implications. The design areas for which options are specified are the following:
Send policy
Deliver policy
Accept policy
Retransmit policy
Acknowledge policy

## Slide 28: Send Policy
In the absence of both pushed data and a closed transmission window a sending TCP entity is free to transmit data at its own convenience
TCP may construct a segment for each batch of data provided or it may wait until a certain amount of data accumulates before constructing and sending a segment
Infrequent and large transmissions have low overhead in terms of segment generation and processing
If transmissions are frequent and small, the system is providing quick response
Notes: In the absence of both pushed data and a closed transmission window (see Figure 15.2a), a sending TCP entity is free to transmit data at its own convenience, within its current credit allocation. As data are issued by the user, they are buffered in the transmit buffer. TCP may construct a segment for each batch of data provided by its user or it may wait until a certain amount of data accumulates before constructing and sending a segment. The actual policy will depend on performance considerations. If transmissions are infrequent and large, there is low overhead in terms of segment generation and processing. On the other hand, if transmissions are frequent and small, the system is providing quick response.

## Slide 29: Deliver Policy
In the absence of a Push, a receiving TCP entity is free to deliver data to the user at its own convenience
May deliver as each in-order segment is received, or may buffer data before delivery
If deliveries are infrequent and large, the user is not receiving data as promptly as may be desirable
If deliveries are frequent and small, there may be unnecessary processing, as well as operating system interrupts
Notes: In the absence of a Push, a receiving TCP entity is free to deliver data to the user at its own convenience. It may deliver data as each in-order segment is received, or it may buffer data from a number of segments in the receive buffer before delivery. The actual policy will depend on performance considerations. If deliveries are infrequent and large, the user is not receiving data as promptly as may be desirable. On the other hand, if deliveries are frequent and small, there may be unnecessary processing both in TCP and in the user software, as well as an unnecessary number of operating system interrupts.

## Slide 30: Accept Policy
If segments arrive out of order the receiving TCP entity has two options:
In-order
Accepts only segments that arrive in order; any segment that arrives out of order is discarded
Makes for simple implementation but places a burden on the networking facility
If a single segment is lost in transit, then all subsequent segments must be retransmitted
In-window
Accepts all segments that are within the receive window
Requires a more complex acceptance test and a more sophisticated data storage scheme
Notes: When all data segments arrive in order over a TCP connection, TCP places the data in a receive buffer for delivery to the user. It is possible, however, for segments to arrive out of order. In this case, the receiving TCP entity has two options:
In-order: Accept only segments that arrive in order; any segment that arrives out of order is discarded.
In-window: Accept all segments that are within the receive window (see Figure 15.2b).
The in-order policy makes for a simple implementation but places a burden on the networking facility, as the sending TCP must time out and retransmit segments that were successfully received but discarded because of misordering. Furthermore, if a single segment is lost in transit, then all subsequent segments must be retransmitted once the sending TCP times out on the lost segment.
The in-window policy may reduce transmissions but requires a more complex acceptance test and a more sophisticated data storage scheme to buffer and keep track of data accepted out of order.

## Slide 31: Retransmit Policy
Retransmission strategies:
First-only
Maintain one retransmission timer for entire queue
Efficient in terms of traffic generated
Can have considerable delays
Batch
Maintain one retransmission timer for entire queue
Reduces the likelihood of long delays
May result in unnecessary retransmissions
Individual
Maintain one timer for each segment in the queue
More complex implementation
Notes: TCP maintains a queue of segments that have been sent but not yet acknowledged. The TCP specification states that TCP will retransmit a segment if it fails to receive an acknowledgment within a given time. A TCP implementation may employ one of three retransmission strategies:
First-only: Maintain one retransmission timer for the entire queue. If an acknowledgment is received, remove the appropriate segment or segments from the queue and reset the timer. If the timer expires, retransmit the segment at the front of the queue and reset the timer.
Batch: Maintain one retransmission timer for the entire queue. if an acknowledgment is received, remove the appropriate segment or segments from the queue and reset the timer. If the timer expires, retransmit all segments in the queue and reset the timer.
Individual: Maintain one timer for each segment in the queue. If an acknowledgment is received, remove the appropriate segment or segments from the queue and destroy the corresponding timer or timers. If any timer expires, retransmit the corresponding segment individually and reset its timer.
The first-only policy is efficient in terms of traffic generated, because only lost segments (or segments whose ACK was lost) are retransmitted. Because the timer for the second segment in the queue is not set until the first segment is acknowledged, however, there can be considerable delays. The individual policy solves this problem at the expense of a more complex implementation. The batch policy also reduces the likelihood of long delays but may result in unnecessary retransmissions.
The actual effectiveness of the retransmit policy depends in part on the accept policy of the receiver. If the receiver is using an in-order accept policy, then it will discard segments received after a lost segment. This fits best with batch retransmission. If the receiver is using an in-window accept policy, then a first-only or individual retransmission policy is best. Of course, in a mixed network of computers, both accept policies may be in use.

## Slide 32: Acknowledge Policy
Timing of acknowledgment:
Immediate
Immediately transmit an empty segment containing the appropriate acknowledgement number
Simple and keeps the remote TCP fully informed
Limits unnecessary retransmissions
Results in extra segment transmissions
Can cause a further load on the network
Cumulative
Wait for an outbound segment with data on which to piggyback the acknowledgement
Typically used
Requires more processing at the receiving end and complicates the task of estimating round-trip time
Notes: When a data segment arrives that is in sequence, the receiving TCP entity has two options concerning the timing of acknowledgment:
Immediate: When data are accepted, immediately transmit an empty (no data) segment containing the appropriate acknowledgment number.
Cumulative: When data are accepted, record the need for acknowledgment, but wait for an outbound segment with data on which to piggyback the acknowledgment. To avoid long delay, set a persist timer (Table 15.1); if the timer expires before an acknowledgment is sent, transmit an empty segment containing the appropriate acknowledgment number.
The immediate policy is simple and keeps the remote TCP entity fully informed, which limits unnecessary retransmissions. However, this policy results in extra segment transmissions, namely, empty segments used only to ACK. Furthermore, the policy can cause a further load on the network. Consider that a TCP entity receives a segment and immediately sends an ACK. Then the data in the segment are released to the application, which expands the receive window, triggering another empty TCP segment to provide additional credit to the sending TCP entity.
Because of the potential overhead of the immediate policy, the cumulative policy is typically used. Recognize, however, that the use of this policy requires more processing at the receiving end and complicates the task of estimating round-trip time by the sending TCP entity.

## Slide 33: User Datagram Protocol (UDP)
Transport-level protocol that is commonly used as part of the TCP/IP protocol suite
RFC 768
Provides a connectionless service for application-level procedures
Unreliable service; delivery and duplicate protection are not guaranteed
Reduces overhead and may be adequate in many cases
Notes: In addition to TCP, there is one other transport-level protocol that is in common use
as part of the TCP/IP suite: the User Datagram Protocol (UDP), specified in RFC 768.
UDP provides a connectionless service for application-level procedures. Thus, UDP is
basically an unreliable service; delivery and duplicate protection are not guaranteed.
However, this does reduce the overhead of the protocol and may be adequate in many
cases.
The strengths of the connection-oriented approach are clear. It allows connection-
related features such as flow control, error control, and sequenced delivery.
Connectionless service, however, is more appropriate in some contexts. At lower layers
(internet, network), a connectionless service is more robust (e.g., see discussion
in Section 9.5). In addition, it represents a “least common denominator” of service
to be expected at higher layers. Further, even at transport and above there is justification
for a connectionless service. There are instances in which the overhead of
connection establishment and termination is unjustified or even counterproductive.
Examples include the following:
• Inward data collection: Involves the periodic active or passive sampling of
data sources, such as sensors, and automatic self-test reports from security
equipment or network components. In a real-time monitoring situation, the
loss of an occasional data unit would not cause distress, because the next
report should arrive shortly.
• Outward data dissemination: Includes broadcast messages to network users,
the announcement of a new node or the change of address of a service, and the
distribution of real-time clock values.
• Request-response: Applications in which a transaction service is provided
by a common server to a number of distributed TS users, and for which a
single request-response sequence is typical. Use of the service is regulated at
the application level, and lower-level connections are often unnecessary and
cumbersome.
• Real-time applications: Applications, such as voice and telemetry, that involve
a degree of redundancy and/or a real-time transmission requirement. These
must not have connection-oriented functions such as retransmission.
Thus, there is a place at the transport level for both a connection-oriented and
a connectionless type of service.

## Slide 34
Notes: UDP sits on top of IP. Because it is connectionless, UDP has very little to do. Essentially, it adds a port addressing capability to IP. This is best seen by examining the UDP header, shown in Figure 15.11. The header includes a source port and destination port. The Length field contains the length of the entire UDP segment, including header and data. The checksum is the same algorithm used for TCP and IP. For UDP, the checksum applies to the entire UDP segment plus a pseudoheader prefixed to the UDP header at the time of calculation and which is the same pseudoheader used for TCP. If an error is detected, the segment is discarded and no further action is taken.
The checksum field in UDP is optional. If it is not used, it is set to zero. However, it should be pointed out that the IP checksum applies only to the IP header and not to the data field, which in this case consists of the UDP header and the user data. Thus, if no checksum calculation is performed by UDP, then no check is made on the user data at either the transport or internet protocol layers.

## Slide 35: Summary
Connection-oriented transport protocol mechanisms
  Reliable sequencing network service
  Unreliable network service
UDP
TCP
  Services
  Header format
  Mechanisms
  Implementation policy options
Notes: Chapter 15 summary.

## Slide 36: Additional Slides

## Slide 37
Notes: Figure 15.2 shows the view of this mechanism from the sending and receiving sides (compare Figure 7.3). Typically, both sides take both views because data may be exchanged in both directions. Note that the receiver is not required to immediately acknowledge incoming segments but may wait and issue a cumulative acknowledgment for a number of segments.
The receiver needs to adopt some policy concerning the amount of data it permits the sender to transmit. The conservative approach is to only allow new segments up to the limit of available buffer space. If this policy were in effect in Figure 15.1, the first credit message implies that B has 1000 available octets in its buffer, and the second message that B has 1400 available octets.
A conservative flow control scheme may limit the throughput of the transport connection in long-delay situations. The receiver could potentially increase throughput by optimistically granting credit for space it does not have. For example, if a receiver's buffer is full but it anticipates that it can release space for 1000 octets within a round-trip propagation time, it could immediately send a credit of 1000. If the receiver can keep up with the sender, this scheme may increase throughput and can do no harm. If the sender is faster than the receiver, however, some segments may be discarded, necessitating a retransmission. Because retransmissions are not otherwise necessary with a reliable network service (in the absence of internet congestion), an optimistic flow control scheme will complicate the protocol.

## Slide 38: Table 15.1 Transport Protocol Timers
Notes: Incidentally, the retransmission timer is only one of a number of timers needed for proper functioning of a transport protocol. These are listed in Table 15.1, together with a brief explanation.

## Slide 39
Notes: There are other problems to contend with. Just as a delayed SYN or lost response can give rise to a duplicate SYN, a delayed data segment or lost acknowledgment can give rise to duplicate data segments, as we have seen in Figure15.5. Such a delayed or duplicated data segment can interfere with data transfer, as illustrated in Figure 15.6. Assume that with each new connection, each transport protocol entity begins numbering its data segments with sequence number 1. In the figure, a duplicate copy of segment SN = 401 from an old connection arrives during the lifetime of a new connection and is delivered to B before delivery of the legitimate data segment SN = 401. One way of attacking this problem is to start each new connection with a different sequence number that is far removed from the last sequence number of the most recent connection. For this purpose, the connection request is of the form SYN i+1, where i is the sequence number of the first data segment that will be sent on this connection.

## Slide 40
Notes: Now consider that a duplicate SYN i may survive past the termination of the connection. Figure 15.7 depicts the problem that may arise. An old SYN i arrives at B after the connection is terminated. B assumes that this is a fresh request and responds with SYN j, meaning that B accepts the connection request and will begin transmitting with SN = j+1. Meanwhile, A has decided to open a new connection with B and sends SYN k. B discards this as a duplicate. Now both sides have transmitted and subsequently received a SYN segment, and therefore think that a valid connection exists. However, when A initiates data transfer with a segment numbered k+1. B rejects the segment as being out of sequence.

## Slide 41: Connection Termination
Two-way handshake was found to be inadequate for an unreliable network service
Out of order segments could cause the FIN segment to arrive before the last data segment
    To avoid this problem the next sequence number after the last octet of data can be assigned to FIN
    Each side must explicitly acknowledge the FIN of the other using an ACK with the sequence number of the FIN to be acknowledged
Notes: The state diagram of Figure 15.3 defines the use of a simple two-way handshake for connection establishment, which was found to be unsatisfactory in the face of an unreliable network service. Similarly, the two-way handshake defined in that diagram for connection termination is inadequate for an unreliable network service. Misordering of segments could cause the following scenario. A transport entity in the CLOSE WAIT state sends its last data segment, followed by a FIN segment, but the FIN segment arrives at the other side before the last data segment. The receiving transport entity will accept that FIN, close the connection, and lose the last segment of data. To avoid this problem, a sequence number can be associated with the FIN, which can be assigned the next sequence number after the last octet of transmitted data. With this refinement, the receiving transport entity, upon receiving a FIN, will wait if necessary for the late-arriving data before closing the connection.
A more serious problem is the potential loss of segments and the potential presence of obsolete segments. Figure 15.8 shows that the termination procedure adopts a similar solution to that used for connection establishment. Each side must explicitly acknowledge the FIN of the other, using an ACK with the sequence number of the FIN to be acknowledged. For a graceful close, a transport entity requires the following:
It must send a FIN i and receive AN = i + 1.
It must receive a FIN j and send AN = j + 1.
It must wait an interval equal to twice the maximum expected segment lifetime.

## Slide 42: Failure Recovery
When the system that the transport entity is running on fails and subsequently restarts, the state information of all active connections is lost
  Affected connections become half open because the side that did not fail does not realize the problem
    Still active side of a half-open connection can close the connection using a keepalive timer
Cont…
Notes: When the system upon which a transport entity is running fails and subsequently restarts, the state information of all active connections is lost. The affected connections become half open because the side that did not fail does not yet realize the problem.
The still active side of a half-open connection can close the connection using a keepalive timer. This timer measures the time the transport machine will continue to await an acknowledgment (or other appropriate reply) of a transmitted segment after the segment has been retransmitted the maximum number of times. When the timer expires, the transport entity assumes that the other transport entity or the intervening network has failed, closes the connection, and signals an abnormal close to the TS user.

## Slide 43: Failure Recovery
    In the event that a transport entity fails and quickly restarts, half-open connections can be terminated more quickly by the the use of the RST segment
      Failed side returns an RST i to every segment i that it receives
      RST i must be checked for validity on the other side
          If valid an abnormal termination occurs
    There is still the chance that some user data will be lost or duplicated
Notes: In the event that a transport entity fails and quickly restarts, half-open connections can be terminated more quickly by the use of the RST segment. The failed side returns an RST i to every segment i that it receives. When the RST i reaches the other side, it must be checked for validity based on the sequence number i, because the RST could be in response to an old segment. If the reset is valid, the transport entity performs an abnormal termination.
These measures clean up the situation at the transport level. The decision as to whether to reopen the connection is up to the TS users. The problem is one of synchronization. At the time of failure, there may have been one or more outstanding segments in either direction. The TS user on the side that did not fail knows how much data it has received, but the other user may not, if state information were lost. Thus, there is the danger that some user data will be lost or duplicated.

## Slide 44: TCP Services
RFC 793
Defined in terms of primitives and parameters
TCP labels data as:
Data stream Push
Urgent data signaling
Notes: In this section we look at TCP (RFC 793), first at the service it provides to the TS user and then at the internal protocol details.
TCP is designed to provide reliable communication between pairs of processes (TCP users) across a variety of reliable and unreliable networks and internets. TCP provides two useful facilities for labeling data: push and urgent:
Data stream push: Ordinarily, TCP decides when sufficient data have accumulated to form a segment for transmission. The TCP user can require TCP to transmit all outstanding data up to and including that labeled with a push flag. On the receiving end, TCP will deliver these data to the user in the same manner. A user might request this if it has come to a logical break in the data.
Urgent data signaling: This provides a means of informing the destination TCP user that significant or "urgent" data is in the upcoming data stream. It is up to the destination user to determine appropriate action.
As with IP, the services provided by TCP are defined in terms of primitives and parameters. The services provided by TCP are considerably richer than those provided by IP, and hence the set of primitives and parameters is more complex.

## Slide 45: Table 15.2 TCP Service Request Primitives
(Table is on
page 488
in textbook)
Notes: Table 15.2 lists TCP service request primitives, which are issued by a TCP user to TCP

## Slide 46: Table 15.3 TCP Service Response Primitives
* = Not used for Unspecified Passive Open
(Table is on
page 489
in textbook)
Notes: Table 15.3 lists TCP service response primitives, which are issued by TCP to a local TCP user.