## Slide 1: Data and Computer Communications
Tenth Edition
by William Stallings
Notes: “Data and Computer Communications”, 10/e, by William Stallings, Chapter 19 “Routing”.

## Slide 2: Routing
Chapter 19
Notes: This chapter begins with a brief overview of issues involved in routing
design. Next, we look at the routing function in packet-switching networks. Then
we look at key routing algorithms for the Internet. Finally, the chapter examines
least-cost algorithms that are a central part of routing in switched networks.

## Slide 3: Routing in Packet Switching Networks
Key design issue for (packet) switched networks
Select route across network between end nodes
Characteristics required:
  Correctness
  Simplicity
  Robustness
  Stability
  Fairness
  Optimality
  Efficiency
Notes: The primary function of a packet-switching network is to accept packets from a
source station and deliver them to a destination station. To accomplish this, a path
or route through the network must be determined; generally, more than one route
is possible. Thus, a routing function must be performed. The requirements for this
function include the following:
• Correctness
• Simplicity
• Robustness
• Stability
• Fairness
• Optimality
• Efficiency
The first two items on the list, correctness and simplicity, are self-explanatory.
Robustness has to do with the ability of the network to deliver packets via some
route in the face of localized failures and overloads. Ideally, the network can react
to such contingencies without the loss of packets or the breaking of virtual circuits.
The designer who seeks robustness must cope with the competing requirement for
stability. Techniques that react to changing conditions have an unfortunate tendency
to either react too slowly to events or to experience unstable swings from one
extreme to another. For example, the network may react to congestion in one area
by shifting most of the load to a second area. Now the second area is overloaded and
the first is underutilized, causing a second shift. During these shifts, packets may
travel in loops through the network.
A trade-off also exists between fairness and optimality. Some performance
criteria may give higher priority to the exchange of packets between nearby stations
compared to an exchange between distant stations. This policy may maximize average
throughput but will appear unfair to the station that primarily needs to communicate
with distant stations.
Finally, any routing technique involves some processing overhead at each
node and often a transmission overhead as well, both of which impair network
efficiency. The penalty of such overhead needs to be less than the benefit accrued
based on some reasonable metric, such as increased robustness or fairness.

## Slide 4: Table 19.1 Elements of Routing Techniques for Packet-Switching Networks
Notes: With these requirements in mind, we are in a position to assess the various
design elements that contribute to a routing strategy. Table 19.1 lists these elements.
Some of these categories overlap or are dependent on one another. Nevertheless,
an examination of this list serves to clarify and organize routing concepts.

## Slide 5: Performance Criteria
Used for selection of route
Simplest is to choose “minimum hop”
Can be generalized as “least cost” routing
Because “least cost” is more flexible it is more common than “minimum hop”
Notes: The selection of a route is generally based on some performance
criterion. The simplest criterion is to choose the minimum-hop route
(one that passes through the least number of nodes) through the network. This
is an easily measured criterion and should minimize the consumption of network
resources. A generalization of the minimum-hop criterion is least-cost routing. In
this case, a cost is associated with each link, and, for any pair of attached stations,
the route through the network that accumulates the least cost is sought.

## Slide 6
Notes: Figure 19.1 illustrates a network in which the two arrowed lines between a pair of nodes represent a link between these nodes, and the corresponding numbers represent the current link cost in each direction. The shortest path (fewest hops) from node 1 to node 6 is 1-3-6 (cost = 5 + 5 = 10), but the least-cost path is 1-4-5-6 (cost = 1 + 1 + 2 = 4).
Costs are assigned to links to support one or more design objectives. For example, the cost could be inversely related to the data rate (i.e., the higher the data rate on a link, the lower the assigned cost of the link) or the current queuing delay on the link. In the first case, the least-cost route should provide the highest throughput. In the second case, the least-cost route should minimize delay.
In either the minimum-hop or least-cost approach, the algorithm for determining
the optimum route for any pair of stations is relatively straightforward, and
the processing time would be about the same for either computation. Because the
least-cost criterion is more flexible, this is more common than the minimum-hop
criterion.

## Slide 7: Decision Time and Place
Decision time
Packet or virtual circuit basis
Decision place
Distributed - made by each node
Fixed or dynamically changing
More complex, but more robust
Centralized – made by a designated node
Source – made by source station
Notes: Routing decisions are made on the basis of some performance criterion. Two key characteristics of the decision are the time and place that the decision is made.
Decision time is determined by whether the routing decision is made on a packet or virtual circuit basis. When the internal operation of the network is datagram, a routing decision is made individually for each packet. For internal virtual circuit operation, a routing decision is made at the time the virtual circuit is established. In the simplest case, all subsequent packets using that virtual circuit follow the same route. In more sophisticated network designs, the network may dynamically change the route assigned to a particular virtual circuit in response to changing conditions (e.g., overload or failure of a portion of the network).
The term decision place refers to which node or nodes in the network are responsible for the routing decision. Most common is distributed routing, in which each node has the responsibility of selecting an output link for routing packets as they arrive. For centralized routing, the decision is made by some designated node, such as a network control center. The danger of this latter approach is that the loss of the network control center may block operation of the network. The distributed approach is perhaps more complex but is also more robust. A third alternative, used in some networks, is source routing. In this case, the routing decision is actually made by the source station rather than by a network node and is then communicated to the network. This allows the user to dictate a route through the network that meets criteria local to that user.

## Slide 8: Network Information Source and Update Timing
Routing decisions usually based on knowledge of network, traffic load, and link cost
  Distributed routing
    Using local knowledge, information from adjacent nodes, information from all nodes on a potential route
  Central routing
    Collect information from all nodes
Issue of update timing
Depends on routing strategy
Fixed - never updated
Adaptive - regular updates
Notes: Most routing strategies require that decisions be based on knowledge of the topology of the network, traffic load, and link cost.
With distributed routing, in which the routing decision is made by each node, the individual node may make use of only local information, such as the cost of each outgoing link. Each node might also collect information from adjacent (directly connected) nodes, such as the amount of congestion experienced at that node. Finally, there are algorithms in common use that allow the node to gain information from all nodes on any potential route of interest. In the case of centralized routing, the central node typically makes use of information obtained from all nodes.
A related concept is that of information update timing, which is a function of both the information source and the routing strategy. Clearly, if no information is used (as in flooding), there is no information to update. If only local information is used, the update is essentially continuous. For all other information source categories (adjacent nodes, all nodes), update timing depends on the routing strategy. For a fixed strategy, the information is never updated. For an adaptive strategy, information is updated from time to time to enable the routing decision to adapt to changing conditions.
As you might expect, the more information available, and the more frequently it is updated, the more likely the network is to make good routing decisions. On the other hand, the transmission of that information consumes network resources.

## Slide 9: Routing Strategies - Fixed Routing
Use a single permanent route for each source to destination pair of nodes
Determined using a least cost algorithm
Route is fixed
  Until a change in network topology
  Based on expected traffic or capacity
Advantage is simplicity
Disadvantage is lack of flexibility
  Does not react to network failure or congestion
Notes: A large number of routing strategies have evolved for dealing with the routing requirements of packet-switching networks, we survey four key strategies: fixed, flooding, random, and adaptive.
For fixed routing, a single, permanent route is configured for each source-destination pair of nodes in the network. Either of the least-cost routing algorithms described in Section 19.3 could be used. The routes are fixed, or at least only change when there is a change in the topology of the network. Thus, the link costs used in designing routes cannot be based on any dynamic variable such as traffic. They could, however, be based on expected traffic or capacity.
With fixed routing, there is no difference between routing for datagrams and virtual circuits. All packets from a given source to a given destination follow the same route. The advantage of fixed routing is its simplicity, and it should work well in a reliable network with a stable load. Its disadvantage is its lack of flexibility. It does not react to network congestion or failures.

## Slide 10
Notes: Figure 19.2 suggests how fixed routing might be implemented. A central routing matrix is created, to be stored perhaps at a network control center. The matrix shows, for each source-destination pair of nodes, the identity of the next node on the route. Note that it is not necessary to store the complete route for each possible pair of nodes. Rather, it is sufficient to know, for each pair of nodes, the identity of the first node on the route. To see this, suppose that the least-cost route from X to Y begins with the X-A link. Call the remainder of the route R1; this is the part from A to Y. Define R2 as the least-cost route from A to Y. Now, if the cost of R1 is greater than that of R2, then the X-Y route can be improved by using R2 instead. If the cost of R1 is less than R2, then R2 is not the least-cost route from A to Y. Therefore, R1 = R2. Thus, at each point along a route, it is only necessary to know the identity of the next node, not the entire route. In our example, the route from node 1 to node 6 begins by going through node 4. Again consulting the matrix, the route from node 4 to node 6 goes through node 5. Finally, the route from node 5 to node 6 is a direct link to node 6. Thus, the complete route from node 1 to node 6 is 1-4-5-6.
From this overall matrix, routing tables can be developed and stored at each node. From the reasoning in the preceding paragraph, it follows that each node need only store a single column of the routing directory. The node's directory shows the next node to take for each destination.

## Slide 11: Routing Strategies - Adaptive Routing
Used by almost all packet switching networks
Routing decisions change as conditions on the network change due to failure or congestion
Requires information about network
Disadvantages:
Decisions more complex
Tradeoff between quality of network information and overhead
Reacting too quickly can cause oscillation
Reacting too slowly means information may be irrelevant
Notes: In virtually all packet-switching networks, some sort of adaptive routing technique is used. That is, the routing decisions that are made change as conditions on the network change. The principal conditions that influence routing decisions are:
• Failure: When a node or link fails, it can no longer be used as part of a route.
• Congestion: When a particular portion of the network is heavily congested, it is desirable to route packets around rather than through the area of congestion.
For adaptive routing to be possible, information about the state of the network must be exchanged among the nodes. There are several drawbacks associated with the use of adaptive routing, compared to fixed routing:
• The routing decision is more complex; therefore, the processing burden on network nodes increases.
• In most cases, adaptive strategies depend on status information that is collected at one place but used at another. There is a tradeoff here between the quality of the information and the amount of overhead. The more information that is exchanged, and the more frequently it is exchanged, the better will be the routing decisions that each node makes. On the other hand, this information is itself a load on the constituent networks, causing a performance degradation.
• An adaptive strategy may react too quickly, causing congestion-producing oscillation, or too slowly, being irrelevant.

## Slide 12: Adaptive Routing Advantages
Improved performance
Aid in congestion control
These benefits depend on the soundness of the design and nature of the load
Notes: Despite these real dangers, adaptive routing strategies are by far the most prevalent, for two reasons:
• An adaptive routing strategy can improve performance, as seen by the network user.
• An adaptive routing strategy can aid in congestion control, which is discussed in Chapter 20. Because an adaptive routing strategy tends to balance loads, it can delay the onset of severe congestion.
These benefits may or may not be realized, depending on the soundness of the design and the nature of the load. By and large, adaptive routing is an extraordinarily complex task to perform properly. As demonstration of this, most major packet-switching networks, such as ARPANET and its successors, and many commercial networks, have endured at least one major overhaul of their routing strategy.

## Slide 13: Classification of Adaptive Routing Strategies
A convenient way to classify is on the basis of information source
Local (isolated)
Route to outgoing link with shortest queue
Adjacent nodes
Takes advantage of delay and outage information
All nodes
Like adjacent
Can include bias for each destination
Rarely used - does not make use of available information
Distributed or centralized
Notes: A convenient way to classify adaptive routing strategies is on the basis of information source: local, adjacent nodes, all nodes. An example of an adaptive routing strategy that relies only on local information is one in which a node routes each packet to the outgoing link with the shortest queue length, Q. This would have the effect of balancing the load on outgoing links. However, some outgoing links may not be headed in the correct general direction. We can improve matters by also taking into account preferred direction, much as with random routing. In this case, each link emanating from the node would have a bias Bi, for each destination i, such that lower values of Bi indicate more preferred directions. For each incoming packet headed for node i, the node would choose the outgoing link that minimizes Q + Bi. Thus a node would tend to send packets in the right direction, with a concession made to current traffic delays.
Adaptive schemes based only on local information are rarely used because they do not exploit easily available information. Strategies based on information from adjacent nodes or all nodes are commonly found. Both take advantage of information that each node has about delays and outages that it experiences. Such adaptive strategies can be either distributed or centralized. In the distributed case, each node exchanges delay information with other nodes. Based on incoming information, a node tries to estimate the delay situation throughout the network, and applies a least-cost routing algorithm. In the centralized case, each node reports its link delay status to a central node, which designs routes based on this incoming information and sends the routing information back to the nodes.

## Slide 14: Internet Routing Protocols
Routers are responsible for receiving and forwarding packets through the interconnected set of networks
  Makes routing decisions based on knowledge of the topology and traffic/delay conditions of the internet
  Routers exchange routing information using a special routing protocol
  Two concepts in considering the routing function:
  Routing information
      Information about the topology and delays of the internet
  Routing algorithm
      The algorithm used to make a routing decision for a particular datagram, based on current routing information
Notes: The routers in an internet are responsible for receiving and forwarding packets
through the interconnected set of networks. Each router makes routing decision
based on knowledge of the topology and traffic/delay conditions of the internet.
In a simple internet, a fixed routing scheme is possible. In more complex internets,
a degree of dynamic cooperation is needed among the routers. In particular, the
router must avoid portions of the network that have failed and portions of the network
that are congested. To make such dynamic routing decisions, routers exchange
routing information using a special routing protocol for that purpose. Information is
needed about the status of the internet, in terms of which networks can be reached
by which routes, and the delay characteristics of various routes.
In considering the routing function, it is important to distinguish two concepts:
• Routing information: Information about the topology and delays of the
internet
• Routing algorithm: The algorithm used to make a routing decision for a particular
datagram, based on current routing information

## Slide 15: Autonomous Systems (AS)
Exhibits the following characteristics:
  Is a set of routers and networks managed by a single organization
  Consists of a group of routers exchanging information via a common routing protocol
  Except in times of failure, is connected (in a graph-theoretic sense); there is a path between any pair of nodes
Notes: To proceed with our discussion of routing protocols, we need to introduce the concept
of an autonomous system (AS) . An AS exhibits the following characteristics:
1. An AS is a set of routers and networks managed by a single organization.
2. An AS consists of a group of routers exchanging information via a common
routing protocol.
3. Except in times of failure, an AS is connected (in a graph-theoretic sense);
that is, there is a path between any pair of nodes.

## Slide 16: Interior Router Protocol (IRP)
A shared routing protocol which passes routing information between routers within an AS
Custom tailored to specific applications and requirements
Notes: A shared routing protocol, which we shall refer to as an interior router protocol
(IRP) , passes routing information between routers within an AS. The protocol used
within the AS does not need to be implemented outside of the system. This flexibility
allows IRPs to be custom tailored to specific applications and requirements.

## Slide 17
Notes: It may happen, however, that an internet will be constructed of more than one
AS. For example, all of the LANs at a site, such as an office complex or campus,
could be linked by routers to form an AS. This system might be linked through a
wide area network to other ASs. The situation is illustrated in Figure 19.9. In this
case, the routing algorithms and information in routing tables used by routers in different
ASs may differ. Nevertheless, the routers in one AS need at least a minimal
level of information concerning networks outside the system that can be reached.

## Slide 18: Exterior Router Protocol (ERP)
Protocol used to pass routing information between routers in different ASs
Will need to pass less information than an IRP for the following reason:
  If a datagram is to be transferred from a host in one AS to a host in another AS, a router in the first system need only determine the target AS and devise a route to get into that target system
  Once the datagram enters the target AS, the routers within that system can cooperate to deliver the datagram
  The ERP is not concerned with, and does not know about, the details of the route
Examples
Border Gateway Protocol (BGP)
Notes: We refer to the protocol used to pass routing information between routers in different
ASs as an exterior router protocol (ERP) .
We can expect that an ERP will need to pass less information than an IRP
for the following reason. If a datagram is to be transferred from a host in one AS
to a host in another AS, a router in the first system need only determine the target
AS and devise a route to get into that target system. Once the datagram enters the
target AS, the routers within that system can cooperate to deliver the datagram; the
ERP is not concerned with, and does not know about, the details of the route followed
within the target AS.
In the remainder of this section, we look at what are perhaps the most important
examples of these two types of routing protocols: Border Gateway Protocol
(BGP) and Open Shortest Path First (OSPF) Protocol. But first, it is useful to look
at a different way of characterizing routing protocols.

## Slide 19: Approaches to Routing
Internet routing protocols employ one of three approaches to gathering and using routing information:
  Distance-vector routing
  Link-state routing
  Path-vector routing
Notes: Internet routing protocols employ one of three approaches to gathering and using routing
information: distance-vector routing, link-state routing, and path-vector routing.

## Slide 20: Distance-Vector Routing
Requires that each node exchange information with its neighboring nodes
  Two nodes are said to be neighbors if they are both directly connected to the same network
Used in the first-generation routing algorithm for ARPANET
Each node maintains a vector of link costs for each directly attached network and distance and next-hop vectors for each destination
Routing Information Protocol (RIP) uses this approach
Notes: Distance-vector routing requires that each node (router or host that implements
the routing protocol) exchange information with its neighboring nodes.
Two nodes are said to be neighbors if they are both directly connected to the same
network. This approach is that used in the first-generation routing algorithm for
ARPANET, as described in Section 19.2. For this purpose, each node maintains a
vector of link costs for each directly attached network and distance and next-hop
vectors for each destination. The relatively simple Routing Information Protocol
(RIP) uses this approach.
Distance-vector routing requires the transmission of a considerable amount
of information by each router. Each router must send a distance vector to all of its
neighbors, and that vector contains the estimated path cost to all networks in the
configuration. Furthermore, when there is a significant change in a link cost or when
a link is unavailable, it may take a considerable amount of time for this information
to propagate through the internet.

## Slide 21: Link-State Routing
Designed to overcome the drawbacks of distance-vector routing
When a router is initialized, it determines the link cost on each of its network interfaces
The router then advertises this set of link costs to all other routers in the internet topology, not just neighboring routers
From then on, the router monitors its link costs
Whenever there is a significant change the router again advertises its set of link costs to all other routers in the configuration
The OSPF protocol is an example
The second-generation routing algorithm for ARPANET also uses this approach
Notes: Link-state routing is designed to overcome the drawbacks of distance-vector
routing. When a router is initialized, it determines the link cost on each of its network
interfaces. The router then advertises this set of link costs to all other routers in the
internet topology, not just neighboring routers. From then on, the router monitors
its link costs. Whenever there is a significant change (e.g., a link cost increases or
decreases substantially, a new link is created, or an existing link becomes unavailable),
the router again advertises its set of link costs to all other routers in the configuration.
Because each router receives the link costs of all routers in the configuration,
each router can construct the topology of the entire configuration and then calculate
the shortest path to each destination network. Having done this, the router can construct
its routing table, listing the first hop to each destination. Because the router
has a representation of the entire network, it does not use a distributed version of
a routing algorithm, as is done in distance-vector routing. Rather, the router can
use any routing algorithm to determine the shortest paths. In practice, Dijkstra’s
algorithm is used. The OSPF protocol is an example of a routing protocol that uses
link-state routing. The second-generation routing algorithm for ARPANET also
uses this approach.
Both link-state and distance-vector approaches have been used for interior
router protocols. Neither approach is effective for an exterior router protocol.

## Slide 22: Path-Vector Routing
Alternative to dispense with routing metrics and simply provide information about which networks can be reached by a given router and the ASs visited in order to reach the destination network by this route
Differs from a distance-vector algorithm in two respects:
  The path-vector approach does not include a distance or cost estimate
  Each block of routing information lists all of the ASs visited in order to reach the destination network by this route
Notes: An alternative, known as path-vector routing , is to dispense with routing
metrics and simply provide information about which networks can be reached
by a given router and the ASs that must be crossed to get there. The approach
differs from a distance-vector algorithm in two respects: First, the path-vector
approach does not include a distance or cost estimate. Second, each block of
routing information lists all of the ASs visited in order to reach the destination
network by this route.
Because a path vector lists the ASs that a datagram must traverse if it follows
this route, the path information enables a router to perform policy routing. That
is, a router may decide to avoid a particular path in order to avoid transiting a particular
AS. For example, information that is confidential may be limited to certain
kinds of ASs. Or a router may have information about the performance or quality
of the portion of the internet that is included in an AS that leads the router to avoid
that AS. Examples of performance or quality metrics include link speed, capacity,
tendency to become congested, and overall quality of operation. Another criterion
that could be used is minimizing the number of transit ASs.

## Slide 23: Border Gateway Protocol (BGP)
Was developed for use in conjunction with internets that employ the TCP/IP suite
Has become the preferred exterior router protocol for the Internet
Designed to allow routers in different autonomous systems to cooperate in the exchange of routing information
Protocol operates in terms of messages, which are sent over TCP connections
Current version is known as BGP-4 (RFC 4271)
Three functional procedures:
Neighbor acquisition
Neighbor reachability
Network reachability
Notes: BGP was developed for use in conjunction with internets that employ the TCP/IP
suite, although the concepts are applicable to any internet. BGP has become the
preferred exterior router protocol for the Internet.
BGP was designed to allow routers, called gateways in the standard,
in different autonomous systems (ASs) to cooperate in the exchange of routing
information. The protocol operates in terms of messages, which are sent over TCP
connections. The current version of BGP is known as BGP-4 (RFC 4271).

## Slide 24: Table 19.2 BGP-4 Messages
Notes: The repertoire of messages is summarized in Table 19.2.

## Slide 25: Neighbor Acquisition
Occurs when two neighboring routers in different autonomous systems agree to exchange routing information regularly
Two routers send Open messages to each other after a TCP connection is established
  If each router accepts the request, it returns a Keepalive message in response
Protocol does not address the issue of how one router knows the address or even the existence of another router nor how it decides that it needs to exchange routing information with that particular router
Notes: Two routers are considered to be neighbors if they are attached to the same
network. If the two routers are in different autonomous systems, they may wish
to exchange routing information. For this purpose, it is necessary first to perform
neighbor acquisition . In essence, neighbor acquisition occurs when two neighboring
routers in different autonomous systems agree to exchange routing information
regularly. A formal acquisition procedure is needed because one of the routers may
not wish to participate. For example, the router may be overburdened and does not
want to be responsible for traffic coming in from outside the system. In the neighbor
acquisition process, one router sends a request message to the other, which may
either accept or refuse the offer. The protocol does not address the issue of how
one router knows the address or even the existence of another router nor how it
decides that it needs to exchange routing information with that particular router.
These issues must be dealt with at configuration time or by active intervention of a
network manager.
To perform neighbor acquisition, two routers send Open messages to each
other after a TCP connection is established. If each router accepts the request, it
returns a Keepalive message in response.

## Slide 26: Open Shortest Path First (OSPF) Protocol
RFC 2328
Used as the interior router protocol in TCP/IP networks
Computes a route through the internet that incurs the least cost based on a user-configurable metric of cost
Is able to equalize loads over multiple equal-cost paths
Notes: The OSPF protocol (RFC 2328) is now widely used as the interior router protocol in
TCP/IP networks. OSPF computes a route through the internet that incurs the least
cost based on a user-configurable metric of cost. The user can configure the cost to
express a function of delay, data rate, dollar cost, or other factors. OSPF is able to
equalize loads over multiple equal-cost paths.
Each router maintains a database that reflects the known topology of the
autonomous system of which it is a part. The topology is expressed as a directed
graph. The graph consists of the following:
• Vertices, or nodes, of two types:
1. Router
2. Network, which is in turn of two types
a. transit, if it can carry data that neither originate nor terminate on an end
system attached to this network
stub, if it is not a transit network
• Edges are of two types:
1. Graph edges that connect two router vertices when the corresponding routers
are connected to each other by a direct point-to-point link
2. Graph edges that connect a router vertex to a network vertex when the
router is directly connected to the network

## Slide 27
Notes: Figure 19.11, based on one in RFC 2328, shows an example of an autonomous
System.

## Slide 28
Notes: Figure 19.12 is the resulting directed graph. The mapping is
straightforward:
• Two routers joined by a point-to-point link are represented in the graph as
being directly connected by a pair of edges, one in each direction (e.g., routers
6 and 10).
• When multiple routers are attached to a network (such as a LAN or packet-switching
network), the directed graph shows all routers bidirectionally
connected to the network vertex (e.g., routers 1, 2, 3, and 4 all connect to
network 3).
• If a single router is attached to a network, the network will appear in the graph
as a stub connection (e.g., network 7).
• An end system, called a host, can be directly connected to a router, in which
case it is depicted in the corresponding graph (e.g., host 1).
• If a router is connected to other autonomous systems, then the path cost
to each network in the other system must be obtained by some exterior
router protocol. Each such network is represented on the graph by a stub
and an edge to the router with the known path cost (e.g., networks 12
through 15).
A cost is associated with the output side of each router interface. This cost
is configurable by the system administrator. Arcs on the graph are labeled with
the cost of the corresponding router output interface. Arcs having no labeled cost
have a cost of 0. Note that arcs leading from networks to routers always have a
cost of 0.

## Slide 29: Table 19.3 Routing Table for R6
Notes: A database corresponding to the directed graph is maintained by each router.
It is pieced together from link-state messages from other routers in the internet.
Using Dijkstra’s algorithm (see Section 19.4), a router calculates the least-cost
path to all destination networks. The result for router 6 of Figure 19.11 is shown
as a tree in Figure 19.13, with R6 as the root of the tree. The tree gives the entire
route to any destination network or host. However, only the next hop to the destination
is used in the forwarding process. The resulting routing table for router 6
is shown in Table 19.3. The table includes entries for routers advertising external
routes (routers 5 and 7). For external networks whose identity is known, entries
are also provided.

## Slide 30: Dijkstra’s Algorithm
Finds shortest paths from given source nodes to all other nodes
Develop paths in order of increasing path length
Algorithm runs in stages
  Each time adding node with next shortest path
Algorithm terminates when all nodes have been added to T
Notes: Dijkstra's algorithm [DIJK59] can be stated as: Find the shortest paths from a given source node to all other nodes by developing the paths in order of increasing path length. The algorithm proceeds in stages. By the kth stage, the shortest paths to the k nodes closest to (least cost away from) the source node have been determined; these nodes are in a set T. At stage (k + 1), the node not in T that has the shortest path from the source node is added to T. As each node is added to T, its path from the source is defined.
The algorithm terminates when all nodes have been added to T. At termination, the value L(x) associated with each node x is the cost (length) of the least-cost path from s to x. In addition, T defines the least-cost path from s to each other node.

## Slide 31: Dijkstra’s Algorithm Method
Step 1 [Initialization]
T = {s} Set of nodes so far incorporated
L(n) = w(s, n) for n ≠ s
Step 2 [Get Next Node]
Find neighboring node not in T with least-cost path from s
Incorporate node into T
Also incorporate the edge that is incident on that node and a node in T that contributes to the path
Initial path costs to neighboring nodes are simply link costs
Step 3 [Update Least-Cost Paths]
L(n) = min[L(n), L(x) + w(x, n)] for all n Ï T
If latter term is minimum, path from s to n is path from s to x concatenated with edge from x to n
Notes: Dijkstra's Algorithm has three steps; steps 2 and 3 are repeated until T = N. That is, steps 2 and 3 are repeated until final paths have been assigned to all nodes in the network. It can be formally described as shown above, given the following definitions:
N = set of nodes in the network
s = source node
T = set of nodes so far incorporated by the algorithm
w(i, j) = link cost from node i to node j; w(i, i) = 0; w(i, j) = ∞ if two nodes not directly connected; w(i, j) ≥ 0 if two nodes are directly connected
L(n) = cost of the least-cost path from node s to node n that is currently known to the algorithm; at termination, this is the cost of the least-cost path in the graph from s to n.
The algorithm terminates when all nodes have been added to T. At termination, the value L(x) associated with each node x is the cost (length) of the least-cost path from s to x. In addition, T defines the least-cost path from s to each other node. One iteration of steps 2 and 3 adds one new node to T and defines the least-cost path from s to that node. That path passes only through nodes that are in T. To see this, consider the following line of reasoning. After k iterations, there are k nodes in T, and the least-cost path from s to each of these nodes has been defined. Now consider all possible paths from s to nodes not in T. Among those paths, there is one of least cost that passes exclusively through nodes in T (see Problem 12.4), ending with a direct link from some node in T to a node not in T. This node is added to T and the associated path is defined as the least-cost path for that node.

## Slide 32: Table 19.4(a) Example of Least-Cost Routing Algorithms (using Figure 19.1)
Dijkstra'a Algorithm (s = 1)
Notes: Table 19.4a and Figure 19.14 show the result of applying this
algorithm to the graph of Figure 19.1, using s = 1. The shaded edges define the
spanning tree for the graph. The values in each circle are the current estimates of
L (x ) for each node x . A node is shaded when it is added to T . Note that at each
step the path to each node plus the total cost of that path is generated. After the
final iteration, the least-cost path to each node and the cost of that path have been
developed. The same procedure can be used with node 2 as source node, and so on.

## Slide 34: Bellman-Ford Algorithm
Find shortest paths from given node subject to constraint that paths contain at most one link
Find the shortest paths with a constraint of paths of at most two links
Proceeds in stages
Notes: The Bellman-Ford algorithm [FORD62] can be stated as: Find the shortest paths from a given source node subject to the constraint that the paths contain at most one link, then find the shortest paths with a constraint of paths of at most two links, and so on. This algorithm also proceeds in stages.
For the iteration of step 2 with h = K, and for each destination node n, the algorithm compares potential paths from s to n of length K + 1 with the path that existed at the end of the previous iteration. If the previous, shorter, path has less cost, then that path is retained. Otherwise a new path with length K + 1 is defined from s to n; this path consists of a path of length K from s to some node j, plus a direct hop from node j to node n. In this case, the path from s to j that is used is the K-hop path for j defined in the previous iteration (see Problem 19.5).

## Slide 35: Bellman-Ford Algorithm
Step1 [Initialization]
L0(n) = , for all n  s
Lh(s) = 0, for all h
Step 2 [Update]
For each successive h  0
For each n ≠ s, compute: Lh+1(n)=minj[Lh(j)+w(j,n)]
Connect n with predecessor node j that gives min
Eliminate any connection of n with different predecessor node formed during an earlier iteration
Path from s to n terminates with link from j to n
Notes: The algorithm is formally described as shown. For the iteration of step 2 with h = K, and for each destination node n, the algorithm compares potential paths from s to n of length K + 1 with the path that existed at the end of the previous iteration. If the previous, shorter, path has less cost, then that path is retained. Otherwise a new path with length K + 1 is defined from s to n; this path consists of a path of length K from s to some node j, plus a direct hop from node j to node n. In this case, the path from s to j that is used is the K-hop path for j defined in the previous iteration.

## Slide 36: Table 19.4(b) Example of Least-Cost Routing Algorithms (using Figure 19.1)
Bellman-Ford Algorithm (s = 1)
Notes: Table 19.4b and Figure 19.15 show the result of applying
this algorithm to Figure 19.1, using s = 1.s At each step, the least-cost paths
with a maximum number of links equal to h are found. After the final iteration,
the least-cost path to each node and the cost of that path have been
developed. The same procedure can be used with node 2 as source node,
and so on. Note that the results agree with those obtained using Dijkstra’s
algorithm.

## Slide 38: Comparison
Bellman-Ford
  Calculation for node n needs link cost to neighboring nodes plus total cost to each neighbor from s
  Each node can maintain set of costs and paths for every other node
  Can exchange information with direct neighbors
  Can update costs and paths based on information from neighbors and knowledge of link costs
Dijkstra
  Each node needs complete topology
  Must know link costs of all links in network
  Must exchange information with all other nodes
Notes: One interesting comparison can be made between these two algorithms, having to do with what information needs to be gathered. Consider first the Bellman-Ford algorithm. In step 2, the calculation for node n involves knowledge of the link cost to all neighboring nodes to node n ]i.e., w(j, n)] plus the total path cost to each of those neighboring nodes from a particular source node s [i.e., Lh(j)]. Each node can maintain a set of costs and associated paths for every other node in the network and exchange this information with its direct neighbors from time to time. Each node can therefore use the expression in step 2 of the Bellman-Ford algorithm, based only on information from its neighbors and knowledge of its link costs, to update its costs and paths. On the other hand, consider Dijkstra's algorithm. Step 3 appears to require that each node must have complete topological information about the network. That is, each node must know the link costs of all links in the network. Thus, for this algorithm, information must be exchanged with all other nodes.

## Slide 39: Evaluation
Dependent on
Processing time of algorithms
Amount of information required from other nodes
Implementation specific
Both converge under static topology and costs
Both converge to same solution
If link costs change, algorithms attempt to catch up
If link costs depend on traffic, which depends on routes chosen, may have feedback instability
Notes: In general, evaluation of the relative merits of the two algorithms should consider the processing time of the algorithms and the amount of information that must be collected from other nodes in the network or internet. The evaluation will depend on the implementation approach and the specific implementation.
A final point: Both algorithms are known to converge under static conditions of topology, and link costs and will converge to the same solution. If the link costs change over time, the algorithm will attempt to catch up with these changes. However, if the link cost depends on traffic, which in turn depends on the routes chosen, then a feedback condition exists, and instabilities may result.

## Slide 40: Summary
Routing in packet-switching networks
  Characteristics
  Routing strategies
Examples: Routing in ARPANET
  First generation: Distance Vector Routing
  Second generation: Link-State Routing
  Third generation
Internet routing protocols
  Autonomous systems
  Approaches to routing
  Border gateway protocol
  OSPF protocol
Least-cost algorithms
  Dijkstra’s algorithm
  Bellman-Ford algorithm
  Comparison
Notes: Chapter 19 summary.

## Slide 41: Additional Slides

## Slide 42: Routing Strategies - Flooding
Packet sent by node to every neighbor
Eventually multiple copies arrive at destination
No network information required
Each packet is uniquely numbered so duplicates can be discarded
Need to limit incessant retransmission of packets
  Nodes can remember identity of packets retransmitted
  Can include a hop count in packets
Notes: Another simple routing technique is flooding. This technique requires no network information whatsoever and works as follows. A packet is sent by a source node to every one of its neighbors. At each node, an incoming packet is retransmitted on all outgoing links except for the link on which it arrived. Eventually, a number of copies of the packet will arrive at the destination. The packet must have some unique identifier (e.g., source node and sequence number, or virtual circuit number and sequence number) so that the destination knows to discard all but the first copy.
Unless something is done to stop the incessant retransmission of packets, the number of packets in circulation just from a single source packet grows without bound. One way to prevent this is for each node to remember the identity of those packets it has already retransmitted. When duplicate copies of the packet arrive, they are discarded. A simpler technique is to include a hop count field with each packet. The count can originally be set to some maximum value, such as the diameter (length of the longest minimum-hop path through the network) of the network. Each time a node passes on a packet, it decrements the count by one. When the count reaches zero, the packet is discarded.

## Slide 43
Notes: An example of the latter tactic is shown in Figure 19.3. The label on each packet in the figure indicates the current value of the hop count field in that packet. A packet is to be sent from node 1 to node 6 and is assigned a hop count of 3. On the first hop, three copies of the packet are created, and the hop count is decrement to 2. For the second hop of all these copies, a total of nine copies are created. One of these copies reaches node 6, which recognizes that it is the intended destination and does not retransmit. However, the other nodes generate a total of 22 new copies for their third and final hop. Each packet now has a hope count of 1. Note that if a node is not keeping track of packet identifier, it may generate multiple copies at this third stage. All packets received from the third hop are discarded, because the hop count is exhausted. In all, node 6 has received four additional copies of the packet.

## Slide 44: Properties of Flooding
All possible routes are tried
Highly robust
Can be used to send emergency messages
At least one packet will have taken minimum hop route
Nodes directly or indirectly connected to source are visited
Disadvantages:
High traffic load generated
Security concerns
Notes: The flooding technique has three remarkable properties:
• All possible routes between source and destination are tried. Thus, no matter what link or node outages have occurred, a packet will always get through if at least one path between source and destination exists.
• Because all routes are tried, at least one copy of the packet to arrive at the destination will have used a minimum-hop route.
• All nodes that are directly or indirectly connected to the source node are visited.
Because of the first property, the flooding technique is highly robust and could be used to send emergency messages. An example application is a military network that is subject to extensive damage. Because of the second property, flooding might be used initially to set up the route for a virtual circuit. The third property suggests that flooding can be useful for the dissemination of important information to all nodes; we will see that it is used in some schemes to disseminate routing information. The principal disadvantage of flooding is the high traffic load that it generates, which is directly proportional to the connectivity of the network. Another disadvantage is that every node sees the routing data, which may create a security concern.

## Slide 45: Routing Strategies - Random Routing
Simplicity of flooding with much less traffic load
Node selects one outgoing path for retransmission of incoming packet
Selection can be random or round robin
A refinement is to select outgoing path based on probability calculation
No network information needed
Random route is typically neither least cost nor minimum hop
Notes: Random routing has the simplicity and robustness of flooding with far less traffic load. With random routing, a node selects only one outgoing path for retransmission of an incoming packet. The outgoing link is chosen at random, excluding the link on which the packet arrived. If all links are equally likely to be chosen, then a node may simply utilize outgoing links in a round-robin fashion.
A refinement of this technique is to assign a probability to each outgoing link and to select the link based on that probability. The probability could be based on data rate, or on fixed link costs.
Like flooding, random routing requires the use of no network information. Because the route taken is random, the actual route will typically not be the least-cost route nor the minimum-hop route. Thus, the network must carry a higher than optimum traffic load, although not nearly as high as for flooding.

## Slide 46
Notes: As an example, Figure 19.4 show the status of node 4 of Figure 19.1 at a certain point in time. Node 4 has links to four other nodes. A fair number of packets have been arriving and a backlog has built up, with a queue of packets waiting for each of the outgoing links. A packet arrives from node 1 destined for node 6. To which outgoing link should the packet be routed? Based on current queue lengths and the values of bias (B6) for each outgoing link, the minimum value of Q + B6 is 4, on the link to node 3. Thus, node 4 routes the packet through node 3.

## Slide 47: ARPANET Routing Strategies 1st Generation
Distance Vector Routing
1969
Distributed adaptive using estimated delay
  Queue length used as estimate of delay
Version of Bellman-Ford algorithm
Node exchanges delay vector with neighbors
Update routing table based on incoming information
Doesn't consider line speed, just queue length and responds slowly to congestion
Notes: In this section, we look at several examples of routing strategies. All of these were initially developed for ARPANET, which is a packet-switching network that was the foundation of the present-day Internet. It is instructive to examine these strategies for several reasons. First, these strategies and similar ones are also used in other packet-switching networks, including a number of networks on the Internet. Second, routing schemes based on the ARPANET work have also been used for internetwork routing in the Internet and in private internetworks. And finally, the ARPANET routing scheme evolved in a way that illuminates some of the key design issues related to routing algorithms.
The original routing algorithm, designed in 1969, was a distributed adaptive algorithm using estimated delay as the performance criterion and a version of the Bellman-Ford algorithm (Section 19.4). The approach used is referred to as distance-vector routing.

## Slide 48
Notes: Figure 19.5 shows the data structures of the original ARPANET
algorithm, using the network of Figure 19.6. This is the same network as that of
Figure 19.1, with some of the link costs having different values (and assuming the
same cost in both directions). Figure 19.5a shows the routing table for node 1 at
an instant in time that reflects the link costs of Figure 19.6. For each destination,
a delay is specified, and the next node on the route that produces that delay. At
some point, the link costs change to those of Figure 19.1. Assume that node 1’s
neighbors (nodes 2, 3, and 4) learn of the change before node 1. Each of these
nodes updates its delay vector and sends a copy to all of its neighbors, including
node 1 (Figure 19.5b). Node 1 discards its current routing table and builds a new
one, based solely on the incoming delay vector and its own estimate of link delay
to each of its neighbors. The result is shown in Figure 19.5c.

## Slide 49
Notes: The estimated link delay is simply the queue length for that link. Thus, in
building a new routing table, the node will tend to favor outgoing links with shorter
queues. This tends to balance the load on outgoing links. However, because queue
lengths vary rapidly with time, the distributed perception of the shortest route could
change while a packet is en route. This could lead to a thrashing situation in which
a packet continues to seek out areas of low congestion rather than aiming at the
destination.

## Slide 50: ARPANET Routing Strategies 2nd Generation
Link-State Routing
1979
Distributed adaptive using delay criterion
  Using timestamps of arrival, departure and ACK times
Re-computes average delays every 10 seconds
Any changes are flooded to all other nodes
Re-computes routing using Dijkstra’s algorithm
Good under light and medium loads
Under heavy loads, little correlation between reported delays and those experienced
Notes: After some years of experience and several minor modifications, the original routing algorithm was replaced by a quite different one in 1979 [MCQU80]. The major shortcomings of the old algorithm were these:
The algorithm did not consider line speed, merely queue length. Thus, higher-capacity links were not given the favored status they deserved.
Queue length is, in any case, an artificial measure of delay, because some variable amount of processing time elapses between the arrival of a packet at a node and its placement in an outbound queue.
The algorithm was not very accurate. In particular, it responded slowly to congestion and delay increases.
The new algorithm is also a distributed adaptive one, using delay as the performance criterion, but the differences are significant. Rather than using queue length as a surrogate for delay, the delay is measured directly. At a node, each incoming packet is timestamped with an arrival time. A departure time is recorded when the packet is transmitted. If a positive acknowledgment is returned, the delay for that packet is recorded as the departure time minus the arrival time plus transmission time and propagation delay. The node must therefore know link data rate and propagation time. If a negative acknowledgment comes back, the departure time is updated and the node tries again, until a measure of successful transmission delay is obtained.
Every 10 seconds, the node computes the average delay on each outgoing link. If there are any significant changes in delay, the information is sent to all other nodes using flooding. Each node maintains an estimate of delay on every network link. When new information arrives, it recomputes its routing table using Dijkstra's algorithm (Section 19.4).
The second-generation routing algorithm is referred to as a link-state routing algorithm.

## Slide 51
Notes: As an example, consider a network that consists of two regions with only two links, A and B, connecting the two regions (Figure 19.7). Each route between two nodes in different regions must pass through one of these links. Assume that a situation develops in which most of the traffic is on link A. This will cause the link delay on A to be significant, and at the next opportunity, this delay value will be reported to all other nodes. These updates will arrive at all nodes at about the same time, and all will update their routing tables immediately. It is likely that this new delay value for link A will be high enough to make link B the preferred choice for most, if not all, inter-region routes. Because all nodes adjust their routes at the same time, most or all inter-region traffic shifts at the same time to link B. Now the link delay value on B will become high, and there will be a subsequent shift to link A. This oscillation will continue until the traffic volume subsides.
There are a number of reasons why this oscillation is undesirable:
A significant portion of available capacity is unused at just the time when it is needed most: under heavy traffic load.
The overutilization of some links can lead to the spread of congestion within the network (this will be seen in the discussion of congestion in Chapter 20).
The large swings in measured delay values result in the need for more frequent routing update messages. This increases the load on the network at just the time when the network is already stressed.

## Slide 52: ARPANET Routing Strategies 3rd Generation
1987
Link cost calculation changed
  Damp routing oscillations
  Reduce routing overhead
Measure average delay over last 10 seconds and transform into link utilization estimate
Normalize this based on current value and previous results
Set link cost as function of average utilization
Notes: The ARPANET designers concluded that the essence of the problem was that every node was trying to obtain the best route for all destinations, and that these efforts conflicted. It was concluded that under heavy loads, the goal of routing should be to give the average route a good path instead of attempting to give all routes the best path.
The designers decided that it was unnecessary to change the overall routing algorithm. Rather, it was sufficient to change the function that calculates link costs. This was done in such a way as to damp routing oscillations and reduce routing overhead. The calculation begins with measuring the average delay over the last 10 seconds.

## Slide 53
Notes: In Figure 19.8, delay is normalized to the value achieved on an idle line, which is just propagation delay plus transmission time. One curve on the figure indicates the way in which the actual delay rises as a function of utilization; the increase in delay is due to queuing delay at the node. For the revised algorithm, the cost value is kept at the minimum value until a given level of utilization is reached. This feature has the effect of reducing routing overhead at low traffic levels. Above a certain level of utilization, the cost level is allowed to rise to a maximum value that is equal to three times the minimum value. The effect of this maximum value is to dictate that traffic should not be routed around a heavily utilized line by more than two additional hops.
Note that the minimum threshold is set higher for satellite links. This encourages the use of terrestrial links under conditions of light traffic, because the terrestrial links have much lower propagation delay. Note also that the actual delay curve is much steeper than the transformation curves at high utilization levels. It is this steep rise in link cost that causes all of the traffic on a link to be shed, which in turn causes routing oscillations.
In summary, the revised cost function is keyed to utilization rather than delay. The function acts similar to a delay-based metric under light loads and to a capacity-based metric under heavy loads.

## Slide 54
Notes: Figure 19.10 illustrates the formats of all of the BGP messages.
Each message begins with a 19-octet header containing three fields, as indicated by
the shaded portion of each message in the figure:
• Marker: Reserved for authentication. The sender may insert a value in this
field that would be used as part of an authentication mechanism to enable the
recipient to verify the identity of the sender.
• Length: Length of message in octets.
• Type: Type of message: Open, Update, Notification, Keepalive.
To acquire a neighbor, a router first opens a TCP connection to the neighbor
router of interest. It then sends an Open message. This message identifies the AS to
which the sender belongs and provides the IP address of the router. It also includes
a Hold Time parameter, which indicates the number of seconds that the sender
proposes for the value of the Hold Timer. If the recipient is prepared to open a
neighbor relationship, it calculates a value of Hold Timer that is the minimum of
its Hold Time and the Hold Time in the Open message. This calculated value is
the maximum number of seconds that may elapse between the receipt of successive
Keepalive and/or Update messages by the sender.
The Keepalive message consists simply of the header. Each router issues these
messages to each of its peers often enough to prevent the Hold Timer from expiring.
The Update message communicates two types of information:
• Information about a single route through the internet. This information is
available to be added to the database of any recipient router.
• A list of routes previously advertised by this router that are being withdrawn.
An Update message may contain one or both types of information. Information
about a single route through the network involves three fields: the Network Layer
Reachability Information (NLRI) field, the Total Path Attributes Length field, and
the Path Attributes field. The NLRI field consists of a list of identifiers of networks
that can be reached by this route. Each network is identified by its IP address, which
is actually a portion of a full IP address. Recall that an IP address is a 32-bit quantity
of the form {network, host}. The left-hand or prefix portion of this quantity identifies
a particular network.
The Path Attributes field contains a list of attributes that apply to this particular
route. The following are the defined attributes:
• Origin: Indicates whether this information was generated by an interior router
protocol (e.g., OSPF) or an exterior router protocol (in particular, BGP).
• AS_Path: A list of the ASs that are traversed for this route.
• Next_Hop: The IP address of the border router that should be used as the next
hop to the destinations listed in the NLRI field.
• Multi_Exit_Disc: Used to communicate some information about routes internal
to an AS. This is described later in this section.
• Local_Pref: Used by a router to inform other routers within the same AS of its
degree of preference for a particular route. It has no significance to routers in
other ASs.
• Atomic_Aggregate, Aggregator: These two fields implement the concept of
route aggregation. In essence, an internet and its corresponding address space
can be organized hierarchically (i.e., as a tree). In this case, network addresses
are structured in two or more parts. All of the networks of a given subtree share a
common partial internet address. Using this common partial address, the amount
of information that must be communicated in NLRI can be significantly reduced.
The AS_Path attribute actually serves two purposes. Because it lists the ASs that
a datagram must traverse if it follows this route, the AS_Path information enables a
router to implement routing policies. That is, a router may decide to avoid a particular
path to avoid transiting a particular AS. For example, information that is confidential
may be limited to certain kinds of ASs. Or a router may have information about the
performance or quality of the portion of the internet that is included in an AS that
leads the router to avoid that AS. Examples of performance or quality metrics include
link speed, capacity, tendency to become congested, and overall quality of operation.
Another criterion that could be used is minimizing the number of transit ASs.
The second type of update information is the withdrawal of one or more routes.
In this case, the route is identified by the IP address of the destination network.
Finally, the Notification message is sent when an error condition is detected.
The following errors may be reported:
• Message header error: Includes authentication and syntax errors.
• Open message error: Includes syntax errors and options not recognized in
an Open message. This message can also be used to indicate that a proposed
Hold Time in an Open message is unacceptable.
• Update message error: Includes syntax and validity errors in an Update message.
• Hold timer expired: If the sending router has not received successive Keepalive
and/or Update and/or Notification messages within the Hold Time period,
then this error is communicated and the connection is closed.
• Finite state machine error: Includes any procedural error.
• Cease: Used by a router to close a connection with another router in the
absence of any other error.