## Slide 1: Data and Computer Communications
Tenth Edition
by William Stallings
Notes: “Data and Computer Communications”, 10/e, by William Stallings, Chapter 13 “Wireless LANs”.

## Slide 2: Wireless LANs
Chapter 13
Notes: This chapter provides a survey of WLANs. We begin with an overview
that looks at the motivations for using WLANs and summarize the various
approaches in current use. The next section examines the three principal types
of wireless WLANs, classified according to transmission technology: infrared,
spread spectrum, and narrowband microwave.
The most prominent specification for WLANs was developed by the
IEEE 802.11 working group. This chapter focuses on this standard, and is
based on the 2012 version.

## Slide 3
Notes: Figure 13.1 indicates a simple WLAN configuration that is typical of many environments.
There is a backbone wired LAN, such as Ethernet, that supports servers,
workstations, and one or more bridges or routers to link with other networks. In
addition, there is a control module (CM) that acts as an interface to a WLAN. The
control module includes either bridge or router functionality to link the WLAN
to the backbone. It includes some sort of access control logic, such as a polling or
token-passing scheme, to regulate the access from the end systems. Note that some
of the end systems are stand-alone devices, such as a workstation or a server. Hubs
or other user modules (UMs) that control a number of stations off a wired LAN
may also be part of the WLAN configuration.

## Slide 4
Notes: The configuration of Figure 13.1 can be referred to as a single-cell WLAN; all
of the wireless end systems are within range of a single control module. Another
common configuration, suggested by Figure 13.2, is a multiple-cell WLAN. In this
case, there are multiple control modules interconnected by a wired LAN. Each
control module supports a number of wireless end systems within its transmission
range. For example, with an infrared LAN, transmission is limited to a single
room; therefore, one cell is needed for each room in an office building that requires
wireless support.

## Slide 5
Notes: Figure 13.3 illustrates a different type of configuration, referred to as an
ad hoc network , from that shown in Figures 13.1 and 13.2. Typically, the WLAN
forms a stationary infrastructure consisting of one or more cells with a control
module for each cell. Within a cell, there may be a number of stationary end
systems. Nomadic stations can move from one cell to another. By contrast, there
is no infrastructure for an ad hoc network. Rather, a peer collection of stations
within a range of each other may dynamically configure themselves into a
temporary network.

## Slide 6: Wireless LAN Requirements
Throughput
Number of nodes
Connection to backbone LAN
Service area
Battery power consumption
Transmission robustness and security
Collocated network operation
License-free operation
Handoff/roaming
Dynamic configuration
Notes: A WLAN must meet the same sort of requirements typical of any LAN, including
high capacity, ability to cover short distances, full connectivity among attached
stations, and broadcast capability. In addition, there are a number of requirements
specific to the WLAN environment. The following are among the most important
requirements for WLANs:
• Throughput: The medium access control (MAC) protocol should make as efficient
use as possible of the wireless medium to maximize capacity.
• Number of nodes: WLANs may need to support hundreds of nodes across
multiple cells.
• Connection to backbone LAN: In most cases, interconnection with stations on
a wired backbone LAN is required. For infrastructure WLANs, this is easily
accomplished through the use of control modules that connect to both types of
LANs. There may also need to be accommodation for mobile users and ad hoc
wireless networks.
• Service area: A typical coverage area for a WLAN has a diameter of 100 to
300 m.
• Battery power consumption: Mobile workers use battery-powered workstations
that need to have a long battery life when used with wireless adapters.
This suggests that a MAC protocol that requires mobile nodes to monitor
access points constantly or engage in frequent handshakes with a base
station is inappropriate. Typical WLAN implementations have features
to reduce power consumption while not using the network, such as a
sleep mode.
• Transmission robustness and security: Unless properly designed, a WLAN
may be especially vulnerable to interference and network eavesdropping.
The design of a WLAN must permit reliable transmission even in a
noisy environment and should provide some level of security from
eavesdropping.
• Collocated network operation: As WLANs become more popular, it is quite
likely for two or more WLANs to operate in the same area or in some area
where interference between the LANs is possible. Such interference may
thwart the normal operation of a MAC algorithm and may allow unauthorized
access to a particular LAN.
• License-free operation: Users would prefer to buy and operate WLAN products
without having to secure a license for the frequency band used by the
LAN.
• Handoff/roaming: The MAC protocol used in the WLAN should enable
mobile stations to move from one cell to another.
• Dynamic configuration: The MAC addressing and network management
aspects of the WLAN should permit dynamic and automated addition, deletion,
and relocation of end systems without disruption to other users.

## Slide 7: Wi-Fi Alliance
There is always a concern whether products from different vendors will successfully interoperate
Wireless Ethernet Compatibility Alliance (WECA)
  Industry consortium formed in 1999
Renamed the Wi-Fi (Wireless Fidelity) Alliance
  Created a test suite to certify interoperability for 802.11 products
Notes: Although 802.11 products are all based on the same standards, there is always a
concern whether products from different vendors will successfully interoperate.
To meet this concern, the Wireless Ethernet Compatibility Alliance (WECA), an
industry consortium, was formed in 1999. This organization, subsequently renamed
the Wi-Fi (Wireless Fidelity) Alliance, created a test suite to certify interoperability
for 802.11 products.

## Slide 8
Notes: Figure 13.4 illustrates the model developed by the 802.11 working group. The
smallest building block of a WLAN is a basic service set (BSS) , which consists
of some number of stations executing the same MAC protocol and competing
for access to the same shared wireless medium. A BSS may be isolated or it may
connect to a backbone distribution system (DS) through an access point (AP) .
The AP functions as a bridge and a relay point. In a BSS, client stations do not
communicate directly with one another. Rather, if one station in the BSS wants to
communicate with another station in the same BSS, the MAC frame is first sent
from the originating station to the AP, and then from the AP to the destination
station. Similarly, a MAC frame from a station in the BSS to a remote station is
sent from the local station to the AP and then relayed by the AP over the DS
on its way to the destination station. The BSS generally corresponds to what is
referred to as a cell in the literature. The DS can be a switch, a wired network, or
a wireless network.
When all the stations in the BSS are mobile stations, with no connection to
other BSSs, the BSS is called an independent BSS (IBSS) . An IBSS is typically an
ad hoc network. In an IBSS, the stations all communicate directly, and no AP is
involved.
A simple configuration is shown in Figure 13.4, in which each station belongs
to a single BSS; that is, each station is within wireless range only of other stations
within the same BSS. It is also possible for two BSSs to overlap geographically, so
that a single station could participate in more than one BSS. Further, the association
between a station and a BSS is dynamic. Stations may turn off, come within range,
and go out of range.
An extended service set (ESS) consists of two or more BSSs interconnected by
a distribution system. Typically, the distribution system is a wired backbone LAN
but can be any communications network. The ESS appears as a single logical LAN
to the logical link control (LLC) level.
Figure 13.4 indicates that an AP is implemented as part of a station; the AP
is the logic within a station that provides access to the DS by providing DS services
in addition to acting as a station. To integrate the IEEE 802.11 architecture
with a traditional wired LAN, a portal is used. The portal logic is implemented
in a device, such as a bridge or router, that is part of the wired LAN and that is
attached to the DS.

## Slide 9: Medium Access Control
MAC layer covers three functional areas:
Reliable data delivery
Access control
Security
Notes: The IEEE 802.11 MAC layer covers three functional areas: reliable data delivery, access control, and security. This section covers the first two topics.

## Slide 10: Reliable Data Delivery
Can be dealt with at a higher layer
More efficient to deal with errors at MAC level
802.11 includes frame exchange protocol
  Station receiving frame returns acknowledgment (ACK) frame
  Exchange treated as atomic unit
  If no ACK within short period of time, retransmit
802.11 physical and MAC layers unreliable
  Noise, interference, and other propagation effects result in loss of frames
  Even with error-correction codes, frames may not successfully be received
Notes: As with any wireless network, a wireless LAN using the IEEE 802.11 physical and MAC layers is subject to considerable unreliability. Noise, interference, and other propagation effects result in the loss of a significant number of frames. Even with error correction codes, a number of MAC frames may not successfully be received. This situation can be dealt with by reliability mechanisms at a higher layer, such as TCP. However, timers used for retransmission at higher layers are typically on the order of seconds. It is therefore more efficient to deal with errors at the MAC level. For this purpose, IEEE 802.11 includes a frame exchange protocol. When a station receives a data frame from another station, it returns an acknowledgment (ACK) frame to the source station. This exchange is treated as an atomic unit, not to be interrupted by a transmission from any other station. If the source does not receive an ACK within a short period of time, either because its data frame was damaged or because the returning ACK was damaged, the source retransmits the frame.

## Slide 11: Four Frame Exchange
RTS alerts all stations within range of source that exchange is under way
CTS alerts all stations within range of destination
Other stations don’t transmit to avoid collision
RTS/CTS exchange is a required function of MAC but may be disabled
Can use four-frame exchange for better reliability
Source issues a Request to Send (RTS) frame
Destination responds with Clear to Send (CTS)
After receiving CTS, source transmits data
Destination responds with ACK
Notes: Thus, the basic data transfer mechanism in IEEE 802.11 involves an exchange of two frames. To further enhance reliability, a four-frame exchange may be used. In this scheme, a source first issues a Request to Send (RTS) frame to the destination. The destination then responds with a Clear to Send (CTS). After receiving the CTS, the source transmits the data frame, and the destination responds with an ACK. The RTS alerts all stations that are within reception range of the source that an exchange is under way; these stations refrain from transmission in order to avoid a collision between two frames transmitted at the same time. Similarly, the CTS alerts all stations that are within reception range of the destination that an exchange is under way. The RTS/CTS portion of the exchange is a required function of the MAC but may be disabled.

## Slide 12
Notes: The 802.11 working group considered two types of proposals for a MAC algorithm:
distributed access protocols, which, like Ethernet, distribute the decision
to transmit over all the nodes using a carrier sense mechanism; and centralized
access protocols, which involve regulation of transmission by a centralized decision
maker. A distributed access protocol makes sense for an ad hoc network of
peer workstations (typically an IBSS) and may also be attractive in other WLAN
configurations that consist primarily of bursty traffic. A centralized access
protocol is natural for configurations in which a number of wireless stations are
interconnected with each other and some sort of base station that attaches to a
backbone wired LAN; it is especially useful if some of the data is time sensitive
or high priority.
The end result for 802.11 is a MAC algorithm called DFWMAC (distributed
foundation wireless MAC) that provides a distributed access control mechanism
with an optional centralized control built on top of that. Figure 13.5 illustrates the
architecture. The lower sublayer of the MAC layer is the distributed coordination
function (DCF). DCF uses a contention algorithm to provide access to all traffic.
Ordinary asynchronous traffic directly uses DCF. The point coordination function
(PCF) is a centralized MAC algorithm used to provide contention-free service. PCF
is built on top of DCF and exploits features of DCF to assure access for its users.

## Slide 13: Distributed Coordination Function (DCF)
DCF sublayer uses CSMA algorithm
Does not include a collision detection function because it is not practical on a wireless network
Includes a set of delays that amounts as a priority scheme
If station has frame to send it listens to medium
If medium is idle, station may transmit
Else waits until current transmission is complete
Notes: The DCF sublayer makes use of a simple CSMA (carrier sense multiple access) algorithm. If a station has a MAC frame to transmit, it listens to the medium. If the medium is idle, the station may transmit; otherwise the station must wait until the current transmission is complete before transmitting. The DCF does not include a collision detection function (i.e., CSMA/CD) because collision detection is not practical on a wireless network. The dynamic range of the signals on the medium is very large, so that a transmitting station cannot effectively distinguish incoming weak signals from noise and the effects of its own transmission.
To ensure the smooth and fair functioning of this algorithm, DCF includes a set of delays that amounts to a priority scheme. Let us start by considering a single delay known as an interframe space (IFS). In fact, there are three different IFS values, but the algorithm is best explained by initially ignoring this detail.

## Slide 14
Notes: Using an IFS, the rules for CSMA access are as follows (Figure 13.6):
A station with a frame to transmit senses the medium. If the medium is idle, it waits to see if the medium remains idle for a time equal to IFS. If so, the station may transmit immediately.
2. If the medium is busy (either because the station initially finds the medium busy or because the medium becomes busy during the IFS idle time), the station defers transmission and continues to monitor the medium until the current transmission is over
3. Once the current transmission is over, the station delays another IFS. If the medium remains idle for this period, then the station backs off a random amount of time and again senses the medium. If the medium is still idle, the station may transmit. During the backoff time, if the medium becomes busy, the backoff timer is halted and resumes when the medium becomes idle.
4. If the transmission is unsuccessful, which is determined by the absence of an acknowledgement, then it is assumed that a collision has occurred.
To ensure that backoff maintains stability, binary exponential backoff, described in Chapter 12, is used. Binary exponential backoff provides a means of handling a heavy load. Repeated failed attempts to transmit result in longer and longer backoff times, which helps to smooth out the load. Without such a backoff, the following situation could occur: Two or more stations attempt to transmit at the same time, causing a collision. These stations then immediately attempt to retransmit, causing a new collision.

## Slide 15: Priority IFS Values
SIFS
(short IFS)
For all immediate response actions
PIFS
(point coordination function IFS)
Used by the centralized controller in PCF scheme when issuing polls
DIFS
(distributed coordination function IFS)
Used as minimum delay for asynchronous frames contending for access
Notes: The preceding scheme is refined for DCF to provide priority-based access by the simple expedient of using three values for IFS:
SIFS (short IFS): The shortest IFS, used for all immediate response actions, as explained in the following discussion
PIFS (point coordination function IFS): A midlength IFS, used by the centralized controller in the PCF scheme when issuing polls
DIFS (distributed coordination function IFS): The longest IFS, used as a minimum delay for asynchronous frames contending for access

## Slide 16
Notes: Figure 13.7a illustrates the use of these time values.

## Slide 17: SIFS
Any station using SIFS to determine transmission opportunity has the highest priority
Used in the following circumstances:
  Acknowledgment (ACK)
    Station responds with an ACK frame after waiting only for a SIFS gap
    Provides for efficient collision recovery
  Clear to Send (CTS)
    Station ensures data frame gets through by issuing RTS
  Poll response
Notes: Consider first the SIFS. Any station using SIFS to determine transmission opportunity has, in effect, the
highest priority, because it will always gain access in preference to a station waiting
an amount of time equal to PIFS or DIFS. The SIFS is used in the following
circumstances:
• Acknowledgment (ACK): When a station receives a frame addressed only
to itself (not multicast or broadcast), it responds with an ACK frame after
waiting only for an SIFS gap. This has two desirable effects. First, because
collision detection is not used, the likelihood of collisions is greater than with
CSMA/CD, and the MAC-level ACK provides for efficient collision recovery.
Second, the SIFS can be used to provide efficient delivery of an LLC protocol
data unit (PDU) that requires multiple MAC frames. In this case, the
following scenario occurs. A station with a multiframe LLC PDU to transmit
sends out the MAC frames one at a time. Each frame is acknowledged by the
recipient after SIFS. When the source receives an ACK, it immediately (after
SIFS) sends the next frame in the sequence. The result is that once a station
has contended for the channel, it will maintain control of the channel until it
has sent all of the fragments of an LLC PDU.
• Clear to Send (CTS): A station can ensure that its data frame will get through
by first issuing a small RTS frame. The station to which this frame is addressed
should immediately respond with a CTS frame if it is ready to receive. All
other stations receive the RTS and defer using the medium.
• Poll response: This is explained in the following discussion of PCF.
The next longest IFS interval is the PIFS. This is used by the centralized
controller in issuing polls and takes precedence over normal contention traffic.
However, those frames transmitted using SIFS have precedence over a PCF poll.
Finally, the DIFS interval is used for all ordinary asynchronous traffic.

## Slide 18: Point Coordination Function (PCF)
Alternative access method implemented on top of DCF
Polling by centralized polling master (point coordinator)
Uses PIFS when issuing polls
Point coordinator polls in round-robin to stations configured for polling
When poll issued, polled station may respond using SIFS
If point coordinator receives response, it issues another poll using PIFS
If no response during expected turnaround time, coordinator issues poll
Coordinator could lock out asynchronous traffic by issuing polls
Have a superframe interval defined
Notes: PCF is an alternative access method implemented on top of the DCF. The operation consists of polling by the centralized polling master (point coordinator). The point coordinator makes use of PIFS when issuing polls. Because PIFS is smaller than DIFS, the point coordinator can seize the medium and lock out all asynchronous traffic while it issues polls and receives responses.
As an extreme, consider the following possible scenario. A wireless network is configured so that a number of stations with time-sensitive traffic are controlled by the point coordinator while remaining traffic contends for access using CSMA. The point coordinator could issue polls in a round-robin fashion to all stations configured for polling. When a poll is issued, the polled station may respond using SIFS. If the point coordinator receives a response, it issues another poll using PIFS. If no response is received during the expected turnaround time, the coordinator issues a poll.
If the discipline of the preceding paragraph were implemented, the point coordinator would lock out all asynchronous traffic by repeatedly issuing polls. To prevent this, an interval known as the superframe is defined. During the first part of this interval, the point coordinator issues polls in a round-robin fashion to all stations configured for polling. The point coordinator then idles for the remainder of the superframe, allowing a contention period for asynchronous access.

## Slide 19
Notes: Figure 13.7b illustrates the use of the superframe. At the beginning of a superframe, the point coordinator may optionally seize control and issue polls for a given period of time. This interval varies because of the variable frame size issued by responding stations. The remainder of the superframe is available for contention-based access. At the end of the superframe interval, the point coordinator contends for access to the medium using PIFS. If the medium is idle, the point coordinator gains immediate access and a full superframe period follows. However, the medium may be busy at the end of a superframe. In this case, the point coordinator must wait until the medium is idle to gain access; this results in a foreshortened superframe period for the next cycle.

## Slide 20: Table 13.4 IEEE 802.11 Physical Layer Standards
(Table is on page 412 in textbook)
Notes: Since its introduction, the IEEE 802.11 standard has been expanded and revised
a number of times. The first version of the standard, simply called IEEE 802.11,
includes the MAC layer and three physical layer specifications, two in the 2.4-GHz
band (ISM) and one in the infrared, all operating at 1 and 2 Mbps. This version
is now obsolete and no longer in use. Table 13.4 summarizes key characteristics
of the subsequent revisions. In this section, we survey 802.11b, 802.11a, 802.11g,
and 802.11n. The following section deals with 802.11ac and 802.11ad, both of which
provide for data rates greater than 1 Gbps.

## Slide 21: IEEE 802.11g
Higher-speed extension to 802.11b
Operates in 2.4GHz band
Compatible with 802.11b devices
Combines physical layer encoding techniques used in 802.11 and 802.11b to provide service at a variety of data rates
  ERP-OFDM for 6, 9, 12, 18, 24, 36, 48, 54Mbps rates
  ERP-PBCC for 22 and 33Mbps rates
Notes: IEEE 802.11g extends 802.11b to data rates above 20 Mbps, up to 54 Mbps. Like 802.11b, 802.11g operates in the 2.4-GHz range and thus the two are compatible. The standard is designed so that 802.11b devices will work when connected to an 802.11g AP, and 802.11g devices will work when connected to an 802.11b AP, in both cases using the lower 802.11b data rate.
EE 802.11g offers a wider array of data rate and modulation scheme options. IEEE 802.11g provides compatibility with 802.11 and 802.11b by specifying the same modulation and framing schemes as these standards for 1, 2, 5.5, and 11 Mbps. At data rates of 6, 9, 12, 18, 24, 36, 48, and 54 Mbps, 802.11g adopts the 802.11a OFDM scheme, adapted for the 2.4 GHz rate; this is referred to as ERP-OFDM, with ERP standing for extended rate physical layer. In addition, an ERP-PBCC scheme is used to provide data rates of 22 and 33 Mbps.

## Slide 22: Table 13.5 Estimated Distance (m) Versus Data Rate
Notes: The IEEE 802.11 standards do not include a specification of speed versus distance objectives. Different vendors will give different values, depending on environment. Table 13.5, based on [LAYL04] gives estimated values for a typical office environment.

## Slide 23: IEEE 802.11n
Has enhancements in three general areas:
  Multiple-input-multiple-output (MIMO) antenna architecture
    Most important enhancement
  Radio transmission scheme
    Increased capacity
  MAC enhancements
    Most significant change is to aggregate multiple MAC frames into a single block for transmission
Notes: With increasing demands being placed on wireless LANs, the 802.11 committee looked for ways to increase the data throughput and overall capacity of 802.11 networks. The goal of this effort is to not just increase the bit rate of the transmitting antennas but to increase the effective throughput of the network. Increasing effective throughput involves not only looking at the signal encoding scheme, but also at the antenna architecture and the MAC frame structure. The result of these efforts is a package of improvements and enhancements embodied in IEEE 802.11n. This standard is defined to operate in both the 2.4-GHz and the 5-GHz bands and can therefore be made upwardly compatible with either 802.11a or 802.11b/g.
IEEE 802.11n embodies changes in three general areas: use of MIMO, enhancements in radio transmission, and MAC enhancements. We briefly examine each of these.
Multiple-input-multiple-output (MIMO) antenna architecture is the most important of the enhancements provided by 802.11n. A discussion of MIMO is beyond our scope, so we content ourselves with a brief overview. In a MIMO scheme, the transmitter employs multiple antennas. The source data stream is divided into n substreams, one for each of the n transmitting antennas. The individual substreams are the input to the transmitting antennas (multiple input). At the receiving end, m antennas receive the transmissions from the n source antennas via a combination of line-of-sight transmission and multipath. The outputs from the m receiving antennas (multiple output) are combined with the signals from the other receive radios. With a lot of complex math, the result is a much better receive signal than can be achieved with either a single antenna or multiple frequency channels. 802.11n defines a number of different combinations for the number of transmitters and the number of receivers, from 2  1 to 4  4. Each additional transmitter or receiver in the system increases the SNR (signal-to-noise ratio).
In addition to MIMO, 802.11n makes a number of changes in the radio transmission scheme to increase capacity. The most significant of these techniques, known as channel bonding, combines two 20-MHz channels to create a 40-MHz channel. Using OFDM, this allows for twice as many subchannels, doubling the transmission rate.
Finally, 802.11 provides some MAC enhancements. The most significant change is to aggregate multiple MAC frames into a single block for transmission. Once a station acquires the medium for transmission, it can transmit long packets without significant delays between transmissions. The receiver sends a single block acknowledgement. Frame aggregation can result in significantly improved efficiency in the use of the transmission capacity.

## Slide 24: IEEE 802.11ac
Includes the option of multiuser MIMO (MU-MIMO)
  On the downlink the transmitter is able to use its antenna resources to transmit multiple frames to different stations, all at the same time and over the same frequency spectrum
  Each antenna of a MU-MIMO AP can simultaneously communicate with a different single-antenna device, such as a smartphone or tablet
Requires that every 802.11ac transmission be sent as an A-MPDU aggregate
Notes: Two other changes going from 802.11n to 802.11ac are noteworthy.
802.11ac includes the option of multiuser MIMO (MU-MIMO). This means that
on the downlink, the transmitter is able to use its antenna resources to transmit
multiple frames to different stations, all at the same time and over the same
frequency spectrum. Thus, each antenna of a MU-MIMO AP can simultaneously
communicate with a different single-antenna device, such as a smartphone
or tablet. This enables the AP to deliver significantly more data in many
environments.
Another difference is that 802.11ac requires that every 802.11ac transmission
to be sent as an A-MPDU aggregate. Briefly, this requirement is imposed
to guarantee efficient use of the channel. For a more extended explanation, see
[CISC12b].

## Slide 25: IEEE 802.11ad
A version of 802.11 operating in the 60-GHz frequency band
  Offers the potential for much wider channel bandwidth than the 5-GHz band
  Few devices operate in the 60-GHz which means communications would experience less interference than in the other bands used by 802.11
Undesirable propagation characteristics:
  Losses are much higher in this range than in the ranges used for traditional microwave systems
  Multipath losses can be quite high
  Millimeter-wave signals generally don’t penetrate solid objects
Notes: IEEE 802.11ad is a version of 802.11 operating in the 60-GHz frequency band. This
band offers the potential for much wider channel bandwidth than the 5-GHz band,
enabling high data rates with relatively simple signal encoding and antenna characteristics.
Few devices operate in the 60-GHz band, which means communications
would experience less interference than in the other bands used by 802.11.
However, at 60 GHz, 802.11ad is operating in the millimeter range, which has
some undesirable propagation characteristics:
1. Free space loss increases with the square of the frequency [Equation (4.3)];
thus losses are much higher in this range than in the ranges used for traditional
microwave systems.
2. Multipath losses can be quite high. Reflection occurs when an electromagnetic
signal encounters a surface that is large relative to the wavelength of the
signal; scattering occurs if the size of an obstacle is on the order of the wavelength
of the signal or less; diffraction occurs when the wavefront encounters
the edge of an obstacle that is large compared to the wavelength.
3. Millimeter-wave signals generally don’t penetrate solid objects.
For these reasons, 802.11ad is likely to be useful only within a single room.
Because it can support high data rates and, for example, could easily transmit
uncompressed high-definition video, it is suitable for applications such as replacing
wires in a home entertainment system, or streaming high-definition movies from
your cell phone to your television.

## Slide 26: 802.11ac and 802.11ad Differences
802.11ac
Supports a MIMO antenna configuration
802.11ad
Is designed for single-antenna operation
Has a huge channel bandwidth of 2160 MHz
Notes: There are two striking differences between 802.11ac and 802.11ad. Whereas
802.11ac supports a MIMO antenna configuration, 802.11ad is designed for single-antenna
operation. And 802.11ad has a huge channel bandwidth of 2160 MHz.

## Slide 27: Access and Privacy Services - Authentication
Used to establish station identity
Wired LANs assume physical connection gives authority to use LAN
Not a valid assumption for wireless LANs
802.11 supports several authentication schemes
Does not mandate any particular scheme
From relatively insecure handshaking to public-key encryption
802.11 requires mutually acceptable, successful authentication before association
Notes: There are two characteristics of a wired LAN that are not inherent in a wireless LAN.
1. In order to transmit over a wired LAN, a station must be physically connected to the LAN. On the other hand, with a wireless LAN, any station within radio range of the other devices on the LAN can transmit. In a sense, there is a form of authentication with a wired LAN, in that it requires some positive and presumably observable action to connect a station to a wired LAN.
2. Similarly, in order to receive a transmission from a station that is part of a wired LAN, the receiving station must also be attached to the wired LAN. On the other hand, with a wireless LAN, any station within radio range can receive. Thus, a wired LAN provides a degree of privacy, limiting reception of data to stations connected to the LAN.
IEEE 802.11 defines three services that provide a wireless LAN with these two features:
Authentication: Used to establish the identity of stations to each other. In a wired LAN, it is generally assumed that access to a physical connection conveys authority to connect to the LAN. This is not a valid assumption for a wireless LAN, in which connectivity is achieved simply by having an attached antenna that is properly tuned. The authentication service is used by stations to establish their identity with stations they wish to communicate with. IEEE 802.11 supports several authentication schemes and allows for expansion of the functionality of these schemes. The standard does not mandate any particular authentication scheme, which could range from relatively unsecure handshaking to public-key encryption schemes. However, IEEE 802.11 requires mutually acceptable, successful authentication before a station can establish an association with an AP.

## Slide 28: Access and Privacy Services Deauthentication and Privacy
Deauthentication
  Invoked whenever an existing authentication is to be terminated
Privacy
  Used to prevent messages being read by others
  802.11 allows optional use of encryption
Original WEP security features were weak
Subsequently 802.11i and WPA alternatives evolved giving better security
Notes: Deauthentication: This service is invoked whenever an existing authentication is to be terminated.
Privacy: Used to prevent the contents of messages from being read by other than the intended recipient. The standard provides for the optional use of encryption to assure privacy.
The original 802.11 specification included a set of security features for privacy and authentication that, unfortunately, were quite weak. For privacy, 802.11 defined the Wired Equivalent Privacy (WEP) algorithm. The privacy portion of the 802.11 standard contained major weaknesses. Subsequent to the development of WEP, the 802.11i task group has developed a set of capabilities to address the WLAN security issues. In order to accelerate the introduction of strong security into WLANs, the Wi-Fi Alliance promulgated Wi-Fi Protected Access (WPA) as a Wi-Fi standard. WPA is a set of security mechanisms that eliminates most 802.11 security issues and was based on the current state of the 802.11i standard. As 802.11i evolves, WPA will evolve to maintain compatibility.

## Slide 29: Summary
Wireless LAN configurations
Wireless LAN requirements
IEEE 802.11 architecture and services
  The Wi-Fi alliance
  IEEE 802.11 architecture
  IEEE 802.11 services
IEEE 802.11 medium access control
  Reliable data delivery
  Medium access control
  MAC frame
IEEE 802.11 physical layer
  IEEE 802.11b
  IEEE 802.11a
  IEEE 802.11g
  IEEE 802.11n
Gigabit Wi-Fi
  IEEE 802.11ac
  IEEE 802.11ad
IEEE 802.11 security considerations
  Access and privacy services
  Wireless LAN security standards
Notes: Chapter 13 summary.

## Slide 30: Additional Slides

## Slide 31: Table 13.6 IEEE 802.11ad Modulation and Coding Schemes
BPSK = binary phase-shift keying
DBPSK = differential binary phase-shift keying
LDPC = low density parity check code
OFDM = orthogonal frequency-division multiplexing
OQPSK = offset quadrature phase-shift keying
QAM = quadrature amplitude modulation
QPSK = quadrature phase-shift keying
RS = Reed-Solomon
Notes: IEEE 802.11ad defines four physical layer modulation and coding schemes
(Table 13.6). Each type has a distinct purpose and supports a different range of data rates.
Control PHY (CPHY) is by far the most robustly coded (and consequently,
lowest throughput) mode, with a code rate of only 1/2. Its purpose is exclusively to
transmit control channel messages. The CPHY robustness is evident from its use of
differential encoding, code spreading, and BPSK modulation. Differential encoding
eliminates the need for carrier tracking, 32x spreading contributes a theoretical 15
dB gain to the link budget, and BPSK is very noise tolerant.
As with CPHY, single-carrier PHY (SCPHY) uses the powerful low-density
parity-check (LDPC) code for robust forward error correction and provides three
options for modulation. The set of options for code rate and modulation density allow
for a trade-off between throughput and robustness to be determined operationally.
OFDM PHY (OFDMPHY) employs multicarrier modulation, which can provide
higher modulation densities and hence higher data throughput than the single-carrier
options. As with SCPHY, OFDMPHY provides a choice of error protection
ratio and the depth of modulation applied to the OFDM data carriers, again to
provide operational control over the robustness/throughput trade-off. The choice
between SCPHY and OFDMPHY depends on several factors. OFDM modulation
will generally impose greater power requirements than SCPHY, but is more robust
in the presence of multipath distortion.
The LDPC error-correcting coding technique that is common to the CPHY,
SCPHY, and OFDMPHY is based on a common codeword length of 672 bits carrying
336, 504, 420, or 546 payload bits to achieve a code rate of 1/2, 3/4, 5/8, or 13/16
as required.
Low-power single carrier (LPSCPHY) employs single-carrier modulation to
minimize power consumption. It also uses either Reed–Solomon or Hamming block
codes, which require less IC area and hence less power than LDPC, at the expense
of less robust error correction. Small battery-powered devices could benefit from
the extra power savings.