## Slide 1: Data and Computer Communications
Tenth Edition
by William Stallings
Notes: “Data and Computer Communications”, 10/e, by William Stallings, Chapter 12 “Ethernet”.

## Slide 2: Ethernet
Chapter 12
Notes: We begin this chapter with an overview of the 10-Mbps system and the
basic medium access control (MAC) layer defined for 10-Mbps Ethernet. We
then look at subsequent generations of Ethernet, up to the 100-Gbps version,
examining the physical layer definitions and the enhancements to the MAC
layer. Finally, the chapter looks at the IEEE 802.1Q VLAN standard.

## Slide 3: Traditional Ethernet
Earliest was ALOHA
Developed for packet radio networks
Next came slotted ALOHA
Organized slots equal to transmission time
Station may transmit a frame at any time
If frame is determined invalid, it is ignored
Maximum utilization of channel about 18%
Increased utilization to about 37%
Notes: The most widely used high-speed LANs today are based on Ethernet and were developed by the IEEE 802.3 standards committee. As with other LAN standards, there is both a medium access control layer and a physical layer, which are considered in turn in what follows.
It is easier to understand the operation of CSMA/CD if we look first at some earlier schemes from which CSMA/CD evolved.
CSMA/CD and its precursors can be termed random access, or contention, techniques. They are random access in the sense that there is no predictable or scheduled time for any station to transmit; station transmissions are ordered randomly. They exhibit contention in the sense that stations contend for time on the shared medium.
The earliest of these techniques, known as ALOHA, was developed for packet radio networks. However, it is applicable to any shared transmission medium. ALOHA, or pure ALOHA as it is sometimes called, specifies that a station may transmit a frame at any time. The station then listens for an amount of time equal to the maximum possible round-trip propagation delay on the network (twice the time it takes to send a frame between the two most widely separated stations) plus a small fixed time increment. If the station hears an acknowledgment during that time, fine; otherwise, it resends the frame. If the station fails to receive an acknowledgment after repeated transmissions, it gives up. A receiving station determines the correctness of an incoming frame by examining a frame check sequence field, as in HDLC. If the frame is valid and if the destination address in the frame header matches the receiver's address, the station immediately sends an acknowledgment. The frame may be invalid due to noise on the channel or because another station transmitted a frame at about the same time. In the latter case, the two frames may interfere with each other at the receiver so that neither gets through; this is known as a collision. If a received frame is determined to be invalid, the receiving station simply ignores the frame.
ALOHA is as simple as can be, and pays a penalty for it. Because the number of collisions rises rapidly with increased load, the maximum utilization of the channel is only about 18%.
To improve efficiency, a modification of ALOHA, known as slotted ALOHA, was developed. In this scheme, time on the channel is organized into uniform slots whose size equals the frame transmission time. Some central clock or other technique is needed to synchronize all stations. Transmission is permitted to begin only at a slot boundary. Thus, frames that do overlap will do so totally. This increases the maximum utilization of the system to about 37%.

## Slide 4: CSMA/CD Precursors
Carrier Sense Multiple Access (CSMA)
  Station listens to determine if there is another transmission in progress
  If idle, station transmits
  Waits for acknowledgment
  If no acknowledgment, collision is assumed and station retransmits
  Utilization far exceeds ALOHA
Notes: Both ALOHA and slotted ALOHA exhibit poor utilization. Both fail to take advantage of one of the key properties of both packet radio networks and LANs, which is that propagation delay between stations may be very small compared to frame transmission time. Consider the following observations. If the station-to-station propagation time is large compared to the frame transmission time, then, after a station launches a frame, it will be a long time before other stations know about it. During that time, one of the other stations may transmit a frame; the two frames may interfere with each other and neither gets through. Indeed, if the distances are great enough, many stations may begin transmitting, one after the other, and none of their frames get through unscathed. Suppose, however, that the propagation time is small compared to frame transmission time. In that case, when a station launches a frame, all the other stations know it almost immediately. So, if they had any sense, they would not try transmitting until the first station was done. Collisions would be rare because they would occur only when two stations began to transmit almost simultaneously. Another way to look at it is that a short propagation delay provides the stations with better feedback about the state of the network; this information can be used to improve efficiency.
The foregoing observations led to the development of carrier sense multiple access (CSMA). With CSMA, a station wishing to transmit first listens to the medium to determine if another transmission is in progress (carrier sense). If the medium is in use, the station must wait. If the medium is idle, the station may transmit. It may happen that two or more stations attempt to transmit at about the same time. If this happens, there will be a collision; the data from both transmissions will be garbled and not received successfully. To account for this, a station waits a reasonable amount of time after transmitting for an acknowledgment, taking into account the maximum round-trip propagation delay and the fact that the acknowledging station must also contend for the channel to respond. If there is no acknowledgment, the station assumes that a collision has occurred and retransmits.
One can see how this strategy would be effective for networks in which the average frame transmission time is much longer than the propagation time. Collisions can occur only when more than one user begins transmitting within a short time interval (the period of the propagation delay). If a station begins to transmit a frame, and there are no collisions during the time it takes for the leading edge of the packet to propagate to the farthest station, then there will be no collision for this frame because all other stations are now aware of the transmission.
The maximum utilization achievable using CSMA can far exceed that of ALOHA or slotted ALOHA. The maximum utilization depends on the length of the frame and on the propagation time; the longer the frames or the shorter the propagation time, the higher the utilization.

## Slide 5
Notes: With CSMA, an algorithm is needed to specify what a station should do if the
medium is found busy. Three approaches are depicted in Figure 12.2.

## Slide 6: Nonpersistent CSMA
If the medium is idle, transmit; otherwise, go to step 2
If the medium is busy, wait an amount of time drawn from a probability distribution and repeat step 1
Disadvantage:
  Capacity is wasted because the medium will generally remain idle following the end of a transmission even if there are one or more stations waiting to transmit
Notes: One algorithm is nonpersistent CSMA. A station wishing to transmit listens to the medium and obeys the following rules:
If the medium is idle, transmit; otherwise, go to step 2.
If the medium is busy, wait an amount of time drawn from a probability distribution (the retransmission delay) and repeat step 1.
The use of random delays reduces the probability of collisions. To see this, consider that two stations become ready to transmit at about the same time while another transmission is in progress; if both stations delay the same amount of time before trying again, they will both attempt to transmit at about the same time. A problem with nonpersistent CSMA is that capacity is wasted because the medium will generally remain idle following the end of a transmission even if there are one or more stations waiting to transmit.

## Slide 7: 1-Persistent CSMA
Avoids idle channel time
Rules:
    If medium is idle, transmit
    If medium is busy, listen until idle; then transmit immediately
Stations are selfish
If two or more stations are waiting, a collision is guaranteed
Notes: To avoid idle channel time, the 1-persistent protocol can be used. A station wishing to transmit listens to the medium and obeys the following rules:
If the medium is idle, transmit; otherwise, go to step 2.
If the medium is busy, continue to listen until the channel is sensed idle; then transmit immediately.
Whereas nonpersistent stations are deferential, 1-persistent stations are selfish. If two or more stations are waiting to transmit, a collision is guaranteed. Things get sorted out only after the collision.

## Slide 8: P-Persistent CSMA
A compromise to try and reduce collisions and idle time
P-persistent CSMA rules:
    If medium is idle, transmit with probability p, and delay one time unit with probability (1–p)
    If medium is busy, listen until idle and repeat step 1
    If transmission is delayed one time unit, repeat step 1
Issue of choosing effective value of p to avoid instability under heavy load
Notes: A compromise that attempts to reduce collisions, like nonpersistent, and reduce idle time, like 1-persistent, is p-persistent. The rules are:
If the medium is idle, transmit with probability p, and delay one time unit with probability (1 – p). The time unit is typically equal to the maximum propagation delay.
2. If the medium is busy, continue to listen until the channel is idle and repeat step 1.
3. If transmission is delayed one time unit, repeat step 1.

## Slide 9: Value of p?
Have n stations waiting to send
At end of transmission, expected number of stations is np
  If np>1 on average there will be a collision
Repeated transmission attempts mean collisions are likely
Eventually all stations will be trying to send, causing continuous collisions, with throughput dropping to zero
To avoid catastrophe np<1 for expected peaks of n
  If heavy load expected, p must be small
  Smaller p means stations wait longer
Notes: The question arises as to what is an effective value of p. The main problem to avoid is one of instability under heavy load. Consider the case in which n stations have frames to send while a transmission is taking place. At the end of the transmission, the expected number of stations that will attempt to transmit is equal to the number of stations ready to transmit times the probability of transmitting, or np. If np is greater than 1, on average multiple stations will attempt to transmit and there will be a collision. What is more, as soon as all these stations realize that their transmission suffered a collision, they will be back again, almost guaranteeing more collisions. Worse yet, these retries will compete with new transmissions from other stations, further increasing the probability of collision. Eventually, all stations will be trying to send, causing continuous collisions, with throughput dropping to zero. To avoid this catastrophe, np must be less than one for the expected peaks of n; therefore, if a heavy load is expected to occur with some regularity, p must be small. However, as p is made smaller, stations must wait longer to attempt transmission. At low loads, this can result in very long delays. For example, if only a single station desires to transmit, the expected number of iterations of step 1 is 1/p (see Problem 12.2). Thus, if p = 0.1, at low load, a station will wait an average of 9 time units before transmitting on an idle line.

## Slide 10: Description of CSMA/CD
If the medium is idle, transmit; otherwise, go to step 2
If the medium is busy, continue to listen until the channel is idle, then transmit immediately
If a collision is detected, transmit a brief jamming signal to assure that all stations know that there has been a collision and cease transmission
After transmitting the jamming signal, wait a random amount of time, referred to as the backoff, then attempt to transmit again
1.
2.
3.
4.
Notes: CSMA, although more efficient than ALOHA or slotted ALOHA, still has one glaring inefficiency. When two frames collide, the medium remains unusable for the duration of transmission of both damaged frames. For long frames, compared to propagation time, the amount of wasted capacity can be considerable. This waste can be reduced if a station continues to listen to the medium while transmitting. This leads to the following rules for CSMA/CD:
If the medium is idle, transmit; otherwise, go to step 2.
If the medium is busy, continue to listen until the channel is idle, then transmit immediately.
If a collision is detected during transmission, transmit a brief jamming signal to assure that all stations know that there has been a
collision and then cease transmission.
After transmitting the jamming signal, wait a random amount of time, referred to as the backoff, then attempt to transmit again (repeat
from step 1).

## Slide 11: Which Persistence Algorithm?
IEEE 802.3 uses 1-persistent
Both nonpersistent and p-persistent have performance problems
1-persistent seems more unstable than p-persistent
Because of greed of the stations
Wasted time due to collisions is short
With random backoff unlikely to collide on next attempt to send
Notes: An important rule followed in most CSMA/CD systems, including the IEEE standard, is that frames should be long enough to allow collision detection prior to the end of transmission. If shorter frames are used, then collision detection does not occur, and CSMA/CD exhibits the same performance as the less efficient CSMA protocol.
For a CSMA/CD LAN, the question arises as to which persistence algorithm to use. You may be surprised to learn that the algorithm used in the IEEE 802.3 standard is 1-persistent. Recall that both nonpersistent and p-persistent have performance problems. In the nonpersistent case, capacity is wasted because the medium will generally remain idle following the end of a transmission even if there are stations waiting to send. In the p-persistent case, p must be set low enough to avoid instability, with the result of sometimes atrocious delays under light load. The 1-persistent algorithm, which means, after all, that p = 1, would seem to be even more unstable than p-persistent due to the greed of the stations.

## Slide 12: Binary Exponential Backoff
IEEE 802.3 and Ethernet both use binary exponential backoff
A station will attempt to transmit repeatedly in the face of repeated collisions
  On first 10 attempts, mean random delay doubled
  Value then remains the same for 6 further attempts
  After 16 unsuccessful attempts, station gives up and reports error
1-persistent algorithm with binary exponential backoff is efficient over wide range of loads
Backoff algorithm has last-in, first-out effect
Notes: What saves the day is that the wasted time due to collisions is mercifully short (if the frames are long relative to propagation delay), and with random backoff, the two stations involved in a collision are unlikely to collide on their next tries. To ensure that backoff maintains stability, IEEE 802.3 and Ethernet use a technique known as binary exponential backoff. A station will attempt to transmit repeatedly in the face of repeated collisions. For the first 10 retransmission attempts, the mean value of the random delay is doubled. This mean value then remains the same for 6 additional attempts. After 16 unsuccessful attempts, the station gives up and reports an error. Thus, as congestion increases, stations back off by larger and larger amounts to reduce the probability of collision.
The beauty of the 1-persistent algorithm with binary exponential backoff is that it is efficient over a wide range of loads. At low loads, 1-persistence guarantees that a station can seize the channel as soon as it goes idle, in contrast to the non- and p-persistent schemes. At high loads, it is at least as stable as the other techniques. However, one unfortunate effect of the backoff algorithm is that it has a last-in first-out effect; stations with no or few collisions will have a chance to transmit before stations that have waited longer.

## Slide 13
Notes: IEEE 802.3 defines three types of MAC frames. The basic frame is
the original frame format. In addition, to support data link layer protocol encapsulation
within the data portion of the frame, two additional frame types have
been added. A Q-tagged frame supports 802.1Q VLAN capability, as described in
Section 12.3. An envelope frame is intended to allow inclusion of additional prefixes
and suffixes to the data field required by higher-layer encapsulation protocols
such as those defined by the IEEE 802.1 working group (such as Provider Bridges
and MAC Security), ITU-T, or IETF (such as MPLS).
Figure 12.4 depicts the frame format for all three types of frames; the
differences are contained in the MAC Client Data field. Several additional fields
encapsulate the frame to form an 802.3 packet. The fields are as follows:
• Preamble: A 7-octet pattern of alternating 0s and 1s used by the receiver to
establish bit synchronization.
• Start Frame Delimiter (SFD): The sequence 10101011, which that delimits the
actual start of the frame and enables the receiver to locate the first bit of the
frame.
• Destination Address (DA): Specifies the station(s) for which the frame is
intended. It may be a unique physical address, a multicast address, or a broadcast
address.
• Source Address (SA): Specifies the station that sent the frame.
• Length/Type: Takes on one of two meanings, depending on its numeric value.
If the value of this field is less than or equal to 1500 decimal, then the Length/
Type field indicates the number of MAC Client Data octets contained in the
subsequent MAC Client Data field of the basic frame (length interpretation).
If the value of this field is greater than or equal to 1536 decimal then the
Length/Type field indicates the nature of the MAC client protocol (Type
interpretation). The Length and Type interpretations of this field are mutually
exclusive.
• MAC Client Data: Data unit supplied by LLC. The maximum size of this field
is 1500 octets for a basic frame, 1504 octets for a Q-tagged frame, and 1982
octets for an envelope frame.
• Pad: Octets added to ensure that the frame is long enough for proper CD
operation.
• Frame Check Sequence (FCS): A 32-bit cyclic redundancy check, based on all
fields except preamble, SFD, and FCS.
• Extension: This field is added, if required for 1-Gbps half-duplex operation.
The extension field is necessary to enforce the minimum carrier event duration
on the medium in half-duplex mode at an operating speed of 1 Gbps.

## Slide 14: 100BASE-X
Uses a unidirectional data rate 100 Mbps over single twisted pair or optical fiber link
Encoding scheme same as FDDI
  4B/5B-NRZI
Two physical medium specifications
100BASE-TX
Uses two pairs of twisted-pair cable
100BASE-FX
Uses two optical fiber cables
STP and Category 5 UTP allowed
MTL-3 signaling scheme is used
Convert 4B/5B-NRZI code group into optical signals
Notes: For all of the transmission media specified under 100BASE-X, a unidirectional data rate of 100 Mbps is achieved transmitting over a single link (single twisted pair, single optical fiber). For all of these media, an efficient and effective signal encoding scheme is required. The one chosen is referred to as 4B/5B-NRZI. This scheme is further modified for each option. See Appendix 12A for a description.
The 100BASE-X designation includes two physical medium specifications, one for twisted pair, known as 100BASE-TX, and one for optical fiber, known as 100-BASE-FX.
100BASE-TX makes use of two pairs of twisted-pair cable, one pair used for transmission and one for reception. Both STP and Category 5 UTP are allowed. The MTL-3 signaling scheme is used (described in Appendix 12A).
100BASE-FX makes use of two optical fiber cables, one for transmission and one for reception. With 100BASE-FX, a means is needed to convert the 4B/5B-NRZI code group stream into optical signals. The technique used is known as intensity modulation. A binary 1 is represented by a burst or pulse of light; a binary 0 is represented by either the absence of a light pulse or a light pulse at very low intensity.

## Slide 15: Full Duplex Operation
Traditional Ethernet half duplex
Using full-duplex, station can transmit and receive simultaneously
100-Mbps Ethernet in full-duplex mode, giving a theoretical transfer rate of 200 Mbps
Stations must have full-duplex adapter cards
And must use switching hub
  Each station constitutes separate collision domain
  CSMA/CD algorithm no longer needed
  802.3 MAC frame format used
Notes: A traditional Ethernet is half duplex: a station can either transmit or receive a frame, but it cannot do both simultaneously. With full-duplex operation, a station can transmit and receive simultaneously. If a 100-Mbps Ethernet ran in full-duplex mode, the theoretical transfer rate becomes 200 Mbps.
Several changes are needed to operate in full-duplex mode. The attached stations must have full-duplex rather than half-duplex adapter cards. The central point in the star wire cannot be a simple multiport repeater but rather must be a switching hub. In this case each station constitutes a separate collision domain. In fact, there are no collisions and the CSMA/CD algorithm is no longer needed. However, the same 802.3 MAC frame format is used and the attached stations can continue to execute the CSMA/CD algorithm, even though no collisions can ever be detected.

## Slide 16: Gigabit Ethernet
Family of standards
  1 Gbps
  10 Gbps
  40 Gbps
  100 Gbps
Applications?
Notes: In late 1995, the IEEE 802.3 committee formed a High-Speed Study Group to
investigate means for conveying packets in Ethernet format at speeds in the gigabits
per second range. The strategy for Gigabit Ethernet is the same as that for Fast
Ethernet. While defining a new medium and transmission specification, Gigabit
Ethernet retains the CSMA/CD protocol and Ethernet format of its 10-Mbps and 100-
Mbps predecessors. It is compatible with 100BASE-T and 10BASE-T, preserving
a smooth migration path. As more organizations moved to 100BASE-T, putting huge
traffic loads on backbone networks, demand for Gigabit Ethernet intensified.
The 1000-Mbps specification calls for the same CSMA/CD
frame format and MAC protocol as used in the 10-Mbps and 100-Mbps version
of IEEE 802.3. For shared-medium hub operation (Figure 11.11b), there are two
enhancements to the basic CSMA/CD scheme:
Carrier extension appends a set of special symbols to the end of short MAC frames so that the resulting block is at least 4096 bit-times in duration, up from the minimum 512 bit-times imposed at 10 and 100 Mbps. This is so that the frame length of a transmission is longer than the propagation time at 1 Gbps.
Frame bursting: This feature allows for multiple short frames to be transmitted consecutively, up to a limit, without relinquishing control for CSMA/CD between frames. Frame bursting avoids the overhead of carrier extension when a single station has a number of small frames ready to send.
With a switching hub (Figure 11.11c), which provides dedicated access to the
medium, the carrier extension and frame bursting features are not needed. This is
because data transmission and reception at a station can occur simultaneously without
interference and with no contention for a shared medium.

## Slide 17
Notes: The current 1-Gbps specification for IEEE 802.3 includes the following physical layer alternatives (Figure 12.5):
1000BASE-SX: This short-wavelength option supports duplex links of up to 275 m using 62.5-µm multimode or up to 550 m using 50-µm multimode fiber. Wavelengths are in the range of 770 to 860 nm.
1000BASE-LX: This long-wavelength option supports duplex links of up to 550 m of 62.5-µm or 50-µm multimode fiber or 5 km of 10-µm single-mode fiber. Wavelengths are in the range of 1270 to 1355 nm.
1000BASE-CX: This option supports 1-Gbps links among devices located within a single room or equipment rack, using copper jumpers (specialized shielded twisted-pair cable that spans no more than 25 m). Each link is composed of a separate shielded twisted pair running in each direction.
1000BASE-T: This option makes use of four pairs of Category 5 unshielded twisted pair to support devices over a range of up to 100 m, transmitting and receiving on all four pairs at the same time, with echo cancelation circuitry.
The signal encoding scheme used for the first three Gigabit Ethernet options just listed is 8B/10B, which is described in Appendix 12A. The signal-encoding scheme used for 1000BASE-T is 4D-PAM5, a complex scheme whose description is beyond our scope.

## Slide 18: 10Gbps Ethernet
Growing interest in 10Gbps Ethernet
  High-speed backbone use
  Future wider deployment
Alternative to ATM and other WAN technologies
Uniform technology for LAN, MAN, or WAN
Advantages of 10Gbps Ethernet
  No expensive, bandwidth-consuming conversion between Ethernet packets and ATM cells
  IP and Ethernet together offers QoS and traffic policing approach ATM
  Have a variety of standard optical interfaces
Notes: With gigabit products still fairly new, attention has turned in the past several years to a 10-Gbps Ethernet capability. The principle driving requirement for 10 Gigabit Ethernet is the increase in Internet and intranet traffic. A number of factors contribute to the explosive growth in both Internet and intranet traffic:
An increase in the number of network connections
An increase in the connection speed of each end-station (e.g., 10 Mbps users moving to 100 Mbps, analog 56-kbps users moving to DSL and cable modems)
An increase in the deployment of bandwidth-intensive applications such as high-quality video
An increase in Web hosting and application hosting traffic
Initially network managers will use 10-Gbps Ethernet to provide high-speed, local backbone interconnection between large-capacity switches. As the demand for bandwidth increases, 10-Gbps Ethernet will be deployed throughout the entire network and will include server farm, backbone, and campuswide connectivity. This technology enables Internet service providers (ISPs) and network service providers (NSPs) to create very high-speed links at a low cost, between co-located, carrier-class switches and routers.
The technology also allows the construction of metropolitan area networks (MANs) and WANs that connect geographically dispersed LANs between campuses or points of presence (PoPs). Thus, Ethernet begins to compete with ATM and other wide area transmission and networking technologies. In most cases where the customer requirement is data and TCP/IP transport, 10-Gbps Ethernet provides substantial value over ATM transport for both network end users and service providers:
No expensive, bandwidth-consuming conversion between Ethernet packets and ATM cells is required; the network is Ethernet, end to end.
The combination of IP and Ethernet offers quality of service and traffic policing capabilities that approach those provided by ATM, so that advanced traffic engineering technologies are available to users and providers.
A wide variety of standard optical interfaces (wavelengths and link distances) have been specified for 10-Gbps Ethernet, optimizing its operation and cost for LAN, MAN, or WAN applications.

## Slide 19
Notes: Figure 12.6 illustrates potential uses of 10-Gbps Ethernet. Higher-capacity backbone pipes will help relieve congestion for workgroup switches, where Gigabit Ethernet uplinks can easily become overloaded, and for server farms, where 1-Gbps network interface cards are already in widespread use.
The goal for maximum link distances cover a range of applications: from 300 m to 40 km. The links operate in full-duplex mode only, using a variety of optical fiber physical media.

## Slide 20
Notes: Four physical layer options are defined for 10-Gbps Ethernet (Figure 12.7). The first three of these have two suboptions: an "R" suboption and a "W" suboption. The R designation refers to a family of physical layer implementations that use a signal encoding technique known as 64B/66B, described in Appendix 12A. The R implementations are designed for use over dark fiber, meaning a fiber optic cable that is not in use and that is not connected to any other equipment. The W designation refers to a family of physical layer implementations that also use 64B/66B signaling but that are then encapsulated to connect to SONET equipment.
The four physical layer options are
10GBASE-S (short): Designed for 850-nm transmission on multimode fiber. This medium can achieve distances up to 300 m. There are 10GBASE-SR and 10GBASE-SW versions.
10GBASE-L (long): Designed for 1310-nm transmission on single-mode fiber. This medium can achieve distances up to 10 km. There are 10GBASE-LR and 10GBASE-LW versions.
10GBASE-E (extended): Designed for 1550-nm transmission on single-mode fiber. This medium can achieve distances up to 40 km. There are 10GBASE-ER and 10GBASE-EW versions.
10GBASE-LX4: Designed for 1310-nm transmission on single-mode or multimode fiber. This medium can achieve distances up to 10 km. This medium uses wavelength-division multiplexing (WDM) to multiplex the bit stream across four light waves.

## Slide 21: 100-Gbps Ethernet
Preferred technology for wired LAN
Preferred carrier for bridging wireless technologies into local Ethernet networks
Cost-effective, reliable and interoperable
Popularity of Ethernet technology:
  Availability of cost-effective products
  Reliable and interoperable network products
  Variety of vendors
Notes: Ethernet is widely deployed and is the preferred technology for wired local area networking. Ethernet dominates enterprise LANs, broadband access, data center networking, and has also become popular for communication across metropolitan and even wide area networks. Further, it is now the preferred carrier wire line vehicle for bridging wireless technologies, such as WiFi and WiMAX, into local Ethernet networks.
This popularity of Ethernet technology is due to the availability of cost-effective, reliable, and interoperable networking products from a variety of vendors. The development of converged and unified communications, the evolution of massive server farms, and the continuing expansion of VoIP, TVoIP, and Web 2.0 applications have driven the need for ever faster Ethernet switches. The following are market drivers for 100-Gbps Ethernet:
Data center/Internet media providers: To support the growth of Internet multimedia content and Web applications, content providers have been expanding data centers, pushing 10-Gbps Ethernet to its limits. Likely to be high-volume early adopters of 100-Gbps Ethernet.
Metro-Video/Service Providers: Video on demand has been driving a new generation of 10-Gbps Ethernet metropolitan/core network buildouts. Likely to be high-volume adopters in the medium term.
Enterprise LANs: Continuing growth in convergence of voice/video/data and in unified communications is driving up network switch demands. However, most enterprises still rely on 1-Gbps or a mix of 1-Gbps and 10-Gbps Ethernet, and adoption of 100-Gbps Ethernet is likely to be slow.
Internet exchanges/ISP (Internet Service Provider) core routing: With the massive amount of traffic flowing through these nodes, these installations are likely to be early adopters of 100-Gbps Ethernet.

## Slide 22: Table 12.3 Media Options for 40-Gbps and 100-Gbps Ethernet
Naming nomenclature:
Copper: K = backplane; C = cable assembly
Optical: S = short reach (100m); L - long reach (10 km); E = extended long reach (40 km)
Coding scheme: R = 64B/66B block coding
Final number: number of lanes (copper wires or fiber wavelengths)
Notes: IEEE 802.3ba specifies three types of transmission media (Table 12.3): copper backplane, twisted pair, and optical fiber. For copper media, four separate physical lanes are specified. For optical fiber, either 4 or 10 wavelength lanes are specified, depending on data rate and distance.

## Slide 23: Summary
Traditional Ethernet
  IEEE 802.3 medium access control
  IEEE 802.3 10-Mbps specifications (Ethernet)
IEEE 802.1Q VLAN standard
High-speed Ethernet
  IEEE 802.3 100-Mbps specifications (Fast Ethernet)
  Gigabit Ethernet
  10-Gbps Ethernet
  100-Gbps Ethernet
Notes: Chapter 12 summary.