## Slide 1: Data and Computer Communications
Tenth Edition
by William Stallings
Notes: “Data and Computer Communications”, 10/e, by William Stallings, Chapter 25 “Internet Multimedia Support”.

## Slide 2: Internet Multimedia Support
Chapter 25
Notes: An in-depth discussion of multimedia applications is well beyond the
scope of this book. In this chapter, we focus on a few key topics. First, we
examine some of the key characteristics of real-time traffic. Next we look at
SIP (Session Initiation Protocol) and its use to support voice over IP. Finally,
we examine the Real-Time Transport Protocol.

## Slide 3
Notes: Figure 25.1 illustrates a typical real-time environment. Here, a server is generating
audio to be transmitted at 64 kbps. The digitized audio is transmitted in packets
containing 160 octets of data, so that one packet is issued every 20 ms. These packets
are passed through an internet and delivered to a multimedia PC, which plays
the audio in real time as it arrives. However, because of the variable delay imposed
by the Internet, the interarrival times between packets are not maintained at a fixed
20 ms at the destination. To compensate for this, the incoming packets are buffered,
delayed slightly, and then released at a constant rate to the software that generates
the audio.
The compensation provided by the delay buffer is limited. To understand this,
we need to define the concept of delay jitter , which is the maximum variation in
delay experienced by packets in a single session. For example, if the minimum endto-
end delay seen by any packet is 1 ms and the maximum is 6 ms, then the delay
jitter
is 5 ms. As long as the time delay buffer delays incoming packets by at least
5 ms, then the output of the buffer will include all incoming packets. However, if
the buffer delayed packets only by 4 ms, then any incoming packets that had experienced
a relative delay of more than 4 ms (an absolute delay of more than 5 ms)
would have to be discarded so as not to be played back out of order.

## Slide 4
Notes: The description of real-time traffic so far implies a series of equal-size packets
generated at a constant rate. This is not always the profile of the traffic. Figure 25.2
illustrates some of the common possibilities:
• Continuous data source: Fixed-size packets are generated at fixed intervals.
This characterizes applications that constantly generate data, have few redundancies,
and that are too important to compress in a lossy way. Examples are
air traffic control radar and real-time simulations.
• On/off source: The source alternates between periods when fixed-size packets
are generated at fixed intervals and periods of inactivity. A voice source, such
as in telephony or audio conferencing, fits this profile.
• Variable packet size: The source generates variable-length packets at uniform
intervals. An example is digitized video in which different frames may experience
different compression ratios for the same output quality level.

## Slide 5: Requirements for Real-Time Communication
Low jitter
Low latency
Ability to easily integrate non-real-time and real-time services
Adaptable to dynamically changing network and traffic conditions
High effective capacity utilization
Good performance for large networks and large numbers of connections
Modest buffer requirements within the network
Low overhead in header bits per packet
Low processing overhead per packet within the network and at the end system
Notes: [ARAS94] lists the following as desirable properties for real-time communication:
• Low jitter
• Low latency
• Ability to easily integrate non-real-time and real-time services
• Adaptable to dynamically changing network and traffic conditions
• Good performance for large networks and large numbers of connections
• Modest buffer requirements within the network
• High effective capacity utilization
• Low overhead in header bits per packet
• Low processing overhead per packet within the network and at the end system
These requirements are difficult to meet in a wide area IP-based network or
internet. Neither TCP (Transport Control Protocol) nor UDP (User Datagram
Protocol) by itself is appropriate. We will see that RTP provides a reasonable foundation
for addressing these issues.

## Slide 6: Hard Versus Soft Real-Time Applications
Soft
Can tolerate the loss of some portion of the communicated data
Hard
Have zero loss tolerance
Impose fewer requirements on the network, therefore permissible to focus on maximizing network utilization, even at the cost of some lost or misordered packets
A deterministic upper bound on jitter and high reliability takes precedence over network utilization considerations
Notes: A distinction needs to be made between hard and soft real-time communication
applications. Soft real-time applications can tolerate the loss of some portion of the
communicated data, while hard real-time applications have zero loss tolerance. In
general, soft real-time applications impose fewer requirements on the network, and
it is therefore permissible to focus on maximizing network utilization, even at the
cost of some lost or misordered packets. In hard real-time applications, a deterministic
upper bound on jitter and high reliability takes precedence over network
utilization considerations.

## Slide 7: Voice Over IP (VoIP)
The transmission of speech across IP-based network
Works by encoding voice information into a digital format, which can be carried across IP networks in discrete packets
Has two main advantages over traditional telephony:
  Is usually cheaper to operate than an equivalent telephone system with a PBX and conventional telephone network service
  Readily integrates with other services, such as combining Web access with telephone features through a single PC or terminal
Notes: We have referred a number of times in this text to the trend toward the convergence
of data, voice, and video transmission using IP-based networks. This convergence
enables the delivering of advanced services at lower cost for residential users, business
customers of varying sizes, and service providers. One of the key technologies
underlying this convergence is VoIP (voice over IP), which has become increasingly
prevalent in organizations of all sizes.
In essence, VoIP is the transmission of speech across IP-based network. VoIP
works by encoding voice information into a digital format, which can be carried
across IP networks in discrete packets. VoIP has two main advantages over traditional
telephony.
1. A VoIP system is usually cheaper to operate than an equivalent telephone system
with a PBX and conventional telephone network service. There are several reasons
for this. Whereas traditional telephone networks allocate dedicated circuits
for voice communications using circuit switching, VoIP uses packet switching,
allowing the sharing of transmission capacity. Further, packetized voice transmission
fits well in the framework of the TCP/IP protocol suite, enabling the use
of application- and transport-level protocols to support communications.
2. VoIP readily integrates with other services, such as combining Web access
with telephone features through a single PC or terminal.

## Slide 8: VoIP Signaling
Before voice can be transferred using VoIP a call must be placed
The calling user supplies the phone number of a URI which then triggers a set of protocol interactions resulting in the placement of the call
The heart of the call placement process is the Session Initiation Protocol (SIP)
Notes: Before voice can be transferred using VoIP, a call must be placed. In a traditional
phone network, the caller enters the digits of the called number. The telephone
number is processed by the provider’s signaling system to ring the called number.
With VoIP, the calling user (program or individual) supplies the phone number of
a URI (Universal Resource Indicator, a form of URL), which then triggers a set of
protocol interactions resulting in the placement of the call.
The heart of the call placement process for VoIP is the Session Initiation
Protocol (SIP). SIP supports not only VoIP but also many multimedia applications.
Section 25.3 discusses SIP.

## Slide 9
Notes: Once a called party responds, a logical connection is established between the two
parties (or more for a conference call), and voice data may be exchanged in both
directions. Figure 25.3 illustrates the basic flow of voice data in one direction in a
VoIP system. On the sending side, the analog voice signal is first converted into a
digital bit stream and then segmented into packets. The packetization is performed,
typically, by RTP. This protocol includes mechanisms for labeling the packets so
that they can be reassembled in the proper order at the receiving end, plus a buffering
function to smooth out reception and deliver the voice data in a continuous
flow. The RTP packets are then transmitted across the Internet or a private internet
using the User Datagram Protocol and IP protocols.
At the receiving end, the process is reversed. The packet payloads are reassembled
by RTP and put into the proper order. The data are then decompressed
and the digitized voice is processed by a digital-to-analog converter to produce analog
signals for the receiver’s telephone or headset speaker.

## Slide 10
Notes: Ultimately, VoIP using IP-based networks may replace the public circuit-switched
networks in use today. But for the foreseeable future, VoIP must coexist with the
existing telephony infrastructure. Figure 25.4 suggests some of the key elements
involved in the coexistence of the older and newer technologies.

## Slide 11: VoIP Context
The deployment of the VoIP infrastructure has been accompanied by a variety of end-user products including:
  Traditional telephone handset
  Conferencing units
  Mobile units
  Softphone
  Infrastructure equipment developed to support VoIP:
  IP PBX
  Media gateway
Notes: The deployment of the VoIP infrastructure has been accompanied by a variety
of end-user products including the following:
• Traditional telephone handset: These corded or cordless units function much
like a traditional telephone but are VoIP capable. They typically have many
additional features, making use of a screen, and providing capabilities found
in smart mobile phones.
• Conferencing units: These provide the same basic service of conventional
conference calling phone systems. These units also allow users to coordinate
other data communications services, such as text, graphics, video, and
whiteboarding.
• Mobile units: Smart phones and other cell phones with VoIP capability can tie
directly into a VoIP network without going through any kind of gateway system.
• Softphone: The term softphone refers to software operating on a PC that
implements VoIP. Typically, the PC is configured with a headset or a telephone
that makes use of a USB connection to the PC.
There is a wide variety of infrastructure equipment developed to support
VoIP. Here we mention two noteworthy types:
• IP PBX: The IP PBX is designed to support digital and analog phones and
connect to IP-based networks using VoIP, as well as provide if needed a connection
to the public switched telephone network using traditional technology.
• Media gateway: The media gateway connects different physical networks in
order to provide end-to-end connectivity. An important type of media gateway
connects a VoIP network to a circuit-switched telephone network, providing
the necessary conversion and signaling.
The VoIP environment continues to evolve with a large number of products
being developed for service providers, businesses, and residential/personal users.

## Slide 12: Session Initiation Protocol (SIP)
Defined in RFC 3261
An application level control protocol for setting up, modifying, and terminating real-time sessions between participants over an IP data network
Key driving force is to enable Internet telephony
Can support any type of single media or multimedia session, including teleconferencing
Notes: The Session Initiation Protocol (SIP), defined in RFC 3261, is an application-level
control protocol for setting up, modifying, and terminating real-time sessions
between participants over an IP data network. The key driving force behind SIP
is to enable Internet telephony, also referred to as voice over IP (VoIP). SIP can
support any type of single media or multimedia session, including teleconferencing.
SIP supports five facets of establishing and terminating multimedia
communications:
• User location: Users can move to other locations and access their telephony or
other application features from remote locations.
• User availability: Determination of the willingness of the called party to
engage in communications.
• User capabilities: Determination of the media and media parameters to be
used.
• Session setup: Set up point-to-point and multiparty calls, with agreed session
parameters.
• Session management: Including transfer and termination of sessions, modifying
session parameters, and invoking services.
SIP employs design elements developed for earlier protocols. SIP is based on
an HTTP-like request/response transaction model. Each transaction consists of a
client request that invokes a particular method, or function, on the server and at
least one response. SIP uses most of the header fields, encoding rules, and status
codes of HTTP. This provides a readable text-based format for displaying information.
SIP also uses concepts similar to the recursive and iterative searches of DNS
(Domain Name System). SIP incorporates the use of a Session Description Protocol
(SDP), which defines session content using a set of types similar to those used in
MIME (Multipurpose Internet Mail Extension).

## Slide 13: SIP Components and Protocols
Client/server
A client is any network element that sends SIP requests and receives SIP responses
A server is a network element that receives requests in order to service them and sends back responses to those requests
Individual network elements
User agent
Redirect server
Proxy server
Registrar
Location service
Presence server
Can be viewed of consisting of components defined on two dimensions:
Notes: An SIP network can be viewed of consisting of components defined on two dimensions:
client/server and individual network elements. RFC 3261 defines client and
server as follows:
• Client: A client is any network element that sends SIP requests and receives
SIP responses. Clients may or may not interact directly with a human user.
User agent clients and proxies are clients.
• Server: A server is a network element that receives requests in order to service
them and sends back responses to those requests. Examples of servers are
proxies, user agent servers, redirect servers, and registrars.
The individual elements of a standard SIP network are as follows:
• User Agent: Resides in every SIP end station. It acts in two roles:
—User agent client (UAC): Issues SIP requests
—User agent server (UAS): Receives SIP requests and generates a response
that accepts, rejects, or redirects the request
• Redirect Server: Used during session initiation to determine the address of
the called device. The redirect server returns this information to the calling
device, directing the UAC to contact an alternate URI. This is analogous to
iterative searches in DNS.
• Proxy Server: An intermediary entity that acts as both a server and a client
for the purpose of making requests on behalf of other clients. A proxy server
primarily plays the role of routing, which means its job is to ensure that a
request is sent to another entity closer to the targeted user. Proxies are also
useful for enforcing policy (e.g., making sure a user is allowed to make a call).
A proxy interprets, and, if necessary, rewrites specific parts of a request message
before forwarding it. This is analogous to recursive searches in DNS.
• Registrar: A server that accepts REGISTER requests and places the information
it receives (the SIP address and associated IP address of the registering
device) in those requests into the location service for the domain it handles.
• Location Service: A location service is used by a SIP redirect or proxy server
to obtain information about a callee’s possible location(s). For this purpose,
the location service maintains a database of SIP-address/IP-address mappings.
• Presence Server: Accepts, stores, and distributes presence information. The
presence server has two distinct sets of clients:
—Presentities (producers of information) provide presence information to the
server to be stored and distributed.
—Watchers (consumers of information) receive presence information from
the server.
The various servers are defined in RFC 3261 as logical devices. They may be
implemented as separate servers configured on the Internet or they may be combined
into a single application that resides in a physical server.

## Slide 14
Notes: Figure 25.5 shows how some of the SIP components relate to one another and
the protocols that are employed. A user agent acting as a client (in this case UAC
alice) uses SIP to set up a session with a user agent that will act as a server (in this
case UAS bob). The session initiation dialogue uses SIP and involves one or more
proxy servers to forward requests and responses between the two user agents. The
user agents also make use of the Session Description Protocol, which is used to
describe the media session.
The proxy servers may also act as redirect servers as needed. If redirection is
done, a proxy server will need to consult the location service database, which may
be collocated with a proxy server or not. The communication between the proxy
server and the location service is beyond the scope of the SIP standard. DNS is also
an important part of SIP operation. Typically, a UAC will make a request using the
domain name of the UAS, rather than an IP address. A proxy server will need to
consult a DNS server to find a proxy server for the target domain.
SIP typically runs on top of UDP for performance reasons, and provides its
own reliability mechanisms, but may also use TCP. If a secure, encrypted transport
mechanism is desired, SIP messages may alternatively be carried over the Transport
Layer Security (TLS) protocol, described in Chapter 27.
Associated with SIP is the Session Description Protocol, defined in RFC 4566.
SIP is used to invite one or more participants to a session, while the SDP-encoded
body of the SIP message contains information about what media encodings (e.g.,
voice, video) the parties can and will use. Once this information is exchanged and
acknowledged, all participants are aware of the participants’ IP addresses, available
transmission capacity, and media type. Then data transmission begins, using
an appropriate transport protocol. Typically, the Real-Time Transport Protocol
(RTP), described subsequently, is used. Throughout the session, participants can
make changes to session parameters, such as new media types or new parties to the
session, using SIP messages.

## Slide 15: SIP URI
A resource within a SIP network is identified by a Uniform Resource Identifier
SIP URI’s have a format based on e-mail address formats
If secure transmission is required “sips” is used
  Transported over TLS
Examples of communications resources include the following:
A user of an online service
An appearance on a multiline phone
A mailbox on a messaging system
A telephone number at a gateway service
A group in an organization
Notes: A resource within a SIP network is identified by a Uniform Resource Identifier
(URI). Examples of communications resources include the following:
• A user of an online service
• An appearance on a multiline phone
• A mailbox on a messaging system
• A telephone number at a gateway service
• A group (such as “sales” or “helpdesk”) in an organization
SIP URIs have a format based on e-mail address formats, namely user@
domain. There are two common schemes. An ordinary SIP URI is of the form
sip: bob@biloxi.com
The URI may also include a password, port number, and related parameters.
If secure transmission is required, “sip:” is replaced by “sips:”. In the latter case, SIP
messages are transported over TLS.

## Slide 16: Session Description Protocol (SDP)
Describes the content of sessions, including telephony, Internet radio, and multimedia applications
Includes information about:
Media streams
Addresses
Ports
Payload types
Start and stop times
Originator
Notes: The Session Description Protocol (SDP) describes the content of sessions, including
telephony, Internet radio, and multimedia applications. SDP includes information
about the following [SCHU99]:
• Media streams: A session can include multiple streams of differing content.
SDP currently defines audio, video, data, control, and application as stream
types, similar to the MIME types used for Internet mail (Table 24.1).
• Addresses: Indicates the destination addresses, which may be a multicast
address, for a media stream.
• Ports: For each stream, the UDP port numbers for sending and receiving are
specified.
• Payload types: For each media stream type in use (e.g., telephony), the payload
type indicates the media formats that can be used during the session.
• Start and stop times: These apply to broadcast sessions, like a television or
radio program. The start, stop, and repeat times of the session are indicated.
• Originator: For broadcast sessions, the originator is specified, with contact
information. This may be useful if a receiver encounters technical
difficulties.

## Slide 17: Real-Time Transport Protocol (RTP)
Defined in RFC 3550
Best suited to soft real-time communication
Lacks the necessary mechanisms to support hard real-time traffic
Two protocols that make up RTP are:
RTP
Data transfer protocol
RTCP
Control protocol
Notes: The most widely used transport-level protocol is TCP. Although TCP has proven
its value in supporting a wide range of distributed applications, it is not suited
for use with real-time distributed applications. By a real-time distributed application,
we mean one in which a source is generating a stream of data at a constant
rate, and one or more destinations must deliver that data to an application at
the same constant rate. Examples of such applications include audio and video
conferencing, live video distribution (not for storage but for immediate play),
shared workspaces, remote medical diagnosis, telephony, command and control
systems, distributed interactive simulations, games, and real-time monitoring. A
number of features of TCP disqualify it for use as the transport protocol for such
applications:
1. TCP is a point-to-point protocol that sets up a connection between two endpoints.
Therefore, it is not suitable for multicast distribution.
2. TCP includes mechanisms for retransmission of lost segments, which then
arrive out of order. Such segments are not usable in most real-time applications.
3. TCP contains no convenient mechanism for associating timing information
with segments, which is another real-time requirement.
The other widely used transport protocol, UDP, does not exhibit the first two
characteristics listed but, like TCP, does not provide timing information. By itself,
UDP does not provide any general-purpose tools useful for real-time applications.
Although each real-time application could include its own mechanisms for
supporting real-time transport, there are a number of common features that warrant
the definition of a common protocol. A protocol designed for this purpose is
the Real-Time Transport Protocol (RTP), defined in RFC 3550. RTP is best suited
to soft real-time communication. It lacks the necessary mechanisms to support hard
real-time traffic.
This section provides an overview of RTP. We begin with a discussion of realtime
transport requirements. Next, we examine the philosophical approach of RTP.
The remainder of the section is devoted to the two protocols that make up RTP:
The first is simply called RTP and is a data transfer protocol; the other is a control
protocol known as RTCP (RTP Control Protocol).

## Slide 18
Notes: Figure 25.6 illustrates the manner in which RTP realizes the principle of integrated
layer processing. RTP is designed to run on top of a connectionless transport
protocol such as UDP. UDP provides the basic port addressing functionality of the
transport layer. RTP contains further transport-level functions, such as sequencing.
However, RTP by itself is not complete. It is completed by modifications and/or
additions to the RTP headers to include application-layer functionality. The figure
indicates that several different standards for encoding video data can be used in
conjunction with RTP for video transmission.

## Slide 19: RTP Concepts
RTP supports the transfer of real-time data among a number of participants in a session
  A session is a logical association among two or more RTP entities that is maintained for the duration of the data transfer
    Defined by:
      RTP port number
      RTCP port number
      Participant IP addresses
Notes: RTP supports the transfer of real-time data among a number
of participants in a session. A session is simply a logical association among two or
more RTP entities that is maintained for the duration of the data transfer. A session
is defined by the following:
• RTP port number: The destination port address is used by all participants
for RTP transfers. If UDP is the lower layer, this port number appears in the
Destination Port field (see Figure 2.6) of the UDP header.
• RTCP port number: The destination port address is used by all participants
for RTCP transfers.
• Participant IP addresses: This can either be a multicast IP address, so that the
multicast group defines the participants, or a set of unicast IP addresses.
Although RTP can be used for unicast real-time transmission, its strength lies
in its ability to support multicast transmission. For this purpose, each RTP data unit
includes a source identifier that identifies which member of the group generated the
data. It also includes a timestamp so that the proper timing can be re-created on the
receiving end using a delay buffer. RTP also identifies the payload format of the
data being transmitted.

## Slide 20: RTP Relays
A relay operating at a given protocol layer is an intermediate system that acts as both a destination and a source in a data transfer
Two kinds:
  Mixer
  Translator
Notes: RTP allows the use of two kinds of RTP relays: translators and mixers. First
we need to define the concept of relay. A relay operating at a given protocol layer
is an intermediate system that acts as both a destination and a source in a data
transfer. For example, suppose that system A wishes to send data to system B but
cannot do so directly. Possible reasons are that B may be behind a firewall or B
may not be able to use the format transmitted by A. In such a case, A may be able
to send the data to an intermediate relay R. R accepts the data unit, makes any
necessary changes or performs any necessary processing, and then transmits the
data to B.

## Slide 21: Mixer
    RTP relay that receives streams of RTP packets from one or more sources, combines these streams, and forwards a new RTP packet stream to one or more destinations
    May change the data format or simply perform the mixing function
    Provides the timing information in the combined packet stream and identifies itself as the source of synchronization
Notes: A mixer is an RTP relay that receives streams of RTP packets from one or
more sources, combines these streams, and forwards a new RTP packet stream to
one or more destinations. The mixer may change the data format or simply perform
the mixing function. Because the timing among the multiple inputs is not typically
synchronized, the mixer provides the timing information in the combined packet
stream and identifies itself as the source of synchronization.
An example of the use of a mixer is to combine a number of on/off sources
such as audio. Suppose that a number of systems are members of an audio session
and each generates its own RTP stream. Most of the time only one source is
active, although occasionally more than one source will be “speaking” at the same
time. A new system may wish to join the session, but its link to the network may
not be of sufficient capacity to carry all of the RTP streams. Instead, a mixer could
receive all of the RTP streams, combine them into a single stream, and retransmit
that stream to the new session member. If more than one incoming stream is active
at one time, the mixer would simply sum their PCM values. The RTP header generated
by the mixer includes the identifier(s) of the source(s) that contributed to the
data in each packet.

## Slide 22: Translator
A simple device that produces one or more outgoing RTP packets for each incoming RTP packet
May change the format of the data in the packet or use a different lower-level protocol suite to transfer from one domain to another
Examples of translator use include:
  Convert a video to a lower quality format
  An application-level firewall prevents the forwarding of RTP packets
  Replicate an incoming multicast RTP packet and send it to a number of unicast destinations
Notes: The translator is a simple device that produces one or more outgoing RTP
packets for each incoming RTP packet. The translator may change the format of the
data in the packet or use a different lower-level protocol suite to transfer from one
domain to another. Examples of translator use include the following:
• A potential recipient may not be able to handle a high-speed video signal used
by the other participants. The translator converts the video to a lower-quality
format requiring a lower data rate.
• An application-level firewall may prevent the forwarding of RTP packets.
Two translators are used, one on each side of the firewall, with the outside
one tunneling all multicast packets received through a secure connection to
the translator inside the firewall. The inside translator then sends out RTP
packets to a multicast group protected by the firewall.
• A translator can replicate an incoming multicast RTP packet and send it to a
number of unicast destinations.

## Slide 23
Notes: Each RTP packet includes a fixed header and may also
include additional application-specific header fields. Figure 25.7 shows the fixed
header. The first 12 octets (shaded portion) are always present and consist of the
following fields:
• Version (2 bits): Current version is 2.
• Padding (1 bit): Indicates whether padding octets appear at the end of the
payload. If so, the last octet of the payload contains a count of the number of
padding octets. Padding is used if the application requires that the payload be
an integer multiple of some length, such as 32 bits.
• Extension (1 bit): If set, the fixed header is followed by exactly one extension
header, which is used for experimental extensions to RTP.
• CSRC Count (4 bits): The number of CSRC (contributing source) identifiers
that follow the fixed header.
• Marker (1 bit): The interpretation of the marker bit depends on the payload
type; it is typically used to indicate a boundary in the data stream. For video, it
is set to mark the end of a frame. For audio, it is set to mark the beginning of
a talk spurt.
• Payload Type (7 bits): Identifies the format of the RTP payload, which follows
the RTP header.
• Sequence Number (16 bits): Each source starts with a random sequence number,
which is incremented by one for each RTP data packet sent. This allows
for loss detection and packet sequencing within a series of packets with the
same timestamp. A number of consecutive packets may have the same timestamp
if they are logically generated at the same time; an example is several
packets belonging to the same video frame.
• Timestamp (32 bits): Corresponds to the generation instant of the first octet
of data in the payload. The time units of this field depend on the payload type.
The values must be generated from a local clock at the source.
• Synchronization Source Identifier: A randomly generated value that uniquely
identifies the source within a session.
Following the fixed header, there may be one or more of the following field:
• Contributing Source Identifier: Identifies a contributing source for the payload.
These identifiers are supplied by a mixer.

## Slide 24: Table 25.1 Payload Types for Standard Audio and Video Encodings (RFC 3551)
Notes: The Payload Type field identifies the media type of the payload and the format
of the data, including the use of compression or encryption. In a steady state,
a source should only use one payload type during a session but may change the
payload type in response to changing conditions, as discovered by RTCP. Table 25.1
summarizes the payload types defined in RFC 3551.

## Slide 25: RTP Control Protocol (RTCP)
RFC 3550 outlines four functions performed by RTCP:
Quality of Service (QoS) and congestion control
Identification
Session size estimation and scaling
Session control
Notes: The RTP data transfer protocol is used only for the transmission of user data,
typically in multicast fashion among all participants in a session. A separate control
protocol (RTCP) also operates in a multicast fashion to provide feedback to
RTP data sources as well as all session participants. RTCP uses the same underlying
transport service as RTP (usually UDP) and a separate port number. Each participant
periodically issues an RTCP packet to all other session members. RFC 3550
outlines four functions performed by RTCP:
• Quality of Service (QoS) and congestion control: RTCP provides feedback
on the quality of data distribution. Because RTCP packets are multicast, all
session members can assess how well other members are performing and
receiving. Sender reports enable receivers to estimate data rates and the quality
of the transmission. Receiver reports indicate any problems encountered
by receivers, including missing packets and excessive jitter. For example,
an audio–video application might decide to reduce the rate of transmission
over low-speed links if the traffic quality over the links is not high enough
to support the current rate. The feedback from receivers is also important in
diagnosing distribution faults. By monitoring reports from all session recipients,
a network manager can tell whether a problem is specific to a single user
or more widespread.
• Identification: RTCP packets carry a persistent textual description of the
RTCP source. This provides more information about the source of data packets
than the random SSRC identifier and enables a user to associate multiple
streams from different sessions. For example, separate sessions for audio and
video may be in progress.
• Session size estimation and scaling: To perform the first two functions, all participants
send periodic RTCP packets. The rate of transmission of such packets
must be scaled down as the number of participants increases. In a session with
few participants, RTCP packets are sent at the maximum rate of one every five
seconds. RFC 3550 includes a relatively complex algorithm by which each participant
limits its RTCP rate on the basis of the total session population. The
objective is to limit RTCP traffic to less than 5% of total session traffic.
• Session control: RTCP optionally provides minimal session control information.
An example is a participant identification to be displayed in the user interface.

## Slide 26
Notes: An RTCP transmission consists of a number of separate RTCP packets
bundled in a single UDP datagram (or other lower-level data unit). The following
packet types are defined in RFC 3550:
• Sender Report (SR)
• Receiver Report (RR)
• Source Description (SDES)
• Goodbye (BYE)
• Application Specific
Figure 25.8 depicts the formats of these packet types. Each type begins with a
32-bit word containing the following fields:
• Version (2 bits): Current version is 2.
• Padding (1 bit): If set, indicates that this packet contains padding octets at the
end of the control information. If so, the last octet of the padding contains a
count of the number of padding octets.
• Count (5 bits): The number of reception report blocks contained in an SR
or RR packet (RC), or the number of source items contained in an SDES or
BYE packet.
• Packet Type (8 bits): Identifies RTCP packet type.
• Length (16 bits): Length of this packet is 32-bit words, minus one.
In addition, the Sender Report and Receiver Report packets contain the following
field:
• Synchronization Source Identifier: Identifies the source of this RTCP packet.
RTCP receivers provide reception quality feedback using a
Sender Report or a Receiver Report, depending on whether the receiver is also a
sender during this session. Figure 25.8a shows the format of a Sender Report. The
Sender Report consists of a header, already described; a sender information block;
and zero or more reception report blocks. The sender information block includes
the following fields:
• NTP Timestamp (64 bits): The absolute wall clock time when this report was
sent; this is an unsigned fixed-point number with the integer part in the first
32 bits and the fractional part in the last 32 bits. This may be used by the
sender in combination with timestamps returned in receiver reports to measure
round-trip time to those receivers.
• RTP Timestamp (32 bits): This is the relative time used to create timestamps
in RTP data packets. This lets recipients place this report in the appropriate
time sequence with RTP data packets from this source.
• Sender’s Packet Count (32 bits): Total number of RTP data packets transmitted
by this sender so far in this session.
• Sender’s Octet Count (32 bits): Total number of RTP payload octets transmitted
by this sender so far in this session.
Following the sender information block are zero or more reception report
blocks. One reception block is included for each source from which this participant
has received data during this session. Each block includes the following fields:
• SSRC_n (32 bits): Identifies the source referred to by this report block.
• Fraction lost (8 bits): The fraction of RTP data packets from SSRC_n lost
since the previous SR or RR packet was sent.
• Cumulative Number of Packets Lost (24 bits): Total number of RTP data
packets from SSRC_n lost during this session.
• Extended Highest Sequence Number Received (32 bits): The least significant
16 bits record the highest RTP data sequence number received from SSRC_n.
The most significant 16 bits record the number of times the sequence number
has wrapped back to zero.
• Interarrival Jitter (32 bits): An estimate of the jitter experienced on RTP data
packets from SSRC_n, explained later.
• Last SR Timestamp (32 bits): The middle 32 bits of the NTP timestamp in the
last SR packet received from SSRC_n. This captures the least significant half
of the integer and the most significant half of the fractional part of the timestamp
and should be adequate.
• Delay Since Last SR (32 bits): The delay, expressed in units of 2-16 s, between
receipt of the last SR packet from SSRC_n and the transmission of this report
block. These last two fields can be used by a source to estimate round-trip
time to a particular receiver.
The format for the Receiver Report (Figure 25.8b) is the
same as that for a Sender Report, except that the Packet Type field has a different
value and there is no sender information block.
The Source Description packet (Figure 25.8d) is
used by a source to provide more information about itself. The packet consists of a
32-bit header followed by zero or more chunks, each of which contains information
describing this source. Each chunk begins with an identifier for this source or for a
contributing source. This is followed by a list of descriptive items.
The BYE packet indicates that one or more sources are no longer
active. This confirms to receivers that a prolonged silence is due to departure
rather than network failure. If a BYE packet is received by a mixer, it is forwarded
with the list of sources unchanged. The format of the BYE packet consists of a
32-bit header followed by one or more source identifiers. Optionally, the packet
may include a textual description of the reason for leaving.
Application-Defined Packet This packet is intended for experimental use for
functions and features that are application specific. Ultimately, an experimental
packet type that proves generally useful may be assigned a packet type number and
become part of the standardized RTCP.

## Slide 27: Summary
SIP
  SIP components and protocols
  SIP uniform resource identifier
  Examples of operation
  SIP messages
  Session description protocol
RTP
  RTP protocol architecture
  RTP data transfer protocol
  RTCP
Real-time traffic
  Real-time traffic characteristics
  Requirements for Real-time communication
  Hard versus soft real-time applications
VoIP
  VoIP signaling
  VoIP processing
  VoIP context
Notes: Chapter 25 summary.

## Slide 28: Additional Slides

## Slide 29: Table 25.2 SDES Types (RFC 3550)
Notes: Table 25.2 lists the types of descriptive items defined in RFC 3550.